## Slide 1: Programmable Packet Scheduling at Line Rate
Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh, Sharad Chole, Shang-Tse Chuang, Anurag Agrawal, Hari Balakrishnan, Tom Edsall, Sachin Katti, Nick McKeown

## Slide 2: Programmable scheduling at line rate
Motivation: Can’t deploy new schedulers in production networks
The status quo in line-rate switches
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
2
Queues/
Scheduler
RMT
RMT, Domino
RMT
RMT, Domino
???
The scheduler is still fixed
Notes:   Flow of the talk:
  Why is programmable scheduling important?
  Why can’t we do programmable scheduling today? After all, switches are becoming more programmable as I spoke about in the last talk, so why isn’t that sufficient?

## Slide 3: Why is programmable scheduling hard?
Many algorithms, yet no consensus on abstractions, cf.
  Parse graphs for parsing
  Match-action tables for forwarding
  Packet transactions for data-plane algorithms
Scheduler has tight timing requirements
  Can’t simply use an FPGA/CPU
Need expressive abstraction that can run at line rate

## Slide 4: What does the scheduler do?
It decides
In what order are packets sent
  e.g., FCFS, priorities, weighted fair queueing
At what time are packets sent
  e.g., Token bucket shaping
Notes: A programmable scheduler needs to programmatically decide on these two attributes.

## Slide 5: A strawman programmable scheduler
Very little time on the dequeue side => limited programmability
Can we move programmability to the enqueue side instead?
Classification
Programmable logic to decide order or time
Packets

## Slide 6: The Push-In First-Out Queue
Key observation
In many cases, relative order of buffered packets does not change
i.e., a packet’s place in the scheduling order is known at enqueue
The Push-In First-Out Queue (PIFO): Packets are pushed into an arbitrary location based on a rank, and dequeued from the head
2
5
9
7
9
10
13
8

## Slide 7: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
…
...
p.rank= T[f] + p.len
Notes: End by reminding them that the reason this works is that the rank can be computed before enqueue
Make it clear that you have an extended budget on the enqueue side.

## Slide 8
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Rank Computation
Queues/
Scheduler
PIFO Scheduler
A programmable scheduler
Rank computation is a packet transaction (Domino, SIGCOMM’ 16)

## Slide 9
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Rank Computation
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len
p.rank = p.start
Fair queuing

## Slide 10
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
tokens = min(
tokens + rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
tokens = tokens - p.len
last = now
p.rank = p.send
Rank Computation
Token bucket shaping

## Slide 11: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Notes:   TODO: Fix alignment of this slide with the previous one.

## Slide 12: Shortest remaining flow size
Rank Computation
f = flow(p)
p.rank = f.rem_size
2
9
8
5
PIFO Scheduler

## Slide 13: Beyond a single PIFO
x
1
y
1
x
2
b1
b2
b3
y
2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical Packet Fair Queuing
Hierarchical scheduling algorithms need hierarchy of PIFOs
Notes: Practice narration here, too much waffling.
Mohammad: Explain the example more clearly.
Mohammad: Make sure colors are consistent.

## Slide 14: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical Packet Fair Queuing
PIFO-Red
(WFQ on a & b)
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
B
R
B
B
R
R
B
R
Notes: Similar alignment issues.
Letters aren’t aligned.
Mohammad: Show how the packet gets shipped out, i.e., differentiate packets from classes on dequeue.

## Slide 15: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow
Cannot express some scheduling algorithms, e.g., output shaping.

## Slide 16: PIFO in hardware
Performance targets for a shared-memory switch
  1 GHz pipeline
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
  PIFO hardware shared across ports
Naive solution: flat, sorted array is infeasible
Exploit observation that ranks increase within a flow

## Slide 17: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
1 enqueue + 1 dequeue per clock cycle
Can be shared among multiple logical PIFOs
Notes: Logical PIFOs can be supported by modifying the dequeuer logic a little bit.
Instead of dequeueing the head packet, we find the first packet for a particular logical PIFO (using an equality check + priority encoder), and then shift at that position.
Make sure to mention logical PIFOs here.
NG: Use of the term PIFO block is too recursive.
Amy: Say that the flow scheduler is implemented as an array of comparators, only now it’s feasible.
Logical pifos: (i.e., PIFOs for different ports or different levels of a hierarchy
.

## Slide 18: Hardware feasibility
The Rank store is just a bank of FIFOs (stable hardware IP)
Flow scheduler for 1K flows meets timing at 1GHz on 16-nm transistor library
  Continues to meet timing until 2048 flows, fails timing at 4096
  7 mm2 overhead for 5-level programmable hierarchical scheduler
  < 4% for a typical chip.

## Slide 19: Related work
  PIFO: Used in theoretical work by Chuang et. al. in the 90s
Universal Packet Scheduling (UPS)
  Single algorithm (LSTF) to replay all schedules, end point sets slack
  Assumes fixed switches => cannot express fair queueing, shaping
  Assumes single priority queue => cannot express hierarchies
Hardware designs for priority queues
  Based on a binary heap, scales to large number of entries
  Needs a single heap for each port => hardware can’t be shared
Notes: I’ll now discuss how PIFO and programmable scheduling relate to the most relevant prior work.

## Slide 20: Conclusion
Programmable scheduling at line rate is within reach
Two benefits:
  Express new schedulers for different performance objectives
  Express existing schedulers as programs, not hardware
Code: http://web.mit.edu/pifo

## Slide 21: Backup slides

## Slide 22: Limitations of PIFOs
Output shaping: PIFOs rate limit input to a queue, not output
Shaping and scheduling are coupled.
Notes: Amy: Depending on whether we are speaking about hardware limitations as well, move this after the hardware part.
These limitations are a little hard to state succinctly. Maybe move them to the backup slides?

## Slide 23: PIFO mesh
Notes: Show a PIFO mesh, and then show how the hierarchical scheduler maps to the PIFO mesh.
Just lets people make the connect from a single PIFO block to multiple PIFO blocks (useful for hierarchies)
Always enq+deq only one per clock cycle.
Mohammad: Each block in the 5-level scheduler runs independently. You can run each block independently.
Emphasize that the blocks are decoupled. Each can run independently. You can instantiate multiple of these.
Because of how the hardware and hierarchical scheduler is designed and you do everything on enqueue, each can run independently.
Maybe bring in the tiling slide

## Slide 24: Proposal: scheduling in P4
Currently not modeled at all, blackbox left to vendor
Only part of the switch that isn’t programmable
PIFOs present a candidate
Concurrent work on Universal Packet Scheduling also requires a priority queue that is identical to a PIFO

## Slide 25: Hardware implementation
Rank
== comparators
> comparators
Priority encoder
Priority encoder
Shift elements based on push, pop indices
Pop
(DEQ)
Push 1
(ENQ)
Push 2
(reinsert)
Logical
PIFO ID
Rank
Rank
Logical
PIFO ID
Rank
Logical
PIFO ID
Rank
Logical
PIFO ID
Meets timing (1 GHz) for up to 2048 flows at 16 nm
Less than 4% area overhead (~7 mm2) for 5-level scheduler

## Slide 26: A PIFO block
Enqueue:
(logical PIFO,
rank, flow)
Dequeue:
(logical PIFO)
ALU

## Slide 27: A PIFO mesh
Enq
Deq
Enq
ALU
Deq
Enq
ALU
Deq
Next-hop lookup
ALU
Next-hop lookup
Next-hop lookup

## Slide 28: Proposal: scheduling in P4
Need to model a PIFO (or priority queue) in P4
Requires an extern instance to model a PIFO
  Can start by including it in a target-specific library
  Later migrate to standard library if there’s sufficient interest
  Section 16 of P4v1.1
Transactions themselves can be compiled down to P4 code using the Domino DSL for stateful algorithms.

## Slide 29: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 30: Composing PIFOs: min. rate guarantees
Minimum rate guarantees:
Provide each flow a guaranteed
rate provided the sum of these
guarantees is below capacity.
PIFO-Root
Prioritize flows under
min. rate
PIFO-A
(FIFO for flow A)
PIFO-B
(FIFO for flow B)
1
3
2
4
2
A
B
A
B
A
Composing PIFOs
Notes: TODO: Flesh out this slide.
Stress that composed PIFOs can be used for more than just hierarchical scheduling.
Slightly better figure maybe?

## Slide 31: Traffic Shaping
1. update tokens
2. p.send = now +
(p.len - tokens) / rate;
3. p.prio =p.send
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Notes: A natural question is whether a PIFO can handle non-work-conserving algorithms?
So, our third example looks at Traffic Shaping, the most common of these non-work-conserving algorithms,
whose goal is to limit a flow to a fixed absolute throughput regardless of its offered load and the offered load of other flows.
We can implement Traffic Shaping using PIFOs by computing a packet’s priority in the PIFO based on the wall-clock
departure time of the packet when it is enqueued and dequeuing a packet whenever its wall-clock time arrives.
A PIFO allows you to express anything where you can determine the transmission order when packets are enqueued.
In other words, anything where the relative order doesn’t change in the future.
There are algorithms for which these are not true. In particular, hierarchical scheduling algorithms are a class of algorithms
for which this is not true. Let’s consider one in particular.

## Slide 32: LSTF
Add transmission delay to slack
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Decrement wait time in queue from slack
Initialize slack
values
Notes: Add transmission time at the switch
Too many examples.

## Slide 33: The PIFO abstraction in one slide
PIFO: A sorted array that let us insert an entry (packet or PIFO pointer) into a PIFO based on a programmable priority
Entries are always dequeued from the head
If an entry is a packet, dequeue and transmit it
If an entry is a PIFO, dequeue it, and continue recursively
Notes: To summarize, let’s look at what the PIFO abstraction entails.