## Slide 1
Abstractions for programming line-rate switches
Programming: Can we implement a new algorithm?
Line rate: Highest wire speed supported by a standard
E.g., Can we program CoDel into a 10G/100G switch?
Programming switch data planes at line rate
Active Networks: security concerns
x86 routers: very flexible, but slower than line rate
NPUs/FPGAs: clunky programming model, still slower than line rate
The history of programmable switches
Programmable parsing, match-action (RMT, FlexPipe, Xpliant)
Line-rate programmability
Parser
Ingress Pipeline
Stage 1
Match
Scheduler
Deparser
Egress Pipeline
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Stage 1
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Eth
IP
TCP
Challenges with line-rate programming
Programming languages like P4 are too low level
No hardware support for stateful operations
Not clear how to program algorithms like RED/CoDel at line rate
Two abstractions for line-rate programming
Packet transactions to program data-plane algorithms
Atoms to represent instruction set
Compiler to translate between the two
All-or-nothing: Compiled code runs at line rate, else rejected
Atom
State
Body
Packet
Headers
Packet
Headers
Stage 1
Stage 2
A machine model for line-rate switches
Atom templates
Atom
State
Body
Atom
State
Body
Atom
State
Body
Atom
State
Body
Atom
State
Body
Specifies atom behavior
Fixed parts and tunable parameters
Must sustain line rate processing of packets
(10 G * 64 ports = 1 GHz at smallest packet size)
Add
Sub
constant
x
2-to-1 Mux
x
choice
bool choice = ??;
int constant = ??;
if ( choice ) {
x = x + constant ;
} else {
x = x - constant ;
}
Packet Transactions
Code blocks that process one packet at a time
Block written in a subset of C (Domino)
One packet transaction per pipeline
No worries about concurrency
Programming with Packet Transactions
Domino
Atoms
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
%NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Other results
Create machines with different atoms, e.g.,
simple writes, read-add-write, conditional updates
Write atom templates as digital circuits, synthesize to
32-nm transistor library, estimate chip area at 1 GHz.
Compile Domino programs to different machines
to see if they can run at line rate.
Details at arxiv.org/abs/1512.05023
Anirudh Sivaraman, Mihai Budiu, Alvin Cheung, Changhoon Kim, Steve Licking, George Varghese, Hari Balakrishnan, Mohammad Alizadeh, Nick McKeown