## Slide 1: Making the fastest routers programmable
Anirudh Sivaraman
Notes: I am going to be talking about how we make today’s fastest routers programmable. By programmable, I mean the ability to change the router’s functionality once it’s been deployed without throwing out and buying a new router every time you need a new feature.

## Slide 2: Traditional network architecture
Fixed-function routers and programmable end points
Notes: To start, let’s see how computer networks are traditionally supposed to be architected. The end-to-end principle tells us that programmability and application logic should reside at the endpoints of a network. The routers that connect the endpoints together should be fixed-function and only perform packet forwarding.

## Slide 3: But, today’s reality is very different
What’s in a fixed-function router? No consensus after decades.
Rate of innovation exceeds our ability to get things into routers.
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters
Notes:   But today’s reality is very different. First, it’s unclear what fixed functionality goes into a router. It was supposed to be forwarding. But today’s routers have a far more bloated feature set including measurement, access control, and tunneling. At the same time, there is no consensus on the right feature set because each vendor has their laundry list of features.
  Because we don’t have consensus and these routers are still fixed, they invariably fall short because someone wants something different from what’s provided. For instance, new router algorithms are developed from time to time and very few actually find their way into production routers. Here’s a timeline of router algorithms developed since the 80s and only a small fraction are available in production routers.

## Slide 4: But, today’s reality is very different
What’s in a fixed-function router? No consensus after decades.
Rate of innovation exceeds our ability to get things into routers.
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 5: One approach: Use end points
Give up on changing routers, use end points instead.
But, end point approaches are inaccurate or inefficient
  Estimating a router’s loss rates from end point measurements is inaccurate
  Congestion control from end points is inefficient
Notes: As a network operator who wants to add functionality to their network, what can you do if a router doesn’t have the features you want? The first approach is to give up on changing routers and do everything from the end points. Many network operators have done this for a variety of different networking tasks. But this is a rather roundabout way of doing things. As an example, let’s say you want to measure if a router deep inside the network is losing packets. One approach is to collect enough measurement date from endpoints scattered throughout the network and then analyze it to indirectly infer if there’s loss on a particular router. Not only is this indirect, it’s also necessarily inaccurate relative to just measuring things on that router.
As another example, the problem of congestion control deals with managing the transmission of packets from end points into the network so that the network’s resources (links, buffers, etc.) are not overloaded. Most solutions to this problem rely entirely on the end points to do congestion control without any router support. At the same time, it is well-known that there are much more efficient ways of doing congestion control if we could add just a little bit of intelligence to the routers.
In summary, depending on the problem, end point approaches can either be inaccurate or leave considerable performance on the table.

## Slide 6: Another approach: Use a software router
Chart: Aggregate Capacity
| 1969.0 | 1982.0 | 1983.0 | 1985.0 | 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2012.0 | 2014.0
Fastest router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 32 | 80 | 240 | 640 | 1280 | 3200
Software router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 0.1 | 0.17 | 4 | 35 | 40 | 100
Software routers 10—100x worse than the fastest routers
Software routers suffer from non-deterministic performance
Notes: Another approach to the problem of a fixed-function router is to use a software router. This is a router built on top of any programmable substrate, whether it be a CPU, GPU or multi-core CPU. To answer that, let’s look at how software routers have fared over time in forwarding performance relative to the fastest routers at that point in time.
Here’s a graph that charts aggregate capacity per unit since the days of the ARPANET with the y-axis in Gbit/s on a log scale. We plot two lines. The blue is a software router at that point in time, while the red is the fastest known router at some point in time. You see two phases. Up through the mid 90s the lines overlap: the fastest routers were in fact server machines with some forwarding software on them that could be swapped out at will. Since the mid 90s as router speeds took off, the fastest routers have been built out of dedicated forwarding hardware and are fixed in their functionality. Software routers have also improved their performance over the same time period, but they remain 10 --- 100 x slower. Further, the performance of a software router depends on the complexity of the feature that you implement on it unlike the fixed-function routers that are rated for a certain line rate on a certain number of ports regardless of what features are on.

## Slide 7: Vision: programmability and performance
Algorithm:
For each packet
Calculate average queue size
if min < avg < max
calculate probability p
mark packet with probability p
else if avg > max
mark packet
Compiler
Scheduler
Ingress pipeline
Egress pipeline
High-speed router:
Notes:   My work looks at whether we can have the best of both worlds, the programmability that has so far been restricted to software routers and the performance that has so far been restricted to fixed-function hardware routers. Put differently, instead of specific features can we provide high-speed reusable primitives in the router’s hardware and program features in software?
  The world I am imagining is something like this. You write an algorithm in a high-level language that tells you what processing to do for each packet. You feed this to a compiler, which then appropriately configures router primitives on a high-speed router like say a box that you buy from Broadcom or Cisco. If you change your mind about the algorithm, you write a new one and then run it through the compiler again.

## Slide 8: This Talk
  Domino (SIGCOMM 2016): programming streaming algorithms
    The first hardware primitives for high-speed execution of streaming algorithms
    A compiler to
      Extract these primitives from a corpus of algorithms
      Check if a set of primitives can support a new algorithm
  PIFO (SIGCOMM 2016): programming the scheduler
    The first primitive that allows us to program scheduling algorithms
    Modest chip area cost when implemented in high-speed hardware
My work
Performance+programmability for important classes of router functions
Notes:   Specifically, I am going to speak about two of my projects that were published at SIGCOMM last year. The first project looks at programming streaming algorithms. These are algorithms that process a stream of packets in one pass in the order in which they arrive. They are allowed to do a bounded amount of work per packet and maintain a bounded amount of router state and include algorithms for network measurement and network resource management. As part of this project, we developed a set of hardware primitives that permit high-speed execution of these algorithms and a method to extract these primitives from a corpus of algorithms.
  The second one looks at programming the router’s scheduler, which decides what packet to transmit next when the link is idle. Here, we developed a single primitive that allows us to program many scheduling algorithms at speeds approaching the fastest routers without losing performance. Further, we designed and synthesized this primitive in hardware to show that it has modest chip area cost.

## Slide 9: Packet Transactions: High-Level Programming for Line-Rate Switches (SIGCOMM 2016)
Anirudh Sivaraman, Alvin Cheung, Mihai Budiu,
Changhoon Kim, Mohammad Alizadeh, Hari Balakrishnan,
George Varghese, Nick McKeown, Steve Licking
Joint work with collaborators at MIT, University of Washington,
Barefoot Networks, Microsoft Research, and Stanford University
Notes: I’ll talk about Domino first. This is based on a paper that appeared at SIGCOMM last year, and is joint work with collaborators at MIT, UW, Barefoot, MSR, and Stanford. The goal of this work was to able to program streaming algorithms on high-speed routers. These are router algorithms that process the incoming packet stream in one pass. The router does a bounded amount of work per packet and maintains a bounded amount of router state to carry out its work. They include algorithms for network measurement such as sketching algorithms and managing a router’s resources, such as its link capacity and buffers.

## Slide 10: Programming streaming algorithms
E.g., packet sampler:
Algorithms spend many clock cycles per packet
But, routers handle 1 packet/cycle
Pipelining bridges this gap
  Atoms: primitives to modify headers, state
  A compiler to
    Extract atoms from a corpus of algorithms
    Check if an atom pipeline can support a new algorithm
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Notes: I’ll give a one-slide overview of the work before I dive into its specific technical contributions.
First, let’s consider an example of a streaming algorithm, which I’ll call the packet sampler. Say you want to sample the source IP address of every 10th packet going through a router. Here’s what the code looks like: I have highlighted router state in red. you count from 0 – 9 and then sample every 10th packet, resetting the count to 0.
First, we note that the packet sampler spends more than 1 clock cycle per packet, where each clock cycle is a ns. Let’s say each LOC was one instruction and took one cycle, that’s at least three cycles per packet regardless of which branch the code takes.
We want this algorithm to run at high speeds. What is this speed? A high-end router handles 1 packet every clock cycle regardless of what features you enable. We would like the same guarantee regardless of what algorithm you program into the router.
Now, when each packet takes multiple clock cycles, but we need to process a new packet every clock cycle, the standard technique is to use a pipeline. Fixed-function routers use a pipeline where each pipeline stage carries out a fixed function like tunneling, forwarding, etc. In the context of this pipeline, we introduce two new ideas.
First is the concept of an atom, which are high-speed hardware primitives that we can embed into the router pipeline’s stages in place of fixed functionality. Atoms modify headers and/or state, and execute atomically: any state updated by an atom is visible to the next packet arriving at that stage a clock cycle. All atoms in a router support 1 packet per cycle, unlike say x86 instructions that have variable throughput depending on instruction.
Second, we built a compiler to go from high-level descriptions of algorithms to atoms. This compiler serves two purposes. In the design phase, we use this compiler to extract atoms from algorithms in a way that the atoms allow not just those, but hopefully other algorithms to be programmed. Once the router has been designed, we use the compiler to check if a given atom pipeline can support a new algorithm.
There’s one big difference between this machine and a processor pipeline. A processor can run any algorithm, but throughput inversely correlates with complexity. On a programmable router only algorithms that sustain one packet per clock cycle can run; all others are rejected. While this seems harsh, this obviates any need for performance profiling and is the model of routers that operators are used to.

## Slide 11: A fixed-function router pipeline
In
Queues/
Scheduler
Out
Parser
match/action
Stage 1
match/action
Stage 2
match/action
Stage N
match/action
Stage 1
Egress pipeline
match/action
Stage N
Deterministic pipelines supporting 1 packet/cycle
Only local memory; must constrain every stage’s action unit
Ingress pipeline
Notes: The only place where buffering is required is the scheduler.

## Slide 12: A programmable atom pipeline
Atom: local memory + action unit,
must handle 1 packet/cycle
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
action unit
X
constant
Add
Mul
2-to-1 Mux
X
choice
Packet
Choice of atoms dictates the algorithms a router supports
Notes: REHEARSE:
One solution is to only provide those instructions that exactly have a throughput of 1 packet per cycle and exclude all instructions that don’t. We call such an instruction an atom to denote an atomic unit of header and/or state manipulation provided by the hardware. More precisely, an atom consists of some local memory like before and an action unit, which is a very specific circuit with a few configurable parameters that acts on this local memory.
Here’s one toy example of such a circuit. When these atom circuits are synthesized to logic gates we ensure that the circuit can sustain a new packet once every clock cycle. Now in practice you would have multiple such atoms acting in parallel on a packet at it goes through a pipeline stage so long as each atom respects the 1 packet per cycle throughput.
Clearly, there are instructions that can only run at throughputs lower than 1 packet per cycle. An example is an instruction that reads some state maybe does something complicated on it and writes this result back. What do we do if a program needs such an instruction
TODO: Maybe show packets marching in lock step.

## Slide 13: Compiling algorithms
Pipeline stages
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0
:(pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1
Input: Algorithms as
packet transactions
Code
pipelining
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Extracting
atoms
Output: Atoms
Checking
against
existing
atoms
Output: Pipeline
Configuration
Notes: Hopefully by now you’re convinced that we need this concept of an atom for high-speed execution. Given that the choice of atoms affects which algorithms we can program, can we try and empirically extract the atoms given a corpus of algorithms? Here’s an overview of how that would work.
The programmer writes an algorithm as what we call a packet transaction. This is identical to a DB transaction in that the packet trans for each packet is assumed to execute atomically, by itself, after the execution of the trans for the previous packet. The programmer’s model is one where each packet executes the trans, updates some state, and only then moves on to the next packet.
Ok, what kind of atoms and how many of them do we need to run the streaming algorithms that we care about? To do this, we first pipeline the algorithm as much as we can so that we can look for fragments of the original code that need to be executed by atoms within the pipeline. We do this for a bunch of different algorithms and mine the pipeline stages to find reusable patterns, which we can then call atoms and build hardware for.
Now, this second step is necessary because we want atoms that work beyond the specific example algorithms and hopefully generalize in some way. For now, the first step is automated, while the second is trial-and-error. Let’s go over each.

## Slide 14: Code pipelining for stateless algorithms
pkt.tmp =
pkt.f1 + pkt.f2
  Stateless algorithm: pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
pkt.f4 =
pkt.tmp - pkt.f3
Easy to pipeline stateless algorithms
Notes: Let’s look at pipelining the code first. Before I describe our algorithm, it’s useful to understand the core concept in pipelining. Our goal is to take a packet transaction and decompose it into a pipeline so that if each pipeline stage executes atomically, the entire transactions semantics are preserved. Let’s see how we do this on some simple examples.
Let’s say you have this stateless algorithm where you do pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3. You could pipeline this into a sequence of stages, where you first add, then subtract. In general if you have a more complicated stateless algorithm, you can still do this. As someone designing the atoms, therefore, you can just design an atom that supports all binary operations on a pair of packet fields, and then you can take any algorithm and break it down into a pipeline of such atoms.

## Slide 15: Code pipelining for stateful algorithms
  Stateful algorithm: x = g(x)
p.tmp = x
p.t1=
s1(p.tmp)
x = p.tn
X
Can’t pipeline: must do x = g(x) atomically in 1 stage
p.tn =
sn(p.t_{n-1})
1. Throughput is 1/N
2. X is shared
N stages
Notes: Now let’s say you want to do the stateful operation x = g(x), where you take x, read it in, do something complicated with it, and then write it back. If you tried to pipeline it into multiple stages, like this, it doesn’t quite work. First of all, you can’t execute the first pipeline stage until the last one has completed and written the most recent value of x. So the throughput you get is at most 1 in N. Second, it assumes we can share memory, which we ruled out earlier.
Instead, we need to design hardware that can carry out the entire operation g(x) in one clock cycle. As a result, the stateful atoms end up looking quite a bit more involved than garden variety x86 instructions. So in any given algorithm, we need to collect together all the operations that touch the same state variable and then turn the entire thing into one atom.

## Slide 16: Code pipelining: the algorithm
Create one node for each instruction
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Now let’s formalize the intuition I showed earlier. This is the packet sampling algorithm from before, which has been rewritten to facilitate dependency analysis in a compiler. We first create a single node for each instruction after rewriting.

## Slide 17: Code pipelining: the algorithm
Stateless
(intra-packet)
dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Then we draw a black edge between any two nodes that have a dependency: these are intra-packet dependencies where one instruction reads a packet field written by another.

## Slide 18: Code pipelining: the algorithm
Stateful
(inter-packet) dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Next we add inter-packet dependencies based on state. An example is the backward flowing red arrow that mandates that you must write to count before you read from it on the next cycle.

## Slide 19: Code pipelining: the algorithm
Strongly connected components
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: At this point, if you look for strongly connected components in the graph, it gets us all of all the operations that touch a piece of state and hence need to go into an atom. Each SCC corresponds to an atomic code fragment that needs to be executed by a single atom.
Some of you who do compilers on a daily basis might notice the similarity to Monica Lam’s work on strongly connected components for software pipelining, where you are trying to overlap the execution of different iterations of a loop. In sw pipelining, a larger SCC implies a lower throughput. Here, on the other hand, a larger SCC means a larger area for the atom in silicon because we are forcing the throughput to be one packet per cycle.

## Slide 20: Code pipelining: the algorithm
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new
Contract SCCs to form DAG
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Once we have these SCCs, we can contract all nodes in an SCC to a single node, and then do a depth-first search on the DAG to get a pipeline.

## Slide 21: Code pipelining: the algorithm
After Depth-First Search
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1

## Slide 22: Extracting atoms
pkt.x = pkt.a + pkt.b
pkt.x = pkt.a - pkt.b
pkt.c = pkt.a (BINOP) pkt.b
x = x + 1
x = x + mux(C, pkt.a)
Accumulator
Stateless
Notes: Now that gives us the pipeline stages for a single algorithm. If we decided to call each pipeline stage an atom and lowered it into hardware, we would have effectively built hardware for a specific algorithm, which is no better than a router today. So we want to look at pipeline stages across a variety of different atoms and then extract common and reusable patterns that are more future proof.
Right now this process is manual and we use trial and error to determine these atoms. Let me show you an example. If you had pkt.x = pkt.a + pkt.b and pkt.x = pkt.x – pkt.b, you could generalize this to pkt.c = pkt.a BINOP pkt.b, where BINOP is any binary operation such as +, -, *, shift, min, max on any pair of packet fields.
If on the other hand, we had pkt.sample = pkt.tmp ? pkt.src : 0, we could generalize that to an atom that conditionally (using pkt.predicate) sets pkt.a to either a constant or another packet field using a mux.

## Slide 23: Does an algorithm map to a given atom?
choice
Add
x = x * x doesn’t map, reject code
x = x + 1 maps to this atom
X
constant
Add
Mul
2-to-1 Mux
X
1
Checks if algorithm can run at full throughput
Use program synthesis for mapping problem.
Notes: Now that gives us the pipeline stages for a single algorithm. If we decided to call each pipeline stage an atom and lowered it into hardware, we would have effectively built hardware for a specific algorithm, which is no better than a router today. So we want to look at pipeline stages across a variety of different atoms and then extract common and reusable patterns that are more future proof.
Right now this process is manual and we use trial and error to determine these atoms. Let me show you an example. If you had pkt.x = pkt.a + pkt.b and pkt.x = pkt.x – pkt.b, you could generalize this to pkt.c = pkt.a BINOP pkt.b, where BINOP is any binary operation such as +, -, *, shift, min, max on any pair of packet fields.
If on the other hand, we had pkt.sample = pkt.tmp ? pkt.src : 0, we could generalize that to an atom that conditionally (using pkt.predicate) sets pkt.a to either a constant or another packet field using a mux.

## Slide 24: Results: A catalog of reusable atoms
Atoms | Description
Stateless | Binary operations on a pair of packet fields
Accumulator | Increment state by value (packet field or constant)
Read/Write | Read or write a state variable
Conditional Accumulator | Accumulate differently based on one predicate
Nested Conditional Accumulator | Accumulate differently based on two predicates
Pairs | Update a pair of mutually dependent state variables
Notes: We went through a whole corpus of algorithms and iterated until we came up with a reasonable set of atoms. Here are the atoms we came up with. These aren’t sacrosanct by any means, but they are a decent start. I’ll explain a few. The stateless atom allows us to perform binary operations on a pair of packet fields. The read/write atoms allows us to either read the last value of state or write in a new value. The accumulator adds a packet field or constant to a state variable, while the conditional does this conditionally.
We also have examples of algorithms that each atom can support. Finally, we took these atoms and wrote them in Verilog to see if we could ensure they ran at 1 GHz. All these atoms meet the 1 GHz timing requirement quite easily and here are individual atom areas. If you take 100 of each, which turns out to be sufficient for our algorithms, the area overhead is less than a percent in aggregate.

## Slide 25: Results: A catalog of reusable atoms
Atoms | Description | Examples
Stateless | Binary operations on a pair of packet fields | TTL decrement, setting header fields, etc.
Accumulator | Increment state by value (packet field or constant) | Counters, sketches, heavy hitters
Read/Write | Read or write a state variable | Bloom filters, indicator variables
Conditional Accumulator | Accumulate differently based on one predicate | Rate Control Protocol, Flowlet switching, sampling
Nested Conditional Accumulator | Accumulate differently based on two predicates | HULL, AVQ, Rank Computation for Start-Time Fair Queueing
Pairs | Update a pair of mutually dependent state variables | CONGA
Notes: We went through a whole corpus of algorithms and iterated until we came up with a reasonable set of atoms. Here are the atoms we came up with. These aren’t sacrosanct by any means, but they are a decent start. I’ll explain a few. The stateless atom allows us to perform binary operations on a pair of packet fields. The read/write atoms allows us to either read the last value of state or write in a new value. The accumulator adds a packet field or constant to a state variable, while the conditional does this conditionally.
We also have examples of algorithms that each atom can support. Finally, we took these atoms and wrote them in Verilog to see if we could ensure they ran at 1 GHz. All these atoms meet the 1 GHz timing requirement quite easily and here are individual atom areas. If you take 100 of each, which turns out to be sufficient for our algorithms, the area overhead is less than a percent in aggregate.

## Slide 26: Results: A catalog of reusable atoms
Atoms | Description | Examples | Atom area in squared micron | Additional area for 100 atoms
Stateless | Binary operations on a pair of packet fields | TTL decrement, setting header fields, etc. | 1384 | 0.07%
Accumulator | Increment state by value (packet field or constant) | Counters, sketches, heavy hitters | 431 | 0.022%
Read/Write | Read or write a state variable | Bloom filters, indicator variables | 250 | 0.0125%
Conditional Accumulator | Accumulate differently based on one predicate | Rate Control Protocol, Flowlet switching, sampling | 985 | 0.049%
Nested Conditional Accumulator | Accumulate differently based on two predicates | HULL, AVQ, Rank Computation for Start-Time Fair Queueing | 3597 | 0.18%
Pairs | Update a pair of mutually dependent state variables | CONGA | 5997 | 0.30%
<1 % additional chip area for 100 atom instances

## Slide 27: What algorithms do atoms enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
SRPT
WFQ
STFQ
IntServ
HPFQ
Notes: Now that we have designed these atoms, if we go back to our original timeline, what more can we do?

## Slide 28: What algorithms do atoms enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
WFQ
STFQ
IntServ
HPFQ
Notes: Ok, so there are a few more algorithms we can’t do. Some of these require floating point operations, others require some periodic timer-driven computations, while others need us to coordinate between the enqueue and dequeue pipelines.

## Slide 29: Programmable Packet Scheduling at Line Rate (SIGCOMM 2016)
Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh,
Sharad Chole, Shang-Tse Chuang, Anurag Agrawal, Hari Balakrishnan,
Tom Edsall, Sachin Katti, Nick McKeown
Joint work with collaborators at MIT, Cisco Systems,
Stanford University, and Barefoot Networks
Notes: I’ll start with the PIFO work. This project was joint work with a number of collaborators from MIT, Cisco Systems, Stanford, and Barefoot Networks.

## Slide 30: Why programmable scheduling?
Different performance objectives demand different schedulers
  Isolating different tenants in a datacenter: fair queueing
  Single tenant with many short flows: shortest remaining processing time
Status quo: Menu of schedulers baked into hardware
  Can configure coefficients, but not program a new algorithm
Notes:   Why even care about programmable scheduling? It turns out that different performance objectives demand demand different schedulers within a network. For instance, if you were a dc operator like Google and you had multiple competing tenants, you may want to use a round robin scheduler to isolate clients from each other. On the other hand, if you owned your own cluster with a whole bunch of flows starting and stopping, you would use an algorithm like shortest remaining processing time to minimize the flow completion time.
  The status quo on routers is a limited menu of schedulers baked into hardware. These include algorithms like coarse-grained priorities, deficit round robin, and rate limits on each flow. While you can configure coefficients in these algorithms, you can’t replace the algorithms with new ones.

## Slide 31: Why is programmable scheduling hard?
Many algorithms, yet no consensus on primitives
Tight timing requirements: can’t simply use an FPGA/CPU
Need expressive primitive that can run at high speed
Notes:   So, why has prog. sched eluded us? It’s because despite having many scheduling algorithms over the last few decades, we have no consensus on the right primitive for scheduling.
  Why is a primitive important? The scheduler has demanding throughput requirements: typically, one enqueue and one dequeue every ns. So, you can’t simply throw an FPGA or CPU into the fast path, because just detouring a packet to and from an FPGA is enough to kill the throughput.
  Define clock cycle here.
  What we really need is a simple primitive that we can implement in hardware to support high-speed scheduling.

## Slide 32: What does the scheduler do?
It decides
In what order are packets sent
  e.g., first-in first-out, priorities, weighted fair queueing
At what time are packets sent
  e.g., rate limits
Notes: To get to this primitive, let’s first look at what the scheduler does. It decides on two things. First, the order in which packets are transmitted. This captures work-conserving schedulers that always transmit some packet if the link is idle. They include things like priority scheduling, weighted fair queueing, etc. Second, the scheduler decides the absolute time at which packets are transmitted. This captures non-work-conserving schedulers that some times hold on to packets even if there is spare capacity on the link. The canonical example is token bucket rate limiting, where you want to limit a flow to say 10 Mbit/s even if the flow was the only flow on a link with much larger capacity.

## Slide 33: Schedulers in routers today
Classification
Packets
Fixed schedulers
(priority,
round robin,
rate limits)
Notes: How does a scheduler in a fixed-function router today pick the order and the time? Packets come in, they are classified into one of a fixed set of FIFOs, one for each flow. Then, on the dequeue side, some fixed logic picks the next flow to transmit among flows that have not exceeded their rate limits. Typically, this scheduler maintains some auxiliary state to tell it which queue to dequeue from next.

## Slide 34: A strawman programmable scheduler
Very tight time budget between consecutive dequeues (5 cycles @ 100G)
Can we refactor by precomputing programmable operations off the critical path?
Classification
Programmable dequeue()
function
Packets
Notes: Precomputing _before_ packet is enqueued, not as it is enqueued. So it’s not on the enqueue critical path either.
Let’s say you need to make this programmable. You could make the fixed dequeue logic programmable, by having a programmer supply any dequeue function and any associated auxiliary state. While this is very expressive, the problem is that there is very little time during the dequeue operation because you need to dequeue once every 5 clock cycles to sustain 100 G and more.
// Not much time for any programmable operations
// Hard to pipeline because of state maintained by dequeue operations
The dequeue operation isn’t a computation that can be pipelined over more than 5 clock cycles because dequeue operations are dependent on each other and one dequeue has to finish before the next starts.
//This is because the dequeue operation maintains a large amount of state (such as the head of all the queues), which needs to be updated (in a complicated manner) to its correct // value before the next dequeue operation can start.
Instead, can we refactor the scheduler so that we can precompute as many of the programmable operations before the dequeue operation happens and leave only the essential part of actually dequeueing and transmitting a packet to the dequeue side.
Q: Why is it easy to pipeline on the enqueue side?
On the enqueue side it is easier: you have a much smaller RMW loop for any state. The fixed part of the PIFO handles the fixed computations for you. It’s hard to do the fixed part of the PIFO and prog in the same critical path. That’s why it’s important to pipeline and optimize the hardware for a PIFO and move the stuff off the critical path.

## Slide 35: The Push-In First-Out Queue
Key observation
In many schedulers, relative order of buffered packets does not change
i.e., a packet’s place in the scheduling order is known at enqueue
The Push-In First-Out Queue (PIFO): Packets are pushed into an arbitrary location based on a rank, and dequeued from the head
2
5
9
7
9
10
13
8
Notes:   TODO: Replace rank with urgency maybe?
  Let’s see how we do this. The key observation is that in many practical schedulers, the relative order of packets that are already buffered doesn’t change with future packet arrivals. Put differently, if a packet comes in, its location in the scheduling order can be determined before it is enqueued. The packet can then by pushed into this location, secure in the knowledge that we don’t have to change the relative order of packets that are already buffered.
  Now, some schedulers that confirm to this property are strict priority scheduling, where the location is determined by a packet’s priority, and FCFS, where the location is determined by arrival time.
  A natural primitive for this is a push-in first-out queue (or PIFO) where packets are pushed into an arbitrary location based on rank (which could be either scheduling order or time), but always dequeued from the head. As an illustration, if packet with rank 8 arrived to this PIFO, it would be pushed between 7 and 9.

## Slide 36: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
…
...
p.rank= T[f] + p.len
Notes: Now, how do we build a programmable scheduler based on a PIFO? To program the scheduler, we program the packet’s rank computation before enqueueing it into a PIFO because that’s the only programmable part in a PIFO.
How do we program the rank computation? Quite literally, by writing out a program for it. Here’s a made-up program, which computes a packet’s rank using a table T for each flow and the packet’s length.
This is the key modularity in the design. It separates out the fixed logic, which is the task of enforcing ranks, from the programmable logic, which is the task of computing ranks. All we need to ensure is that the rank field is precomputed by the rank computation program before the packet hits the PIFO scheduler. Typically, you would precompute the rank on the same router housing the PIFO scheduler, but as we’ll see this rank computation can happen elsewhere in the network as well.
Ok, so where do the programmable and fixed parts go in a real router?

## Slide 37
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
A programmable scheduler
Rank Computation
…
…
…
…
Notes: For this, let’s look at a router. Packets from all input ports are funneled into a shared ingress pipeline. This pipeline carries out a sequence of packet transformations in these stages such as computing the packet’s ranks. Then there are a set of queues that store the packets before they are picked up for transmission. Then there’s a similar egress pipeline shared across all ports.
In this figure, the PIFOs replace the queues in the scheduler, while the rank computation runs in the ingress pipeline. How exactly do we run the rank computation here and what does each stage in the pipeline do? We’ll deal with that in the second half of the talk. For now, assuming we can compute the ranks in the ingress pipeline, let’s see what scheduling algorithms we can program.

## Slide 38
Out
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Fair queuing
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len
p.rank = p.start
Rank Computation
Notes: The first is fair queueing, a work-conserving scheduler. Let’s pick the virtual start-time fair queueing implementation.
Here, for each packet we compute its virtual start time in an idealized fluid fair scheduler. We do this by setting the packet’s start time to the maximum of the finish time of the last packet in the packet’s flow and the current virtual time. Then, we update the flow’s finish time appropriately.
We then schedule packets in order of their virtual start times, which becomes a packet’s rank in the PIFO.

## Slide 39
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Token bucket shaping
tokens = min(
tokens + rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
tokens = tokens - p.len
last = now
p.rank = p.send
Rank Computation
Notes: Next, let’s look at the canonical non-work-conserving algorithm: token bucket shaping.
The rank computation here is a little more involved. It has three parts.
First, we update the tokens using a standard token bucket that increments at some rate and is capped at some burst size. We also decrement tokens to account for packet transmissions.
Second, for an incoming packet, we set its wall-clock departure time to either the current time or some time in the future when it would have made up the shortfall of tokens.
Third, this departure time becomes the packet’s rank in a PIFO.

## Slide 40: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Notes: Ok, so we have looked at two algorithms where the rank computation runs on the switch. The rank computation can, in fact, run anywhere in the network. For instance, let’s compress this pipeline down to a switch. Let’s also introduce an end host.

## Slide 41: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Rank Computation
f = flow(p)
p.rank = f.rem_size
Notes: We can use this end host to compute the ranks for the shortest remaining flow size scheduler. Here, the end host has an RPC-like workload, where each RPC is a flow, and sets the remaining flow size to the remaining number of bytes in the current RPC.

## Slide 42: Beyond a single PIFO
x
1
y
1
x
2
b1
b2
b3
y
2
a1
Hierarchical scheduling algorithms need hierarchy of PIFOs
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
Notes: Ok, so we have seen examples of what a single PIFO can do. Common to these examples is the property that the relative order of buffered packets doesn’t change with future arrivals.
There are algorithms that violate this property, such as hierarchical schedulers. I’ll illustrate this through hierarchical packet-fair queueing. Here, the idea is to divide capacity between two classes, Left and Right, in some ratio. Then, we recursively divide capacity between flows within each class, such as a, b and c, d.
So, let’s see why HPFQ cannot be served by a single PIFO. Let’s say this is the current state of the system, with packets departing from the head. Now, when the first packet from flow a arrives, we need to satisfy two constraints simultaneously. One, classes red and blue must alternate because they share capacity equally. Two, within class red, a must be ahead of b, because it has a much higher weight.
To do this, we need to move the packets from b to new locations so that red and blue alternate. Then, we need to move a1 ahead of all packets of b because a has a much higher weight. This combination of moves from a and b is beyond a single PIFO that cannot change the relative order of packets that are already buffered.
But, it turns out we can do this with a hierarchy of PIFOs.

## Slide 43: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
PIFO-Red
(WFQ on a & b)
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
B
R
B
B
R
R
B
R
Notes: This hierarchy of PIFOs is very natural and has a structure similar to the scheduler. The root PIFO arbitrates between two child PIFOs red and blue, while each child PIFO arbitrates between packets.
So, now, let’s see what happens on enq and deq. When a1 shows up, its class R is enqueued into PIFO root, while a1 is enqueued into the red PIFO. On the deq side, let’s say we dequeued now. Then, we pop B out of PIFO root, see that it points to the blue PIFO out, pop x1 out of the blue PIFO, and transmit x1.
So, by recursively dequeuing PIFOs starting from the root, we can transmit successive packets.

## Slide 44: PIFO in hardware
Performance targets for a shared-memory router
  1 GHz pipeline (64 ports * 10 Gbit/s)
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
  Scheduler is shared across ports
Naive solution: flat, sorted array of 60K elements is infeasible
Exploit observation that ranks increase within a flow: sort 1K head packets, one from each flow
7 mm2 area in a 16-nm library for a
5-level programmable scheduler (4% overhead)
Notes: Ok, let’s see if a PIFO is actually feasible.
To answer this, we set out to meet some performance targets typical of a shared-memory switch found in many dcs today. Here are some typical nos: a pipeline with a 1 GHz clock rate, 1K flows and 60K packets.
One important note is that the scheduler (and so PIFO hardware as well) is shared across all ports. So we don’t need separate PIFO hardware for each port, which means we don’t have to multiply the area overhead by the number of ports.
So, how do we do this? A naïve solution is one large array with 60K elements. An incoming element is compared in parallel to all 60K elements and shifted into the right location. With 60K parallel comparators, this is a non-starter.
Instead, we exploit the fact that most schedulers schedule across flows, with the implicit assumption that packet ranks increase within a flow. How do we use this?
I am not going into any detail here and I am happy to take questions offline, but briefly we designed hardware for a PIFO that sorts across the head packets of each flow alone exploiting the fact that the remaining packets within a flow are already sorted by rank as they arrive. The area for this design is quite modest and only occupies an additional 4% relative to a baseline router chip.

## Slide 45: What algorithms do PIFOs enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
WFQ
STFQ
IntServ
HPFQ
Notes: Ok, so there are a few more algorithms we can’t do. Some of these require floating point operations, others require some periodic timer-driven computations, while others need us to coordinate between the enqueue and dequeue pipelines.

## Slide 46: What algorithms do PIFOs enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
WFQ
STFQ
IntServ
HPFQ
Notes: Ok, so there are a few more algorithms we can’t do. Some of these require floating point operations, others require some periodic timer-driven computations, while others need us to coordinate between the enqueue and dequeue pipelines.

## Slide 47: Broader impact
Packet transactions now in P4
Industry interest in PIFOs, Domino’s compiler techniques
Notes: So to conclude by now you are convinced that high-performance networking needs speciailzied hardware. But specialization conflicts with flexibility. If you specialize too much your hardware becomes obsolete tomorrow, if you specialize too little, it doesn’t give you good performance. This is now increasingly true because the slowing down of Moore’s law means that you can no longer just bank on the free lunch of x86 processors getting faster.
My solution to these problems is to tailor primitives to restricted classes of router functionality such as atoms for streaming algos and PIFOs for scheduling.
Beyond the papers, there’s been broader community and industry interest in these ideas. Working with the P4 design group, we introduced the idea of packet transactions into P4, an emerging language to program networking hardware. There has also been industry interest, particularly from Xilinx on implementing PIFOs in their FPGA hardware, and from Barefoot in Domino’s compilation techniques.
//More generally, I think this kind of restricted programmability is of use to other domains beyond networking as the stalling of transistor scaling causes us to do this oxymoronic //thing of specializing hardware and making it flexible at the same time. In future work, I hope to apply the same kind of thinking to other high-performance systems beyond //networking, such as machine learning and video encoding.

## Slide 48: Future Work
Hardware and software for programmable routers
  Primitives for network measurement, host networking, etc.
  Eliminating performance cliffs in programmable pipelines
Specialized systems
  Balancing hardware specialization and software programmability
  Designing and programming a cluster of accelerators and cores
Notes:   Eliminating performance cliffs in a router pipeline

## Slide 49: Backup slides
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0
: (pkt.old + 1);
count = pkt.new;
pkt.old = count;
count = pkt.old + 1;
state = mux(state RELOP C, true) ?
mux(state + p.a, 0)
: mux(state + p.c, 0)

## Slide 50: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
Notes: If you need to cut something: slide 25 and 26.
Happy to talk about the impl. Details offline.
Try and fix orientation of the scheduler.
Feedback: If the point is to just quickly show that you have a hardware implementation and it’s feasible, just use the detailed hardware diagram from the CSAIL talk.
TODO: Give a very brief description + hardware diagram from the CSAIL talk.
Our design has two parts.
A flow scheduler schedules across the head packets of all flows, while a rank store stores packets ranks in a first-in first-out queue for each flow.
The flow scheduler is really a PIFO over the head packets alone.
When an element (say) C6, from flow C with rank 6, is enq, it’s just appended to the back of the rank store. When D4 shows up, it bypasses the rank store and directly goes to the flow scheduler. When we deq, we just pop the head of the flow scheduler array to get A0, then reach into the rank store, pull out A2 and insert it into the flow scheduler array.
If you notice, the flow scheduler has to insert an element like A2 into a sorted array, which we do by comparing it in parallel to all elements in the array. Except now, we can actually do this because the sorted array has only 1K head packets, not all 60K packets.
This block supports up to 1 enq + 1 deq every clock cycle, which is a ns in a typical scheduler. It can also be sliced up across many logical PIFOs, which are PIFOs that are independent of each other, but share the same underlying hardware impl. An example is PIFOs for different output ports, whose schedulers run independently.

## Slide 51: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
7 mm2 area in a 16-nm library for a
5-level programmable scheduler (4% overhead)
Notes: Our design has two parts.
A flow scheduler schedules across the head packets of all flows, while a rank store stores packets ranks in a first-in first-out queue for each flow.
The flow scheduler is really a PIFO over the head packets alone.
When an element (say) C6, from flow C with rank 6, is enq, it’s just appended to the back of the rank store. When D4 shows up, it bypasses the rank store and directly goes to the flow scheduler. When we deq, we just pop the head of the flow scheduler array to get A0, then reach into the rank store, pull out A2 and insert it into the flow scheduler array.
If you notice, the flow scheduler has to insert an element like A2 into a sorted array, which we do by comparing it in parallel to all elements in the array. Except now, we can actually do this because the sorted array has only 1K head packets, not all 60K packets.
This block supports up to 1 enq + 1 deq every clock cycle, which is a ns in a typical scheduler. It can also be sliced up across many logical PIFOs, which are PIFOs that are independent of each other, but share the same underlying hardware impl. An example is PIFOs for different output ports, whose schedulers run independently.

## Slide 52: Acknowledgements
MIT: Suvinay Subramanian, Hari Balakrishnan, Mohammad Alizadeh
Barefoot Networks: Changhoon Kim, Anurag Agrawal, Steve Licking, Mihai Budiu
Cisco Systems: Shang-Tse Chuang, Sharad Chole, Tom Edsall
Microsoft Research: George Varghese
Stanford University: Sachin Katti, Nick McKeown
University of Washington: Alvin Cheung
Notes: I would like to thank an outstanding set of collaborators from
MIT, Barefoot Networks, Cisco Systems, Microsoft Research, Stanford, and University of Washington.

## Slide 53: Recent activity in the area
2008--2013: OpenFlow: Specify router-to-router connectivity
2013--now: Programmable router chips (Barefoot’s Tofino, Intel’s FlexPipe, Cavium’s Xpliant), programming languages (P4)
Router chip programmability is still nascent
  Goal: feature parity with legacy routers without baking in features
  Basic header manipulation; recognize new protocol formats

## Slide 54: Code pipelining in one slide
Goal: if each stage runs atomically, transaction must run atomically
Easy without state: only intra-packet dependencies
  Perform depth-first search on DAG of intra-packet dependencies
  All nodes at the same depth belong to the same pipeline stage
State causes inter-packet dependencies
  Cycles in dep. graph: state read must follow write from previous packet.
  Find strongly connected components; contract SCCs to single nodes
  Depth-first search on resulting DAG

## Slide 55: Future work: An era of specialized systems
With Moore’s law ending, hardware specialization is a necessity
  Video encoding, graphics, machine learning, bitcoin mining, …
Recurring tension between programmability and specialization
  Simple question: How do we design a cluster of processors and accelerators for (machine learning / video encoding / …)?
  Requires synthesizing ideas from languages, compilers, hardware, and networking
Notes: TODO: Check if this is necessary.
If we were completely untethered.
    What’s in the accelerators?
    What’s the storage medium?
    What’s the right programming model?
    What’s the right congestion-control protocol?

## Slide 56: Early routers
Early routers were eminently programmable minicomputers
  IMPs (1969): Honeywell DDP-516 950 Kbit/s (The IMP paper)
  MIT C gateway (1980-1982): 500 Kbit/s on M68K (Lixia Zhang’s paper)
  Fuzzballs (1971-1991): Most known for use on the NSFNET Phase-1 Backbone Network (1986-88): DEC PDP-11/73: 400 Kbit/s (Mill’s paper from SIGCOMM 88)
  Stanford multiprotocol router (1981): DEC PDP 11 / Motorola 68000
  Proteon (1985): 80 Mbit/s (http://www.historyofcomputercommunications.info/Book/12/12.22_Proteon.html#_ftn3)

## Slide 57: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow
Cannot express some scheduling algorithms, e.g., output shaping.
Notes: So it turns out that we can use a tree of PIFOs for many more algorithms. I am not discussing these here, but the paper has further details.
More importantly, we have algorithms that our abstraction doesn’t support. One important class is output shaping, where we rate limit dequeues from the scheduler. We can’t implement this because PIFOs provide prog. on the enq side, not on the deq side. Again, the paper discusses this in depth.

## Slide 58: FAQ
How is this different from P4?
  When we started this work a year ago, P4 was much closer to the hardware. Over time, it’s gotten more high-level, thanks in some part to this work (sequential semantics, ternary operators).
  We do have a P4 backend.
Why a pipeline?
  NPUs have a shared-memory architecture, but sharing memory is hard and slows down the switch.

## Slide 59: FAQ
What’s in the compiler?
  Strongly Connected Components to extract atomic portions.
  Code generation using program synthesis.
Do the atoms generalize in an ML sense?
  We don’t know for sure. We designed the atoms and were able to tweak them a little bit to serve more algorithms. But this is something we don’t yet have a handle on.

## Slide 60: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 61: Relationship to prior compiler techniques
Technique | Prior work | Differences
If Conversion | Kennedy et al. 1983 | No breaks, continue, gotos, loops
Static Single-Assignment | Ferrante et al. 1988 | No branches
Strongly Connected Components | Lam et al. 1989 (Software Pipelining) | Scheduling in space instead of time
Synthesis for instruction mapping | Technology mapping | Map to 1 hardware primitive, not multiple
 | Superoptimization | Counter-example-guided, not brute force

## Slide 62: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 63: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we convert to static single assignment form, which simplifies dependency analysis.
Static single assignment gets its name from the fact that all variables are assigned
Exactly once and no more.
It’s useful because it gets rid of write-after-read and write-after-write dependencies. In our case,
converting to SSA is trivial because we operate on straight-line code with no branches. Typical
SSA implementations are far more involved because they have to deal with branching.

## Slide 64: Expression Flattening
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
pkt.tmp = pkt.arrival - last_time[pkt.id];
pkt.tmp2 = pkt.tmp > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp2
? pkt . new_hop
: saved_hop [ pkt . id ];
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: The last step in canonicalization is to flatten arbitrarily complicated expressions
to bring them into a form closer to the underlying hardware.
(Quickly skim over this.)

## Slide 65: Instruction mapping: results
Generic method to handle fairly complex templates
Templates determine if a Domino program can run at line rate.
Example results:
  Flowlet switching needs conditional execution to save next hop information:
  saved_hop[pkt.id] = pkt.tmp2 ? pkt.new_hop : saved_hop[pkt.id]
  Simple increment suffices for heavy-hitter detection
  count_min_sketch[hash] = count_min_sketch[hash] + 1
Sequential to parallel code
Hardware constraints
Canonicalization

## Slide 66: Generating P4 code
Required changes to P4
  Sequential execution semantics (required for read from, modify, and write back to state)
  Expression support
  Both available in v1.1
Encapsulate every codelet in a table’s default action
Chain together tables as P4 control program
Notes: Say that this project led to sequential execution semantics.

## Slide 67: Branch Removal
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I ‘ll go through these steps quickly. The first step in canonicalization is to remove branching statements.
Branches complicate control flow and make it harder to infer dependencies.
We eliminate branches using a procedure called if conversion that transforms them into C’s conditional operator.
because the only kind of branch we have is an if statement, if conversion is very straightforward in our case, because
we don’t have any kind of unstructured control flow such as a goto, break, or continue, that significantly complicate
if conversion.
This makes the code flow straight from one statement to the next without exception and makes it very easy to infer
dependencies as well: everything on the right of a “equals” is read and the one statement on the left is written.

## Slide 68: Handling State Variables
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we identify state variables, because they complicate the pipelining procedure.
In the absence of state variables, once you have straight-line code, you only need to
consider how you would pipeline the code for a single packet’s processing and you are
done because all other packets follow the same pipeline and there is no interaction
between packets. With state variables, you need to consider interactions between packets.
To simplify our analysis of state variables and dependencies between packets, we explicitly
limit the ways in which state variables can be accessed. We allow only reads and writes to
state and all other arithmetic happens on packet variables. This also lets us reuse an old
value of a state variable down the pipeline if required.

## Slide 69: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 70: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.

## Slide 71: The Domino compiler
Branch Removal
Domino
Handle state variables
Code Pipelining
Instruction Mapping
Processing Pipeline
Canonicalization
(Sequential Code)
Sequential to
parallel code
Respecting hardware
constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 72: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Pair up read/write
flanks
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we pair up reads and writes to state variables to capture the notion
that state variables remain local to a specific stage in the pipeline. If not,
we would have to read from one stage and write from another requiring
us to route longer wires on the chip.

## Slide 73: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Condense strongly
connected components
into codelets
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we look for stongly connected components in this graph,
and condense them into what we call codelets. These capture the essence of
what operations need to be run atomically for the entire transaction to execute atomically.
Now that we have eliminated circles in the graph, we can schedule the resulting
acyclic graph. This is a straightforward process known as critical
path scheduling where we put each node in the earliest pipeline
stage following all its predecessors.

## Slide 74: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Add packet-field
dependencies
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we add read after write dependencies, where we draw an arrow from the
node that writes a value to the node which reads that value.
This is ALL we need to do to handle dependencies in our case because there are
no other waw or war dependencies after SSA.

## Slide 75: Programming with Packet Transactions
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
Pipeline
Domino
pkt.new_hop =
hash3(pkt.sport,
pkt.dport,
pkt.arrival)
%NUM_HOPS;
pkt.id =
hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: TODO: Per Ravi, Hongzi, consider switching to a simpler example like sampled netflow
To give you a flavor for programming using packet transactions, we look at programming
flowlet switching, a data-plane load-balancing algorithm.
To write imperative code for each packet transaction, we use a language
called Domino with a syntax resembling C. On the right, we contrast it against
writing code in P4.
So let me first describe flowlet switching. Its logic is shown here.
The idea in flowlet switching is to load balance groups of packets separated by
a long gap in time across different paths to carry out more fine-grained traffic
splitting relative to standard ECMP.
The logic in is straightforward. You start off by populating a new
hop variable in each packet using some dynamic quantity such as the packet’s arrival time.
Then, you check if the intepacket gap between this packet and its previous one is sufficiently
large and update a state variable called saved_hop if so.
Then, you simply update the last time and set the next hop to the saved hop (which is either
the new value or the old one).
Now, if you were to explain flowlet switching to someone else, like I just did, it’s natural to express its logic
as a block of imperative code and programming in packet transactions lets you do exactly that.
The logic itself becomes the body of a function. This function flowlet is a packet transaction, which conceptually
Executes atomically on each packet. The rest of the Domino program declares state variables as global
variables, packets as structures, and lets you use the rest of C including the macro preprocessor.
================================
So that’s how you express flowlet switching in Domino. When you compile this code it generates
a pipelined implementation in P4 as shown here. This is how you would program the switch today.
The rest of this talk will describe how its relatively straightforward to build a compiler that achieves
this transformation if you exploit characteristics of the underlying domain of line-rate switches.

## Slide 76: The quest for programmability
Switch | Year | Line-rate
Cisco Catalyst | 1999 | 32 Gbit/s
Broadcom 5670 | 2004 | 80 Gbit/s
Broadcom Scorpion | 2007 | 240 Gbit/s
Broadcom Trident | 2010 | 640 Gbit/s
Broadcom Tomahawk | 2014 | 3.2 Tbit/s
Programmability => 10--100x slower than line rate.
System | Year | Substrate | Performance
Click | 2000 | CPUs | 170 Mbit/s
Intel IXP 2400 | 2002 | NPUs | 4 Gbit/s
RouteBricks | 2009 | Multi-core | 35 Gbit/s
PacketShader | 2010 | GPUs | 40 Gbit/s
NetFPGA SUME | 2014 | FPGA | 100 Gbit/s
Notes: Cisco Catalyst: http://www.cisco.com/c/dam/en/us/products/collateral/switches/catalyst-6807-xl-switch/white_paper_c11-728264.doc/_jcr_content/renditions/white_paper_c11-728264_1.jpg
Intel IXP 2400: http://www.intel.com/design/network/papers/ixp2400.pdf: 4 Gbit/s (copyright 2002)
Broadcom 5670 (2004): 80 Gbit/s (8 ports of 10 G) (https://www.broadcom.com/collateral/pb/5670-PB05-R.pdf, 2004)
Broadcom Scorpion (2007) (24 * 10 G from DCTCP paper, and http://www.enterprisetech.com/2014/09/24/broadcom-fights-ethernet-rivals-tomahawk-chips/ suggests 2007)
Trident (2010): 64 * 10 G = 640 G
Trident II (2012): 100 * 10 G = 1 Tbit/s
BCM Tomahawk (2014): 3.2 Tbit/s
Trident and Tomhawk numbers taken from the pages below.
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
TODO: Turn this into a graph.

## Slide 77: The quest for programmability
Programmability => 10--100x slower than line rate.
Chart: Performance scaling of switches
| 2000.0 | 2002.0 | 2009.0 | 2010.0 | 2014.0
Software routers | 0.17 | 4 | 35 | 40 | 100
Line-rate routers | 32 | 80 | 240 | 640 | 3200
Notes: People have recognized this need at least since the late 90s and quite a few software switch platforms have been developed where you take an existing programming substrate and repurpose it for networking.
Now, here’s a line graph showing how the performance of these software switches has scaled with time, and we can see that it’s improved about 1000 fold since 2000, which is quite impressive.
But, at the same time, if you look at the highest end switches (or what I call line-rate switches, because they run at the highest speed that the cable or line can support), they have always been between 10 and 100 times faster than these software platforms. That’s because they have been specialized from the ground up to support just routing. As a result, these programmable platforms never really gained much adoption because they were always slower than the fastest switches.
So, the takeaway, historically is that programmability has cost us 10—100x in performance. And my research looks at designing programmable switch platforms without any performance penalty.

## Slide 78: Compiler targets: diagram
Operation:
+, -, >, <,
AND, OR
pkt.f1/
constant
pkt.f2/
constant
pkt.f3
pkt.f
constant
x
2-to-1
Mux
pkt.f
constant
x
2-to-1
Mux
x
0
2-to-1
Mux
Adder

## Slide 79: Why are switches pipelined?

## Slide 80: Performance requirements at line rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
10 operations per packet: routing, access control (ACL), tunnels, …
Need to process 1 billion pkts/s, 10 ops per packet
Notes: Important segue way here: Let’s talk about why a pipeline is the right hardware architecture for a switch by arguing for it from first principles.

## Slide 81: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
10 GHz processor
Packets
match/action
Can’t build a 10 GHz processor!

## Slide 82: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action

## Slide 83: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action
match/action
match/action
match/action
Memory replication increases die area

## Slide 84: Function-parallel or pipelined architecture
Route lookup table
1 GHz circuit
ACL lookup table
Tunnel lookup table
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
match/action
match/action
match/action
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 85: P4 comparison

## Slide 86: Programming with packet transactions
Algorithm | LOC | P4 LOC
Bloom filter | 29 | 104
Heavy hitter detection | 35 | 192
Rate-Control Protocol | 23 | 75
Flowlet switching | 37 | 107
Sampled NetFlow | 18 | 70
HULL | 26 | 95
Adaptive Virtual Queue | 36 | 147
CONGA | 32 | 89
CoDel | 57 | 271
Notes: Ok, so now that I have shown you how to design these atoms, let’s look at what you can do with them. For this, we need some algorithms, and we picked a set spanning congestion control, measurement, load balancing, and AQM, and wrote them in Domino.
Their lines of code are listed here and they aren’t very different from the number of LOC you would have to write when programming a software switch with these algorithms. So that’s some measure of the abstraction being easy to use.