## Slide 1: Fast and programmable network infrastructure
Anirudh Sivaraman

## Slide 2: Outline
Motivation for fast and programmable networks
Previous work: Designing fast and programmable routers
Ongoing work: How should programmable routers be used?
Future work: Programmable network infrastructure for wireless

## Slide 3: Traditional network architecture
Simple routers; most functionality resides on end hosts

## Slide 4: But, today’s reality is very different
We are demanding more from routers: ACLs, tunnels, measurement etc
Yet, the fastest routers have historically been fixed-function
Rate of innovation exceeds our ability to get things into routers
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters
Notes: Fixed-function routers are great because they let you evolve one part of the network alone
But, we seem to demand much more, and there’s no consensus as to what should be in a router
But, routers are fixed-function, so even though they support some of these demands, they can’t cater to everyone’s requirements.
Now bc there’s no consensue and routers are fixed function, rate of innovation is …

## Slide 5: But, today’s reality is very different
We are demanding more from routers: ACLs, tunnels, measurement etc
Yet, the fastest routers have historically been fixed-function
Rate of innovation exceeds our ability to get things into routers
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 6: One approach: Use a software router
Chart: Aggregate Capacity
| 1969 | 1982 | 1983 | 1985 | 1999 | 2000 | 2002 | 2004 | 2007 | 2009 | 2010 | 2012 | 2014
Fastest router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 32 | 80 | 240 | 640 | 1280 | 3200
Software router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 0.1 | 0.17 | 4 | 35 | 40 | 100
Software routers 10—100x slower than the fastest routers
Software routers suffer from non-deterministic performance

## Slide 7: Prior projects: performance+programmability
Domino (SIGCOMM ‘16):
programming streaming
algorithms
PIFO (SIGCOMM ‘16):
programming scheduling
algorithms
Marple (SIGCOMM ‘17):
programmable and scalable
measurement
Performance+programmability for important classes of router functions
Scheduler
Ingress pipeline
Egress pipeline
Notes:   I’ll discuss two pieces of work: Domino to run on the pipelines and PIFO to run on the scheduler.

## Slide 8: Broader impact
Many ideas from Domino are now in P4, an emerging language for programmable network devices
Industry interest in PIFOs, Domino’s compiler techniques

## Slide 9: How should programmable routers be used?
Let’s assume fast and programmable routers can be built.
How should we use them?
What stays on the end hosts and what should be moved into the network?
E.g., what’s the best location to implement DoS prevention/measurement/congestion control/load balancing/X?
Evaluate using a testbed with a high-speed programmable switch from Barefoot Networks
Notes: Router vendors: Can now design routers in firmware, easier to fix bugs, easier to respond to customer requests
Network operators (e.g., Google, Microsoft, enterprises etc.): Can add features without haggling with ASIC vendor
Stress that programmability and configurability are really not all that different.. Richer configurability is already happening. Programmability is the logical next step because it simplifies your chip, makes it future proof, which is especially important in an era of rising silicon mask costs. P4 may not be the final word on router programmability. It may not all be portable either. But I think the current generation of fixed-function router SDKs will be replaced by richer, more programmable DSLs for routers like what CUDA did for GPUs.
Future work:
  Costs and benefits of a network with enhanced network functionality?

## Slide 10: Hardware+software for wireless
Significant packet processing in both WiFi and cellular networks
  Especially in the context of the physical layer
Designing hardware accelerators for emerging technologies (e.g., 5G)
  Splitting the wireless stack between the host processor and an accelerator