## Slide 1: Programmable networks
Slides courtesy of Patrick Bosshart, Nick McKeown, and Mihai Budiu

## Slide 2: Main references
Forwarding metamorphosis: fast programmable match-action processing in hardware for SDN (SIGCOMM 2013)
P4: programming protocol-independent packet processors (SIGCOMM CCR 2014)

## Slide 3: Outline
Motivation for programmable switches
Early attempts at programmability
Programmability without losing performance: The RMT model
The P4 programming language
What’s happened since?: SmartNICs and Data Processing Units (DPUs)

## Slide 4: Background
Two timescales in a network’s switches.
Data plane: packet-to-packet behavior of a switch, short timescales of a few ns
Control plane: Establishing routes for end-to-end connectivity, longer timescales of a few ms

## Slide 5: Software Defined Networking: What’s the idea?
Separate network control plane from data plane.
Notes: Remind them that OpenFlow is based on match + action.
But it is restricted to a specific set of headers, and nothing more.

## Slide 6: The consequences of SDN
Move control plane out of the switch onto a server.
Well-defined API to data plane (OpenFlow)
  Match on fixed headers, carry out fixed actions.
  Which headers: Lowest common denominator (TCP, UDP, IP, etc.)
Write your own control program.
  Traffic Engineering
  Access Control Policies
Notes: Remind them that OpenFlow is based on match + action.
But it is restricted to a specific set of headers, and nothing more.

## Slide 7: But, the network isn’t truly software-defined
What else might you want to change in the network?
Think of some algorithms that require switch support.
RED, WFQ, PIE, XCP, RCP, DCTCP, …
Lot of performance left on the table.
What about new protocols like IPv6?
Notes: Pause for question: Why might you ever want to change your network’s switches?

## Slide 8: The solution: a programmable switch
Change switch however you like.
Each user “programs” their own algorithm.
Much like we program desktops, smartphones, etc.
Vision: make the network (control and data planes) as easy to program as a computer.
Notes: Pause for question: Why might you ever want to change your network’s switches?

## Slide 9: Early attempts at programmable switches
Chart: Performance scaling
| 1999 | 2000 | 2002 | 2004 | 2007 | 2009 | 2010 | 2014
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Line-Rate router | 32 | 80 | 240 | 640 | 3200
10—100 x loss in performance relative to line-rate, fixed-function switches
Unpredictable performance (e.g., cache contention)
Notes: How would _you_ design a programmable router?
Mention that it is on log scale
Define line rate
Unpredictable performance examples: hardware config (number of cores, RAM size, etc.)

## Slide 10: The RMT model: programmability + performance
Performance: 640 Gbit/s (also called line rate), now 6.4 Tbit/s.
Programmability: New headers, new modifications to packet headers, flexibly size lookup tables, (limited) state modification
Notes: What is match-action?
Why use a pipeline?

## Slide 11: The right architecture for a high-speed switch?
Notes: What is match-action?
Why use a pipeline?

## Slide 12: Performance requirements at line-rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
~10 operations per packet (e.g., routing, ACL, tunnels)
Need to process 1 billion packets per second, 10 ops per packet
Notes: Before we discuss the RMT model, let’s talk a bit about the switch architecture.
The paper doesn’t go into much detail about this and assumes a switch is going to have a pipeline of match-action tables (fixed or not). Why is this a good architecture?
Q: Why is a switch architected as a pipeline? Are there other architectures?

## Slide 13: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
10 GHz processor
Packets
Can’t build a 10 GHz processor!

## Slide 14: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets

## Slide 15: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
Memory replication increases die area
Lookup table
Match
Action
Match
Action
Match
Action
Lookup table
Match
Action
Match
Action
Match
Action
Lookup table
Match
Action
Match
Action
Match
Action
Notes: Rhetorical question: What is the problem with this architecture?

## Slide 16: Function-parallel or pipelined architecture
Route lookup table
Match
Action
1 GHz circuit
ACL lookup table
Match
Action
Tunnel lookup table
Match
Action
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
But, needs careful circuit design to run at 1 GHz
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 17: Fixed function switch
Deparser
In
Queues
Data
Out
ACL Stage
L3 Stage
L2 Stage
Action: set L2D
Stage 1
L2 Table
L2: 128k x 48
Exact match
Action: set L2D, dec TTL
Stage 2
L3 Table
L3: 16k x 32
Longest prefix
match
Action: permit/deny
Stage 3
ACL Table
ACL: 4k
Ternary match
Parser
Notes: Ok, so with this pipeline model, here’s what a fixed function switch looks like
Each table is hardwired to a specific task.
If you want to size smaller or larger tables, you are out of luck.

## Slide 18: Adding flexibility to a fixed-function switch
Flexibility to:
  Trade one memory dimension for another:
    A narrower ACL table with more rules
    A wider MAC address table with fewer rules.
  Add a new table
    Tunneling
  Add a new header field
    VXLAN
  Add a different action
    Compute RTT sums for RCP.
But, can’t do everything: regex, state machines, payload manipulation
Notes: Trade width and height flexibly within the table.
Maybe show how different logical tables can share resources within and across stages.
Maybe use Nick’s slides to illustrate this.
Add some examples.

## Slide 19: RMT: Two simple ideas
Programmable parser
Pipeline of match-action tables
  Match on any parsed field
  Actions combine packet-editing operations (pkt.f1 = pkt.f2 op pkt.f3) in parallel
Notes: This is all you really need to know about the paper 
The rest is just how to make it run at 1 GHz
The idea that you can take different logical tables and split them across pipelines in a flexible way.

## Slide 20: Configuring the RMT architecture
Parse graph
Table graph

## Slide 21: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
IPV6
TCP
UDP
Ethernet IPV4 TCP
Packet:

## Slide 22: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
TCP
UDP
Ethernet IPV4 TCP
Packet:

## Slide 23: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
TCP
UDP
Ethernet IPV4 RCP TCP
Packet:
RCP

## Slide 24: Reconfigurable Match Tables: The Table Graph
VLAN
MAC
FORWARD
IPV4-DA
ETHERTYPE
RCP
ACL
IPV6-DA

## Slide 25: How do the parser and match-action hardware work?

## Slide 26: Programmable parser (Gibb et al. ANCS 2013)
State machine + field extraction in each state (Ethernet, IP, etc.)
State machine implemented as a TCAM
Configure TCAM based on parse graph
Notes: Say that it’s not very different from how grep works on Linux.

## Slide 27: Match/Action Forwarding Model
Programmable Parser
Deparser
In
Queues
Action
Stage 1
Match Table
Action
Stage 2
Match Table
…
Data
Out
Action
Stage N
Match Table
Match
Action Stage
Match
Action Stage
Match
Action Stage

## Slide 28: RMT Logical to Physical Table Mapping
TCAM
640b
640b
Physical
Stage n
Physical
Stage 2
Logical Table 1
Ethertype
Logical Table 6
L2D
8 UDP
2
VLAN
3
IPV4
5
IPV6
4
L2S
7 TCP
SRAM
HASH
Physical
Stage 1
ACL
UDP
TCP
L2S
L2D
IPV4
ETH
VLAN
IPV6
9 ACL
Table Graph
Action
Match Table
Action
Match Table
Action
Match Table
Notes: To make it possible to efficiently use multiple stages of match tables, it is assumed that the RMT Model can be configured to map Logical Tables to the Physical Tables.
To create bigger tables, one table may traverse multiple stages.
To create many smaller tables, several tables can be packed into one stage.
To make the allocation even more flexible, the Action instructions and the Statistic could share the same table space.
This slide gives a crude representation of how the the Logical Tables could be mapped to the Physical Tables.
In practice, the control plane would need to create a Table Flow Graph (to accompany the Parse Graph) to decide how the Logical Tables are mapped.
The control plane is assumed to know the number and size of the physical stages available.
There could be as few as 1 stage. A given switch might only allow Logical Tables to directly correspond to Physical Tables.

## Slide 29: Action Processing Model
Instruction
ALU
Match result
Header In
Field
Header Out
Field
Data
Notes: Action processing is assumed to be available in each physical stage of the pipeline.
The headers are available along with the match result and metadata. Optional state could be available to the Action Processors.
There are assumed to be some number of processors (could be 1, could be hundreds) to perform Actions on headers.
The Action instruction set is assumed to be protocol independent (e.g. “insert these 8 bits starting at bit 19 of the 3rd header”).

## Slide 30
ALU
VLIW Instructions
Match result
Modeled as Multiple VLIW CPUs per Stage
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Obvious parallelism: 200 VLIWs per stage
Notes: Allows you to edit packet fields in parallel.

## Slide 31: Questions
Why are there 16 parsers but only one pipeline?
This switch supports 640 Gbit/s. Switches today support > 1 Tbit/s. How does this happen?
What do you think the chip’s die consists of?
How much do each of these components contribute?
What does RMT not let you do?

## Slide 32: How does programmability affect chip area?
40% Serial I/O
40% Memory
10% Wire
10% Logic
Wire
Logic
Programmability mostly affects logic, which is a small fraction of area.

## Slide 33: Programming RMT: P4
RMT provides flexibility, but programming it is akin to x86 assembly
Concurrently, other programmable chips being developed: Intel FlexPipe, Cavium Xpliant, CORSA, …
Portable language to program these chips
SDN’s legacy: How do we retain control / data plane separation?

## Slide 34: P4 Scope
Control plane
Data plane
Control traffic
Packets
Table mgmt.
Traditional switch
Control plane
Data plane
P4 Program
P4-defined switch
P4 table mgmt.
Notes: This is the P4 API: a new API between the control-plane and the data plane.
The data plane performs mostly stateless high-speed processing.
The data plane is lean and fast; most of the complexity is still in the control plane. P4 does not address this aspect.

## Slide 35: Q: Which data plane? A: Any data plane!
Control plane
Data plane
Programmable switches
FPGA switches
Programmable NICs
Software switches
Notes: P4 should be portable across a large spectrum of switch implementations.

## Slide 36: P4 main ideas
Abstractions for
  Programmable parser: headers, parsers
  Match-action: tables, actions
  Chaining match-action tables: control flow
Fairly simple language. What do you think is missing?
  No type system, modularity, libraries, etc.
Somewhat strange serial-parallel semantics. Why?
  Actions within a stage execute in parallel, stages execute in sequence
Notes: Emphasize that this is a first step and things will get better.

## Slide 37: Reflections on a programmable switch
Why care about programmability?
  If you knew exactly what your switch had to do, you would build it.
  But the only constant is change.
  (Hopefully) no more lengthy standard meetings for a new protocol.
  Attractive to switch vendors like CISCO/Arista
    Hardware development is costly.
    Can be moved out of the company.
  Attractive to chip manufacturers, e.g., Broadcom, Intel
    Think in terms of reusable instructions/primitives, not bespoke features
    Bugs are less expensive because they move to software/firmware.
    Chip is easier to design.

## Slide 38: Why now?
When active networks tried this is 1995, there was no pressing need
What’s the killer app today?
  For SDN, it was network virtualization.
  I think it’s measurement/visibility/troubleshooting for prog. switches
More far out: Maybe push the application into the network?
  HTTP proxies?
  Speculative Paxos, NetPaxos.
  Like GPUs, maybe programmable switches will be used as application accelerators (e.g., NetCache)?
Notes:   The steady state of a network is well understood.
  When things change, people have a hard time debugging, and would like instrumentation.

## Slide 39: What’s happened since?

## Slide 40: Growing research interest in academia
P4 compiler technology (Jose et al., NSDI 2015)
Stateful algorithms (Sivaraman et al., Packet Transactions)
Higher-level languages (Arashloo et al., SNAP)
Programmable scheduling (Sivaraman et al., PIFO; Mittal et al., Universal Packet Scheduling)
Protocol-independent software switches (Shahbaz et al., PISCES)
Programmable NICs (Kaufman et al., FlexNIC)
Network measurement (Li et al., FlowRadar)
Many more papers since
Notes: Flesh this out a little more.

## Slide 41: Momentum around p4.org in industry
P4 reference software switch, compiler, workshops
Industry adoption:
  Netronome Agilio,
  Xilinx Alveo,
  Intel/Barefoot Tofino,
  CISCO Silicon One,
  VMWare XDP (programmability within the NIC driver),
  Pensando SmartNIC,
  NVIDIA/Mellanox DOCA,
  Fungible DPU
  Google (for specifying fixed-function chip behavior)
Similar languages (e.g., NPL by Broadcom)
Culture shift: move towards open source
Notes: Too early to say if this will be widely adopted or not.
Staid companies such as AT&T and CISCO showing up at the working group meetings.
Spend more time on these slides and less time on paper details.

## Slide 42: In-network computing
Move application logic into the network for your favorite application:
  NetCache: load-balanced cache for key-value stores
  NetChain/NetLock: lock managers (e.g., ZooKeeper)
  Harmonia/Pegasus: replicated storage
  SwitchML: ML training inside the network
  String searching
  Stream processing
  …

## Slide 43: SmartNICs
Move programmability to network-interface cards to offload processing from end hosts
  FPGA-based: Xilinx Alveo, Microsoft Azure SmartNIC, NVIDIA/Mellanox Innova 2
  Multicore-based: Broadcom Stingray, BlueField, Cavium LiquidIO
  ASIC/Pipeline-based: Pensando
  Data Processing Units: Fungible
Many programmable in a combination of C and P4
FPGA variants require reprogramming in Verilog
Notes: The FPGA variants do permit easy reconfigurability in software
Also mention P4-NetFPGA briefly

## Slide 44: Programmability in virtual networks
Programmable virtual switches (e.g., OVS): PISCES
Programmability at the RPC layer
  Service meshes interconnect microservices through application-level proxies
  These proxies are programmable through an extension model, e.g., load WebAssembly bytecode into an Envoy/Istio proxy.
Network programmability for Kubernetes clusters.
  Cilium project based on eBPF
Allows us to think of programmability for users of the cloud

## Slide 45: Concluding thoughts
What is the right location for programmability?
  End host, in-network, both?
Who should be programming these networks?
  Network operator, equipment manufacturer, chip vendor?
What is the right hardware architecture?
  ASIC pipeline, FPGAs, multicores?
What is the right language across the entire network?
  P4, C, some combination of the two?
Programmability for virtual networks
  A lot of networking is moving to the cloud, but most network programmability has so far been for on-prem networks
Programmability for the physical layer
  Signal processing for emerging cellular/wireless standards