## Slide 1: Making the fastest routers programmable
Anirudh Sivaraman

## Slide 2: Traditional network architecture
Fixed-function routers and programmable end points
Notes: Maybe add really high-level overview of what people want from programmable routers

## Slide 3: This architecture is unsustainable
What goes into a fixed-function router? No consensus after decades of router design
Rate of innovation exceeds our ability to get things into routers
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
pFabric
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 4: This architecture is unsustainable
What goes into a fixed-function router? No consensus after decades of router design
Rate of innovation exceeds our ability to get things into routers
Workaround: Indirect and inaccurate measurement/control from end points
Fix: Don’t bake policies into routers; instead provide mechanisms
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
pFabric
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters
Notes:   Mention tomography here: whole area devoted to approximately infer the internal characteristics of a network from data collected at the end point.
  TODO: Maybe gray out PIE a bit here.

## Slide 5: One approach: Use a software router
Chart: Aggregate Capacity Per Unit
| 1969.0 | 1982.0 | 1983.0 | 1985.0 | 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2012.0 | 2014.0
Fastest router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 32 | 80 | 240 | 640 | 1280 | 3200
Software router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 0.1 | 0.17 | 4 | 35 | 40 | 100
Software routers 10—100x worse than the fastest routers
Software routers suffer from non-deterministic performance

## Slide 6: Vision: programmability and performance
Algorithm:
For each packet
Calculate average queue size
if min < avg < max
calculate probability p
mark packet with probability p
else if avg > max
mark packet
Compiler
Useful programmability without losing performance
Scheduler
Ingress pipeline
Egress pipeline
High-speed router:
Notes:   Mention that this requires us to think carefully about the
  Functions we need to program.
  The programming models and compilers to program them in.
  The hardware we need.

## Slide 7: This Talk
  PIFO (SSACCABEKM SIGCOMM ‘16): programming the scheduler
    The first primitive that allows us to program scheduling algorithms
    Modest chip area cost when implemented in high-speed hardware
  Domino (SCBKABVML SIGCOMM ‘16): programming streaming algorithms
    The first hardware primitives for high-speed execution of streaming algorithms
    A method to extract these primitives from a corpus of algorithms
My work
Can get performance+programmability for many router functions

## Slide 8: Programmable Packet Scheduling at Line Rate (SIGCOMM 2016)
Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh,
Sharad Chole, Shang-Tse Chuang, Anurag Agrawal, Hari Balakrishnan,
Tom Edsall, Sachin Katti, Nick McKeown
Joint work with collaborators at MIT, Cisco Systems,
Stanford University, and Barefoot Networks

## Slide 9: Why programmable scheduling?
Different performance objectives demand different schedulers
  Isolating different tenants in a datacenter: fair queueing
  Single tenant with many short flows: shortest remaining processing time
Status quo: Rigid schedulers baked into hardware
  Some combination of round robin + priorities + rate limits
  Can configure coefficients, but not program a new algorithm
Notes:   Feedback: Part about different sch. algos. was a little too detailed. Maybe simplify this.

## Slide 10: Why is programmable scheduling hard?
Many algorithms, yet no consensus on primitives
Tight timing requirements: can’t punt to an FPGA/CPU
Need expressive primitive that can run at high speed
Notes:   So, why has prog. sched eluded us? It’s because despite having many scheduling algorithms, we have no consensus on the right abstraction for scheduling.
  Why is this important? Every other aspect of a switch that is programmable has an abstraction for it. For instance, parse graphs capture varied protocol formats. Match-action tables capture many forwarding policies. Packet transactions express many stateful algorithms.
  To compound things, the scheduler has tight timing requirements: typically, one enqueue or dequeue every clock cycle. So, you can’t punt on the problem by putting an FPGA or CPU in the fast path.
  In summary, we need an expressive abstraction that runs at line rate.

## Slide 11: What does the scheduler do?
It decides
In what order are packets sent
  e.g., first-in first-out, priorities, weighted fair queueing
At what time are packets sent
  e.g., rate limits
Notes: To motivate an abstraction, let’s first look at what the scheduler does. It decides on two things. First, the order in which packets are transmitted. This captures work-conserving schedulers like priority scheduling, weighted fair queueing, etc. Second, the absolute time at which packets are transmitted; the canonical example being token bucket rate limiting.
So a programmable scheduler will have to provide a way to flexibly specify both order and time.
TODO: Maybe get rid of the terms work-conserving and non-work-conserving. Think about it.

## Slide 12: Schedulers in routers today
Classification
Packets
Fixed schedulers
(priority, DRR,
rate limits, etc.)
Notes: Here’s a strawman prog. scheduler, which is how you would program a scheduler if you took an existing fixed function scheduler and tried to make that programmable.
Packets come in, they are classified into one of a fixed set of FIFOs, one for each flow. Then, on the dequeue side, some programmable logic picks the next flow to transmit whenever the link is idle. The programmable logic decides both the order in which flows are scheduled, and the absolute times at which flows are scheduled.
The problem with this strawman is that there is very little time on the dequeue side, which greatly limits the programmability it offers. At rates of 100G and beyond, the scheduler supports back-to-back dequeues every few clock cycles. So, the programmable logic must complete within a few clocks to support the next dequeue to the same scheduler.
Instead, can we move programmability to the enqueue side, where each packet has potentially much more processing time available before it is enqueued into the scheduler.

## Slide 13: A strawman programmable scheduler
Very little budget between consecutive dequeues (< 5 cycles @ 100G)
Budget already expended on reading queue head, dequeueing, updating state
Any extra computation will increase the inter-dequeue time => link will idle
Precompute this extra computation and move it off the critical path?
Classification
Programmable dequeue()
function
Packets
Notes: Here’s a strawman prog. scheduler, which is how you would program a scheduler if you took an existing fixed function scheduler and tried to make that programmable.
Packets come in, they are classified into one of a fixed set of FIFOs, one for each flow. Then, on the dequeue side, some programmable logic picks the next flow to transmit whenever the link is idle. The programmable logic decides both the order in which flows are scheduled, and the absolute times at which flows are scheduled.
The problem with this strawman is that there is very little time on the dequeue side, which greatly limits the programmability it offers. At rates of 100G and beyond, the scheduler supports back-to-back dequeues every few clock cycles. So, the programmable logic must complete within a few clocks to support the next dequeue to the same scheduler.
Instead, can we move programmability to the enqueue side, where each packet has potentially much more processing time available before it is enqueued into the scheduler.

## Slide 14: The Push-In First-Out Queue
Key observation
In many schedulers, relative order of buffered packets does not change
i.e., a packet’s place in the scheduling order is known at enqueue
The Push-In First-Out Queue (PIFO): Packets are pushed into an arbitrary location based on a rank, and dequeued from the head
2
5
9
7
9
10
13
8
Notes:   Feedback: Maybe place the figure up top in the slide so that you can describe the key observation in relation to the figure.
  TODO: Replace rank with urgency maybe?
  Let’s see how we do this. The key observation is that in many practical schedulers, the relative order of packets that are already buffered doesn’t change with future packet arrivals. Put differently, if a packet comes in, its location in the scheduling order can be determined before it is enqueued. The packet can then by pushed into this location, secure in the knowledge that we don’t have to change the relative order of packets that are already buffered.
  Now, some schedulers that confirm to this property are strict priority scheduling, where the location is determined by a packet’s priority, and FCFS, where the location is determined by arrival time.
  A natural primitive for this is a push-in first-out queue (or PIFO) where packets are pushed into an arbitrary location based on rank (which could be either scheduling order or time), but always dequeued from the head. As an illustration, if packet with rank 8 arrived to this PIFO, it would be pushed between 7 and 9.

## Slide 15: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
…
...
p.rank= T[f] + p.len
Notes: Now, how do we build a programmable scheduler based on a PIFO? To program the scheduler, we program the packet’s rank computation before enqueueing it into a PIFO because that’s the only programmable part.
How do we program the rank computation? Quite literally, by writing out a program for it. Here’s a made-up program, which computes a packet’s rank using a table T for each flow and the packet’s length.
This is the key modularity in the design. It separates out the fixed logic, which is the task of enforcing ranks, from the programmable logic, which is the task of computing ranks. Also, because the programmability is on the enqueue side, you have much more time to compute ranks for each packet. You can potentially compute a packet’s rank anywhere along the packet’s path from the packet’s host to this switch. We’ll see how this lets us express a variety of schedulers.
Ok, so where do the programmable and fixed parts go in a real router?

## Slide 16
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
A programmable scheduler
Rank Computation
…
…
…
…
Notes: For this, let’s bring up the switch pipeline again. The PIFOs replace the queues in the scheduler, while the rank computation runs in the ingress pipeline.
How do we run the rank computation? We’ll deal with that in the second half of the talk.
Note to self: Mention the term precomputation of rank here.

## Slide 17
Out
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Fair queuing
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len
p.rank = p.start
Rank Computation
Notes: Now let’s see some real algorithms programmed with a PIFO.
The first is fair queueing, a work-conserving scheduler. Let’s pick the virtual start-time fair queueing implementation.
Here, for each packet we compute its virtual start time in an idealized fluid fair scheduler. We do this by setting the packet’s start time to the maximum of the finish time of the last packet in the packet’s flow and the current virtual time. Then, we update the flow’s finish time appropriately.
We then schedule packets in order of their virtual start times, which becomes a packet’s rank in the PIFO.

## Slide 18
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Token bucket shaping
tokens = min(
tokens + rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
tokens = tokens - p.len
last = now
p.rank = p.send
Rank Computation
Notes: Next, let’s look at the canonical non-work-conserving algorithm: token bucket shaping.
The rank computation here is a little more involved. It has three parts.
First, we update the tokens using a standard token bucket that increments at some rate and is capped at some burst size. We also decrement tokens to account for packet transmissions.
Second, for an incoming packet, we set its wall-clock departure time to either the current time or some time in the future when it would have made up the shortfall of tokens.
Third, this departure time becomes the packet’s rank in a PIFO.

## Slide 19: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Notes: Ok, so we have looked at two algorithms where the rank computation runs on the switch. The rank computation can, in fact, run anywhere in the network. For instance, let’s compress this pipeline down to a switch. Let’s also introduce an end host.

## Slide 20: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Rank Computation
f = flow(p)
p.rank = f.rem_size
Notes: We can use this end host to compute the ranks for the shortest remaining flow size scheduler. Here, the end host tracks TCP acks and uses this to set the remaining flow size for each packet in a flow.

## Slide 21: Beyond a single PIFO
x
1
y
1
x
2
b1
b2
b3
y
2
a1
Hierarchical scheduling algorithms need hierarchy of PIFOs
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
Notes: Ok, so we have seen examples of what a single PIFO can do. Common to these examples is the property that the relative order of buffered packets doesn’t change with future arrivals.
There are algorithms that violate this property, such as hierarchical schedulers. I’ll illustrate this through hierarchical packet-fair queueing. Here, the idea is to divide capacity between two classes, Left and Right, in some ratio. Then, we recursively divide capacity between flows within each class, such as a, b and c, d.
So, let’s see why HPFQ cannot be served by a single PIFO. Let’s say this is the current state of the system, with packets departing from the head. Now, when the first packet from flow a arrives, we need to satisfy two constraints simultaneously. One, classes red and blue must alternate because they share capacity equally. Two, within class red, a must be ahead of b, because it has a much higher weight.
To do this, we need to move the packets from b to new locations so that red and blue alternate. Then, we need to move a1 ahead of all packets of b because a has a much higher weight. This combination of moves from a and b is beyond a single PIFO that cannot change the relative order of packets that are already buffered.
But, it turns out we can do this with a hierarchy of PIFOs.

## Slide 22: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
PIFO-Red
(WFQ on a & b)
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
B
R
B
B
R
R
B
R
Notes: This hierarchy of PIFOs is very natural and has a structure similar to the scheduler. The root PIFO arbitrates between two child PIFOs red and blue, while each child PIFO arbitrates between packets.
So, now, let’s see what happens on enq and deq. When a1 shows up, its class R is enqueued into PIFO root, while a1 is enqueued into the red PIFO. On the deq side, let’s say we dequeued now. Then, we pop B out of PIFO root, see that it points to the blue PIFO out, pop x1 out of the blue PIFO, and transmit x1.
So, by recursively dequeuing PIFOs starting from the root, we can transmit successive packets.

## Slide 23: PIFO in hardware
Performance targets for a shared-memory router
  1 GHz pipeline (64 ports * 10 Gbit/s)
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
  Scheduler is shared across ports
Naive solution: flat, sorted array is infeasible
Exploit observation that ranks increase within a flow
Notes: Feedback: maybe remove this.
Ok, let’s see if a PIFO is actually feasible.
To answer this, we set out to meet some performance targets typical of a shared-memory switch like the Trident found in many dcs today. Here are some typical nos: a pipeline with a 1 GHz clock rate, 1K flows and 60K packets.
One important note is that the scheduler (and so PIFO hardware as well) is shared across all ports. So we don’t need separate PIFO hardware for each port, which means we don’t have to multiply the area overhead by the number of ports.
So, how do we do this? A naïve solution is one large array with 60K elements. An incoming element is compared in parallel to all 60K elements and shifted into the right location. With 60K parallel comparators, this is a non-starter.
Instead, we exploit the fact that most schedulers schedule across flows, with the implicit assumption that packet ranks increase within a flow. How do we use this?

## Slide 24: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
7 mm2 area in a 16-nm library for a
5-level programmable scheduler (4% overhead)
Notes: Our design has two parts.
A flow scheduler schedules across the head packets of all flows, while a rank store stores packets ranks in a first-in first-out queue for each flow.
The flow scheduler is really a PIFO over the head packets alone.
When an element (say) C6, from flow C with rank 6, is enq, it’s just appended to the back of the rank store. When D4 shows up, it bypasses the rank store and directly goes to the flow scheduler. When we deq, we just pop the head of the flow scheduler array to get A0, then reach into the rank store, pull out A2 and insert it into the flow scheduler array.
If you notice, the flow scheduler has to insert an element like A2 into a sorted array, which we do by comparing it in parallel to all elements in the array. Except now, we can actually do this because the sorted array has only 1K head packets, not all 60K packets.
This block supports up to 1 enq + 1 deq every clock cycle, which is a ns in a typical scheduler. It can also be sliced up across many logical PIFOs, which are PIFOs that are independent of each other, but share the same underlying hardware impl. An example is PIFOs for different output ports, whose schedulers run independently.

## Slide 25: What algorithms do PIFOs enable?
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
pFabric
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 26: What algorithms do PIFOs enable?
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
pFabric
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 27: This Talk
  PIFO (SSACCABEKM SIGCOMM ‘16): programming the scheduler
    A primitive to program many existing and new scheduling algorithms
    Modest chip area cost when implemented in high-speed hardware
  Domino (SCBKABVML SIGCOMM ‘16): programming streaming algorithms
    Inexpensive hardware primitives for high-speed execution of streaming algorithms
    A method to extract these primitives from a corpus of algorithms
My work

## Slide 28: Packet Transactions: High-Level Programming for Line-Rate Switches (SIGCOMM 2016)
Anirudh Sivaraman, Alvin Cheung, Mihai Budiu,
Changhoon Kim, Mohammad Alizadeh, Hari Balakrishnan,
George Varghese, Nick McKeown, Steve Licking
Joint work with collaborators at MIT, University of Washington,
Barefoot Networks, Microsoft Research, and Stanford University

## Slide 29: An example streaming algorithm
E.g., sample every 10th packet:
Routers handle 1 packet/cycle regardless of
what features are enabled
But, the algorithm takes >1 cycles/packet
How do we bridge this gap?
  Atoms: a hardware primitive for packet header and state modification
  A method to extract atoms from algorithms
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++

## Slide 30: A shared-memory x86 multicore
Shared Memory
Shared memory => contention => non-determinism
Routers expected to have deterministic performance
Packet
Notes: Naïve shared memory either causes inconsistency (stale read) or non-determinism (bypass, followed by pipeline blocking). Can’t have both.
Secondary point: caching cause non-determinism.

## Slide 31: A shared-nothing x86 pipeline
Hard to balance the pipeline to get 1 packet / cycle
Constrain stages in hardware to get 1 packet / cycle
Local
Memory
Local
Memory
Local
Memory
Local
Memory
Packet
Notes: Make the architecture bulletproof so that it handles 1 packet every clock cycle.
First, Slice algorithm into different pipeline stages.
Now the minute you have a pipeline, you want to balance it so that each stage does the same amount of useful work per packet.
If not, your throughput is gated by the slowest stage.
Now, it’s hard to balance the pipeline so that each stage takes exactly 1 cycle per packet regardless of program.
First, it’s hard to even guarantee that each stage executes the same number of instructions for each incoming packet.
Even if it did, because x86 optimizes for the average case and not the worst case, instructions take a differing number of clocks per instruction.
All in all, it’s hard to get 1 packet / cycle.
TODO: Need to work on this.

## Slide 32: A shared-nothing atom pipeline
Atom: local memory + action unit
Atom hardware must support
one packet / cycle
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
action unit
X
constant
Add
Mul
2-to-1 Mux
X
choice
Packet
Notes: Say very clearly that this atom is really JUST an example.

## Slide 33: Extracting atoms from algorithms
Pipeline stages
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0
:(pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1
Input: Algorithms as
packet transactions
Compiler
for
Pipelining
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Look for
reusable
atoms
across algorithms
Output: Atoms
Notes: Given some algorithms, can we figure out what atoms we need?
Say that the algorithm can’t have loops right here and introduce the transaction programming model briefly.
Say that we are going over the process for a single algorithm first.
Maybe use the term codelet here?

## Slide 34: Code pipelining: stateless vs. stateful
pkt.tmp =
pkt.f1 + pkt.f2
  Stateless operation: pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
pkt.f4 =
pkt.tmp - pkt.f3
f1
f2
f3
f4 =
tmp – f3
tmp = f1 + f2
f1
f2
f3
f4
tmp = f1 + f2
f1
f2
f3
f4
tmp
Easy to pipeline stateless operations
Notes: Mention compiler’s goal: extracting atomic stages
Now, let me dive a bit deeper into these atoms to show how the design process is different for atoms that do and do not modify persistent switch state. Let’s do this with some examples.
First, let’s look at the stateless op, f4 = f1 + f2 – f3., click
Now, let’s see what atoms for this operation look like. We can create two atoms in two different pipeline stages. Click,
The first adds f1 and f2 and writes it to tmp. Click,
The second subtracts f3 from tmp.
In general, you can do this for more involved stateless operations by breaking it down into a sequence of pair-wise operations on packet fields.
So, as a switch designer, you can design stateless atoms that perform arithmetic on pairs of packet fields and many stateless operations can be composed out of these simpler pair-wise instructions, by the compiler.

## Slide 35: Code pipelining: stateless vs. stateful
  Stateful operation: x = g(x)
p.tmp = x
p.t1=
s1(p.tmp)
x = p.tn
X
Cannot pipeline: need atom for x = g(x)
p.tn =
sn(p.t_{n-1})
But, X is shared
N stages

## Slide 36: Code pipelining: the algorithm
Create one node for each instruction
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: The code has been simplified (into 3-opcode form) so that they are as close as possible to the hardware.

## Slide 37: Code pipelining: the algorithm
Packet field dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Read/After/Write dependencies

## Slide 38: Code pipelining: the algorithm
State dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 39: Code pipelining: the algorithm
Strongly connected components
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: One slide with animation showing the problem, then bring in analogy to VLIW, and then solution.
TODO: Mention Monica Lam’s VLIW work and time/space duality.

## Slide 40: Code pipelining: the algorithm
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new
Contract SCCs to form DAG
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 41: Code pipelining: the algorithm
After Depth-First Search
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1

## Slide 42: Detecting reusable atoms
pkt.x = pkt.a + pkt.b
pkt.x = pkt.a - pkt.b
pkt.c = pkt.a (BINOP) pkt.b
pkt.sample = pkt.tmp ?
pkt.src : 0
pkt.a = pkt.predicate ?
mux(pkt.b, C)
: mux(pkt.c, C)
Notes: Looked at a large class of algorithms and extracted a library of atoms.
This is how we did it. Here are two examples.
Make sure by this point it is clear why a simple instruction set like x86 is not enough.

## Slide 43: A catalog of reusable atoms
Atoms | Description | Examples
Stateless | All binary operations on a pair of packet fields | TTL decrement, setting header fields, etc.
Read/Write | Read or write a variable | Bloom filters, indicator variables
Accumulator | Increment state by value (packet field or constant) | Counters, sketches, heavy hitters
Conditional Accumulator | Accumulate differently based on one predicate | Rate Control Protocol, Flowlet switching, sampling
Nested Conditional Accumulator | Accumulate differently based on two predicates | HULL, AVQ, Rank Computation for Start-Time Fair Queueing
Pairs | Update a pair of mutually dependent state variables | CONGA
Notes: State up front that the list of atoms is somewhat arbitrary for now.
Maybe even show the circuit for some of these atoms.
You can’t break up the operation into multiple stages.

## Slide 44: A catalog of reusable atoms
Atoms | Description | Examples | Atom area in squared micron | Additional area for 100 atoms
Stateless | All binary operations on a pair of packet fields | TTL decrement, setting header fields, etc. | 1384 | 0.07%
Read/Write | Read or write a variable | Bloom filters, indicator variables | 250 | 0.0125%
Accumulator | Increment state by value (packet field or constant) | Counters, sketches, heavy hitters | 431 | 0.022%
Conditional Accumulator | Accumulate differently based on one predicate | Rate Control Protocol, Flowlet switching, sampling | 985 | 0.049%
Nested Conditional Accumulator | Accumulate differently based on two predicates | HULL, AVQ, Rank Computation for Start-Time Fair Queueing | 3597 | 0.18%
Pairs | Update a pair of mutually dependent state variables | CONGA | 5997 | 0.30%
<1 % additional chip area for 100 atom instances

## Slide 45: What algorithms do atoms enable?
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
pFabric
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 46: What algorithms do atoms enable?
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
pFabric
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 47: Conclusion
High-performance networking needs specialized hardware
Tension between specialization and programmability
Tailor primitives to restricted classes of router functionality
Broader impact:
  Packet transactions in P4
  Industry interest in PIFOs, Domino’s compilation techniques
Restricted programmability will be relevant to other domains as well
Notes:   Streaming algorithms: Atom
  Scheduling: PIFOs
End of Moore’s law means specialization.
Specialization is at odds with programmability.
My approach is to tailor abstractions to very specific classes of switch functionality. The specificity lets you retain high performance, while having a class of algorithms means that it’s somewhat future proof.

## Slide 48: Acknowledgements
MIT: Suvinay Subramanian, Hari Balakrishnan, Mohammad Alizadeh
Barefoot Networks: Changhoon Kim, Anurag Agrawal, Steve Licking, Mihai Budiu
Cisco Systems: Shang-Tse Chuang, Sharad Chole, Tom Edsall
Microsoft Research: George Varghese
Stanford University: Sachin Katti, Nick McKeown
University of Washington: Alvin Cheung
Notes: I would like to thank an outstanding set of collaborators from
MIT, Barefoot Networks, Cisco Systems, Microsoft Research, Stanford, and University of Washington.

## Slide 49: Recent activity in the area
2008--2013: OpenFlow: Specify router-to-router connectivity
2013--now: Programmable router chips (Barefoot’s Tofino, Intel’s FlexPipe, Cavium’s Xpliant), programming languages (P4)
Router chip programmability is still nascent
  Goal: feature parity with legacy routers without baking in features
  Basic header manipulation; recognize new protocol formats

## Slide 50: Code pipelining in one slide
Goal: if each stage runs atomically, transaction must run atomically
Easy without state: only intra-packet dependencies
  Perform depth-first search on DAG of intra-packet dependencies
  All nodes at the same depth belong to the same pipeline stage
State causes inter-packet dependencies
  Cycles in dep. graph: state read must follow write from previous packet.
  Find strongly connected components; contract SCCs to single nodes
  Depth-first search on resulting DAG

## Slide 51: Future work: An era of specialized systems
With Moore’s law ending, hardware specialization is a necessity
  Video encoding, graphics, machine learning, bitcoin mining, …
Recurring tension between programmability and specialization
  Simple question: How do we design a cluster of processors and accelerators for (machine learning / video encoding / …)?
  Requires synthesizing ideas from languages, compilers, hardware, and networking
Notes: TODO: Check if this is necessary.
If we were completely untethered.
    What’s in the accelerators?
    What’s the storage medium?
    What’s the right programming model?
    What’s the right congestion-control protocol?

## Slide 52: Backup slides
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0
: (pkt.old + 1);
count = pkt.new;
pkt.old = count;
count = pkt.old + 1;
state = mux(state RELOP C, true) ?
mux(state + p.a, 0)
: mux(state + p.c, 0)

## Slide 53: Early routers
Early routers were eminently programmable minicomputers
  IMPs (1969): Honeywell DDP-516 950 Kbit/s (The IMP paper)
  MIT C gateway (1980-1982): 500 Kbit/s on M68K (Lixia Zhang’s paper)
  Fuzzballs (1971-1991): Most known for use on the NSFNET Phase-1 Backbone Network (1986-88): DEC PDP-11/73: 400 Kbit/s (Mill’s paper from SIGCOMM 88)
  Stanford multiprotocol router (1981): DEC PDP 11 / Motorola 68000
  Proteon (1985): 80 Mbit/s (http://www.historyofcomputercommunications.info/Book/12/12.22_Proteon.html#_ftn3)

## Slide 54: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow
Cannot express some scheduling algorithms, e.g., output shaping.
Notes: So it turns out that we can use a tree of PIFOs for many more algorithms. I am not discussing these here, but the paper has further details.
More importantly, we have algorithms that our abstraction doesn’t support. One important class is output shaping, where we rate limit dequeues from the scheduler. We can’t implement this because PIFOs provide prog. on the enq side, not on the deq side. Again, the paper discusses this in depth.

## Slide 55: FAQ
How is this different from P4?
  When we started this work a year ago, P4 was much closer to the hardware. Over time, it’s gotten more high-level, thanks in some part to this work (sequential semantics, ternary operators).
  We do have a P4 backend.
Why a pipeline?
  NPUs have a shared-memory architecture, but sharing memory is hard and slows down the switch.

## Slide 56: FAQ
What’s in the compiler?
  Strongly Connected Components to extract atomic portions.
  Code generation using program synthesis.
Do the atoms generalize in an ML sense?
  We don’t know for sure. We designed the atoms and were able to tweak them a little bit to serve more algorithms. But this is something we don’t yet have a handle on.

## Slide 57: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 58: Relationship to prior compiler techniques
Technique | Prior work | Differences
If Conversion | Kennedy et al. 1983 | No breaks, continue, gotos, loops
Static Single-Assignment | Ferrante et al. 1988 | No branches
Strongly Connected Components | Lam et al. 1989 (Software Pipelining) | Scheduling in space instead of time
Synthesis for instruction mapping | Technology mapping | Map to 1 hardware primitive, not multiple
 | Superoptimization | Counter-example-guided, not brute force

## Slide 59: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 60: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we convert to static single assignment form, which simplifies dependency analysis.
Static single assignment gets its name from the fact that all variables are assigned
Exactly once and no more.
It’s useful because it gets rid of write-after-read and write-after-write dependencies. In our case,
converting to SSA is trivial because we operate on straight-line code with no branches. Typical
SSA implementations are far more involved because they have to deal with branching.

## Slide 61: Expression Flattening
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
pkt.tmp = pkt.arrival - last_time[pkt.id];
pkt.tmp2 = pkt.tmp > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp2
? pkt . new_hop
: saved_hop [ pkt . id ];
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: The last step in canonicalization is to flatten arbitrarily complicated expressions
to bring them into a form closer to the underlying hardware.
(Quickly skim over this.)

## Slide 62: Instruction mapping: results
Generic method to handle fairly complex templates
Templates determine if a Domino program can run at line rate.
Example results:
  Flowlet switching needs conditional execution to save next hop information:
  saved_hop[pkt.id] = pkt.tmp2 ? pkt.new_hop : saved_hop[pkt.id]
  Simple increment suffices for heavy-hitter detection
  count_min_sketch[hash] = count_min_sketch[hash] + 1
Sequential to parallel code
Hardware constraints
Canonicalization

## Slide 63: Generating P4 code
Required changes to P4
  Sequential execution semantics (required for read from, modify, and write back to state)
  Expression support
  Both available in v1.1
Encapsulate every codelet in a table’s default action
Chain together tables as P4 control program
Notes: Say that this project led to sequential execution semantics.

## Slide 64: Branch Removal
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I ‘ll go through these steps quickly. The first step in canonicalization is to remove branching statements.
Branches complicate control flow and make it harder to infer dependencies.
We eliminate branches using a procedure called if conversion that transforms them into C’s conditional operator.
because the only kind of branch we have is an if statement, if conversion is very straightforward in our case, because
we don’t have any kind of unstructured control flow such as a goto, break, or continue, that significantly complicate
if conversion.
This makes the code flow straight from one statement to the next without exception and makes it very easy to infer
dependencies as well: everything on the right of a “equals” is read and the one statement on the left is written.

## Slide 65: Handling State Variables
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we identify state variables, because they complicate the pipelining procedure.
In the absence of state variables, once you have straight-line code, you only need to
consider how you would pipeline the code for a single packet’s processing and you are
done because all other packets follow the same pipeline and there is no interaction
between packets. With state variables, you need to consider interactions between packets.
To simplify our analysis of state variables and dependencies between packets, we explicitly
limit the ways in which state variables can be accessed. We allow only reads and writes to
state and all other arithmetic happens on packet variables. This also lets us reuse an old
value of a state variable down the pipeline if required.

## Slide 66: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 67: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.

## Slide 68: The Domino compiler
Branch Removal
Domino
Handle state variables
Code Pipelining
Instruction Mapping
Processing Pipeline
Canonicalization
(Sequential Code)
Sequential to
parallel code
Respecting hardware
constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 69: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Pair up read/write
flanks
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we pair up reads and writes to state variables to capture the notion
that state variables remain local to a specific stage in the pipeline. If not,
we would have to read from one stage and write from another requiring
us to route longer wires on the chip.

## Slide 70: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Condense strongly
connected components
into codelets
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we look for stongly connected components in this graph,
and condense them into what we call codelets. These capture the essence of
what operations need to be run atomically for the entire transaction to execute atomically.
Now that we have eliminated circles in the graph, we can schedule the resulting
acyclic graph. This is a straightforward process known as critical
path scheduling where we put each node in the earliest pipeline
stage following all its predecessors.

## Slide 71: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Add packet-field
dependencies
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we add read after write dependencies, where we draw an arrow from the
node that writes a value to the node which reads that value.
This is ALL we need to do to handle dependencies in our case because there are
no other waw or war dependencies after SSA.

## Slide 72: Programming with Packet Transactions
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
Pipeline
Domino
pkt.new_hop =
hash3(pkt.sport,
pkt.dport,
pkt.arrival)
%NUM_HOPS;
pkt.id =
hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: TODO: Per Ravi, Hongzi, consider switching to a simpler example like sampled netflow
To give you a flavor for programming using packet transactions, we look at programming
flowlet switching, a data-plane load-balancing algorithm.
To write imperative code for each packet transaction, we use a language
called Domino with a syntax resembling C. On the right, we contrast it against
writing code in P4.
So let me first describe flowlet switching. Its logic is shown here.
The idea in flowlet switching is to load balance groups of packets separated by
a long gap in time across different paths to carry out more fine-grained traffic
splitting relative to standard ECMP.
The logic in is straightforward. You start off by populating a new
hop variable in each packet using some dynamic quantity such as the packet’s arrival time.
Then, you check if the intepacket gap between this packet and its previous one is sufficiently
large and update a state variable called saved_hop if so.
Then, you simply update the last time and set the next hop to the saved hop (which is either
the new value or the old one).
Now, if you were to explain flowlet switching to someone else, like I just did, it’s natural to express its logic
as a block of imperative code and programming in packet transactions lets you do exactly that.
The logic itself becomes the body of a function. This function flowlet is a packet transaction, which conceptually
Executes atomically on each packet. The rest of the Domino program declares state variables as global
variables, packets as structures, and lets you use the rest of C including the macro preprocessor.
================================
So that’s how you express flowlet switching in Domino. When you compile this code it generates
a pipelined implementation in P4 as shown here. This is how you would program the switch today.
The rest of this talk will describe how its relatively straightforward to build a compiler that achieves
this transformation if you exploit characteristics of the underlying domain of line-rate switches.

## Slide 73: The quest for programmability
Switch | Year | Line-rate
Cisco Catalyst | 1999 | 32 Gbit/s
Broadcom 5670 | 2004 | 80 Gbit/s
Broadcom Scorpion | 2007 | 240 Gbit/s
Broadcom Trident | 2010 | 640 Gbit/s
Broadcom Tomahawk | 2014 | 3.2 Tbit/s
Programmability => 10--100x slower than line rate.
System | Year | Substrate | Performance
Click | 2000 | CPUs | 170 Mbit/s
Intel IXP 2400 | 2002 | NPUs | 4 Gbit/s
RouteBricks | 2009 | Multi-core | 35 Gbit/s
PacketShader | 2010 | GPUs | 40 Gbit/s
NetFPGA SUME | 2014 | FPGA | 100 Gbit/s
Notes: Cisco Catalyst: http://www.cisco.com/c/dam/en/us/products/collateral/switches/catalyst-6807-xl-switch/white_paper_c11-728264.doc/_jcr_content/renditions/white_paper_c11-728264_1.jpg
Intel IXP 2400: http://www.intel.com/design/network/papers/ixp2400.pdf: 4 Gbit/s (copyright 2002)
Broadcom 5670 (2004): 80 Gbit/s (8 ports of 10 G) (https://www.broadcom.com/collateral/pb/5670-PB05-R.pdf, 2004)
Broadcom Scorpion (2007) (24 * 10 G from DCTCP paper, and http://www.enterprisetech.com/2014/09/24/broadcom-fights-ethernet-rivals-tomahawk-chips/ suggests 2007)
Trident (2010): 64 * 10 G = 640 G
Trident II (2012): 100 * 10 G = 1 Tbit/s
BCM Tomahawk (2014): 3.2 Tbit/s
Trident and Tomhawk numbers taken from the pages below.
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
TODO: Turn this into a graph.

## Slide 74: The quest for programmability
Programmability => 10--100x slower than line rate.
Chart: Performance scaling of switches
| 2000.0 | 2002.0 | 2009.0 | 2010.0 | 2014.0
Software routers | 0.17 | 4 | 35 | 40 | 100
Line-rate routers | 32 | 80 | 240 | 640 | 3200
Notes: People have recognized this need at least since the late 90s and quite a few software switch platforms have been developed where you take an existing programming substrate and repurpose it for networking.
Now, here’s a line graph showing how the performance of these software switches has scaled with time, and we can see that it’s improved about 1000 fold since 2000, which is quite impressive.
But, at the same time, if you look at the highest end switches (or what I call line-rate switches, because they run at the highest speed that the cable or line can support), they have always been between 10 and 100 times faster than these software platforms. That’s because they have been specialized from the ground up to support just routing. As a result, these programmable platforms never really gained much adoption because they were always slower than the fastest switches.
So, the takeaway, historically is that programmability has cost us 10—100x in performance. And my research looks at designing programmable switch platforms without any performance penalty.

## Slide 75: Compiler targets: diagram
Operation:
+, -, >, <,
AND, OR
pkt.f1/
constant
pkt.f2/
constant
pkt.f3
pkt.f
constant
x
2-to-1
Mux
pkt.f
constant
x
2-to-1
Mux
x
0
2-to-1
Mux
Adder

## Slide 76: Why are switches pipelined?

## Slide 77: Performance requirements at line rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
10 operations per packet: routing, access control (ACL), tunnels, …
Need to process 1 billion pkts/s, 10 ops per packet
Notes: Important segue way here: Let’s talk about why a pipeline is the right hardware architecture for a switch by arguing for it from first principles.

## Slide 78: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
10 GHz processor
Packets
match/action
Can’t build a 10 GHz processor!

## Slide 79: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action

## Slide 80: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action
match/action
match/action
match/action
Memory replication increases die area

## Slide 81: Function-parallel or pipelined architecture
Route lookup table
1 GHz circuit
ACL lookup table
Tunnel lookup table
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
match/action
match/action
match/action
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 82: P4 comparison

## Slide 83: Programming with packet transactions
Algorithm | LOC | P4 LOC
Bloom filter | 29 | 104
Heavy hitter detection | 35 | 192
Rate-Control Protocol | 23 | 75
Flowlet switching | 37 | 107
Sampled NetFlow | 18 | 70
HULL | 26 | 95
Adaptive Virtual Queue | 36 | 147
CONGA | 32 | 89
CoDel | 57 | 271
Notes: Ok, so now that I have shown you how to design these atoms, let’s look at what you can do with them. For this, we need some algorithms, and we picked a set spanning congestion control, measurement, load balancing, and AQM, and wrote them in Domino.
Their lines of code are listed here and they aren’t very different from the number of LOC you would have to write when programming a software switch with these algorithms. So that’s some measure of the abstraction being easy to use.