## Slide 1: Programmable Packet Scheduling at Line Rate
Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh, Sharad Chole, Shang-Tse Chuang, Anurag Agrawal, Hari Balakrishnan, Tom Edsall, Sachin Katti, Nick McKeown

## Slide 2: Programmable scheduling at line rate
Motivation: Can’t deploy new schedulers in production networks
The status quo in line-rate switches
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
2
Queues/
Scheduler
RMT
RMT, Domino
RMT
RMT, Domino
???
The scheduler is still fixed
Notes:   Hari: Make the scheduler bigger in this talk.

## Slide 3: Why is programmable scheduling hard?
Many algorithms, yet no consensus on abstractions, cf.
  Parse graphs for parsing
  Match-action tables for forwarding
  Packet transactions for data-plane algorithms
Tight timing requirements
  Scheduler manipulates state every clock cycle
  One decision per clock cycle is typical
Need expressive abstraction that can run at line rate
Notes:   Amy: Tight timing constraints is a red herring because other switch functions also suffer from it.
  Amy: Emphasize that this is MYYYY abstraction.
  So, it should make you wonder. Why is programmable scheduling hard?
  After all, new scheduling algorithms spring up every year.
  The problem is that, despite many years of work on programmable scheduling and hundreds of algorithms, there is
  no consensus on an abstraction to use for ALL scheduling algorithms.
  This is in contrast to other aspects of the switch such as parsing, for which parse graphs are a good abstraction
  and forwarding, for which match-action tables are a good abstraction.
  Because there is no abstraction, one approach is to throw up your hand and build an FPGA or CPU on the critical path.
  But this also isn’t feasible for line rate switches because you need to make decisions within a few clock cycles.
  So we are really looking for an abstraction that is simple enough that it can finish executing within a few clock cycles.
  Packet transactions are insufficient. On the surface of it, scheduling operates on groups of packets
  or queues. Packet transactions on the other hand, operate one packet at a time.

## Slide 4: What does the scheduler do?
It decides
In what order are packets sent
  e.g., FCFS, priorities, weighted fair queueing
At what time are packets sent
  e.g., Token bucket shaping
Notes: A programmable scheduler needs to programmatically decide on these two attributes.

## Slide 5: A strawman programmable scheduler
Very little time on the dequeue side (new decision every cycle)
Limits flexibility in logic that determines order or time
Classification
Programmable logic to decide order or time

## Slide 6: The Push-In First-Out Queue
Key observation
In many cases, relative order of buffered packets does not change
i.e., a packet’s place in the scheduling order is known at enqueue
The Push-In First-Out Queue (PIFO): Packets are pushed into an arbitrary location based on a rank, and dequeued from the head
2
5
9
7
9
10
13
8
Notes:   Amy: The PIFO figure isn’t perfectly aligned. There is whitespace between some boxes and no whitespace between others.

## Slide 7: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
…
...
p.rank= T[f] + p.len
Notes: End by reminding them that the reason this works is that the rank can be computed before enqueue
Make it clear that you have an extended budget on the enqueue side.

## Slide 8
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Rank Computation
Queues/
Scheduler
Rank computation carried out by programmable switch pipeline
  Expressed either as a high-level packet transaction (Domino, SIGCOMM ‘16)
  or directly in a low-level language like P4
PIFO Scheduler
A programmable scheduler

## Slide 9
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Rank Computation
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len
p.rank = p.start
Fair queuing

## Slide 10
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
tokens = min(
tokens + rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
tokens = tokens - p.len
last = now
p.rank = p.send
Rank Computation
Token bucket shaping

## Slide 11: SRPT
2
9
8
5
PIFO Scheduler
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
PIFO Scheduler
Notes:   TODO: Fix alignment of this slide with the previous one.

## Slide 12: SRPT
Rank Computation
f = flow(p)
p.rank = f.rem_size
2
9
8
5
PIFO Scheduler

## Slide 13: Beyond a single PIFO
x
1
y
1
x
2
b1
b2
b3
y
2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical Packet Fair Queuing
Hierarchical scheduling algorithms need hierarchy of PIFOs
Notes: Practice narration here, too much waffling.
Mohammad: Explain the example more clearly.
Mohammad: Make sure colors are consistent.

## Slide 14: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical Packet Fair Queuing
PIFO-Red
(WFQ on a & b)
B
B
B
R
R
R
B
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
R
Notes: Similar alignment issues.
Letters aren’t aligned.
Mohammad: Show how the packet gets shipped out, i.e., differentiate packets from classes on dequeue.

## Slide 15: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow
Certain scheduling algorithms cannot be expressed.
Notes: Amy, NG: Add limitations of what you cannot express.
Mohammad: Add one bullet explaining limitations, go over the limitation very briefly.
TODO: Work on last bullet.

## Slide 16: Limitations of PIFOs
Output shaping: PIFOs rate limit input to a queue, not output
Shaping and scheduling are coupled.
Notes: Amy: Depending on whether we are speaking about hardware limitations as well, move this after the hardware part.
These limitations are a little hard to state succinctly. Maybe move them to the backup slides?

## Slide 17: PIFO in hardware
Performance targets for a shared-memory switch
  1 GHz pipeline
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
  PIFO hardware shared across ports
Naive solution: flat, sorted array is infeasible
Exploit observation that ranks increase within a flow

## Slide 18: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
1 enqueue + 1 dequeue per clock cycle
Can be shared among multiple logical PIFOs
Notes: Logical PIFOs can be supported by modifying the dequeuer logic a little bit.
Instead of dequeueing the head packet, we find the first packet for a particular logical PIFO (using an equality check + priority encoder), and then shift at that position.
Make sure to mention logical PIFOs here.
NG: Use of the term PIFO block is too recursive.
Amy: Say that the flow scheduler is implemented as an array of comparators, only now it’s feasible.
Logical pifos: (i.e., PIFOs for different ports or different levels of a hierarchy
Mohammad: Each block in the 5-level scheduler runs independently. You can run each block independently.
Emphasize that the blocks are decoupled. Each can run independently. You can instantiate multiple of these.
Because of how the hardware and hierarchical scheduler is designed and you do everything on enqueue, each can run independently.
Maybe bring in the tiling slide.

## Slide 19: PIFO mesh
Notes: Show a PIFO mesh, and then show how the hierarchical scheduler maps to the PIFO mesh.
Just lets people make the connect from a single PIFO block to multiple PIFO blocks (useful for hierarchies)
Always enq+deq only one per clock cycle.

## Slide 20: Hardware feasibility
The Rank store is just a bank of FIFOs (stable hardware IP)
Flow scheduler for 1K flows meets timing at 1GHz on 16-nm transistor library
  Continues to meet timing until 2048 flows, fails timing at 4096
  7 mm2 overhead for 5-level programmable hierarchical scheduler
  < 4% for a typical chip.
Notes: What determines clock rate and area overhead?
Maybe one or two slides on what affects what?
Make the 4% area overhead an example as opposed to the only design.
Add some scaling behavior.
Put the 2048, 4096 in context (5 tuples or aggregates?-)

## Slide 21: Related work
  PIFO: Used in theoretical work by Chuang et. al. in the 90s
Universal Packet Scheduling (UPS)
  Single algorithm (LSTF) to replay all schedules, end point sets slack
  Assumes fixed switches => cannot express fair queueing, shaping
  Assumes single priority queue => cannot express hierarchies
Hardware designs for priority queues
  Based on a binary heap, scales to large number of entries
  Needs a single heap for each port => hardware can’t be shared
Notes: Amy: don’t say: “Before you wrap up, …” It sounds like a chore.

## Slide 22: Conclusion
Programmable scheduling at line rate is within reach
Two benefits:
  Express new schedulers for different performance objectives
  Express existing schedulers as programs, not hardware
Code: http://web.mit.edu/pifo

## Slide 23: Backup slides

## Slide 24: Proposal: scheduling in P4
Currently not modeled at all, blackbox left to vendor
Only part of the switch that isn’t programmable
PIFOs present a candidate
Concurrent work on Universal Packet Scheduling also requires a priority queue that is identical to a PIFO

## Slide 25: Hardware implementation
Rank
== comparators
> comparators
Priority encoder
Priority encoder
Shift elements based on push, pop indices
Pop
(DEQ)
Push 1
(ENQ)
Push 2
(reinsert)
Logical
PIFO ID
Rank
Rank
Logical
PIFO ID
Rank
Logical
PIFO ID
Rank
Logical
PIFO ID
Meets timing (1 GHz) for up to 2048 flows at 16 nm
Less than 4% area overhead (~7 mm2) for 5-level scheduler

## Slide 26: A PIFO block
Enqueue:
(logical PIFO,
rank, flow)
Dequeue:
(logical PIFO)
ALU

## Slide 27: A PIFO mesh
Enq
Deq
Enq
ALU
Deq
Enq
ALU
Deq
Next-hop lookup
ALU
Next-hop lookup
Next-hop lookup

## Slide 28: Proposal: scheduling in P4
Need to model a PIFO (or priority queue) in P4
Requires an extern instance to model a PIFO
  Can start by including it in a target-specific library
  Later migrate to standard library if there’s sufficient interest
  Section 16 of P4v1.1
Transactions themselves can be compiled down to P4 code using the Domino DSL for stateful algorithms.

## Slide 29: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 30: Composing PIFOs: min. rate guarantees
Minimum rate guarantees:
Provide each flow a guaranteed
rate provided the sum of these
guarantees is below capacity.
PIFO-Root
Prioritize flows under
min. rate
PIFO-A
(FIFO for flow A)
PIFO-B
(FIFO for flow B)
1
3
2
4
2
A
B
A
B
A
Composing PIFOs
Notes: TODO: Flesh out this slide.
Stress that composed PIFOs can be used for more than just hierarchical scheduling.
Slightly better figure maybe?

## Slide 31: Traffic Shaping
1. update tokens
2. p.send = now +
(p.len - tokens) / rate;
3. p.prio =p.send
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Notes: A natural question is whether a PIFO can handle non-work-conserving algorithms?
So, our third example looks at Traffic Shaping, the most common of these non-work-conserving algorithms,
whose goal is to limit a flow to a fixed absolute throughput regardless of its offered load and the offered load of other flows.
We can implement Traffic Shaping using PIFOs by computing a packet’s priority in the PIFO based on the wall-clock
departure time of the packet when it is enqueued and dequeuing a packet whenever its wall-clock time arrives.
A PIFO allows you to express anything where you can determine the transmission order when packets are enqueued.
In other words, anything where the relative order doesn’t change in the future.
There are algorithms for which these are not true. In particular, hierarchical scheduling algorithms are a class of algorithms
for which this is not true. Let’s consider one in particular.

## Slide 32: LSTF
Add transmission delay to slack
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Decrement wait time in queue from slack
Initialize slack
values
Notes: Add transmission time at the switch
Too many examples.

## Slide 33: The PIFO abstraction in one slide
PIFO: A sorted array that let us insert an entry (packet or PIFO pointer) into a PIFO based on a programmable priority
Entries are always dequeued from the head
If an entry is a packet, dequeue and transmit it
If an entry is a PIFO, dequeue it, and continue recursively
Notes: To summarize, let’s look at what the PIFO abstraction entails.