## Slide 1: Programmable Routers
Anirudh Sivaraman
Notes: I am Anirudh, a graduate student in EECS, working with Hari Balakrishnan. I am going to be talking about programmable routers, a topic of recent interest in the field of Computer Networks.

## Slide 2: What are routers?
Routers: the glue holding the Internet together
Fixed (simple) routers and programmable (smart) end points
Notes: First, what are routers.
Here’s a diagram of a network, say like the Internet, where you have computers (like your laptops, desktops, or phones) connected to other computers. There are some intermediate nodes that allow these computers to talk to one another, which are called routers.
These could be the Wi-Fi Access Point in the building, a cellular base station, or a small NetGear box connecting computers
In a lab.
In their simplest form, routers are the glue that holds the Internet together. And traditionally, the Internet has prided itself
On having fixed routers and smart end hosts. So the routers are fixed, cannot be changed and carry out the singular task of moving packets from one interface to another. All the intelligent diverse stuff (like Web browsing, watching videos, or running
a Web server happens on the end hosts: either your phone or a server somewhere).

## Slide 3: The need for a programmable router
Customize network to an operator’s needs
  Access control policies in an enterprise
  Share traffic unequally between users
  New protocol formats (IPv6)
Can we “program“ a router?
  E.g., download a code fragment and run it on a router (like a CPU today?)
Notes: But over time, people have felt the need for a programmable router, where the router is no longer fixed, but can be programmed to suit a network operator’s needs. I have listed a few examples of where this is useful. If you are a network admin within a company, you may not want some people to be able to access certain parts of the company. You may want to flexibly divide up bandwidth between users in a base station proportional to how much they pay, or you may just want to deploy a new format.
So, the question is can we program a router. And what I mean by programming a router is the same as what you would call programming a CPU or phone today. Very simply put, can I download a code fragment and run it on the router, just like you do with a computer today.

## Slide 4: The quest for programmability
Programmability => 10--100x slower than line rate.
Chart: Performance scaling of routers
| 2000 | 2002 | 2009 | 2010 | 2014
Software routers | 0.17 | 4 | 35 | 40 | 100
Line-rate routers | 32 | 80 | 240 | 640 | 3200
Notes: People have recognized this need at least since the late 90s and quite a few software router platforms have been developed where you take an existing programming substrate and repurpose it for networking.
Now, here’s a line graph showing how the performance of these software routers has scaled with time, and we can see that it’s improved about 1000 fold since 2000, which is quite impressive.
But, at the same time, if you look at the highest end routers (or what I call line-rate routers, because they run at the highest speed that the cable or line can support), they have always been between 10 and 100 times faster than these software platforms. That’s because they have been specialized from the ground up to support just routing. As a result, these programmable platforms never really gained much adoption because they were always slower than the fastest routers.
So, the takeaway, historically is that programmability has cost us 10—100x in performance. And my research looks at designing programmable router platforms without any performance penalty.

## Slide 5: The internals of a line-rate switch
Parser
Ingress Pipeline
Stage 1
Match
Scheduler
Deparser
Egress Pipeline
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Stage 1
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Eth
IP
TCP
Pipelines run at 1 GHz or more.
Notes: So, let me briefly go through how we do this.
Here’s a mock-up of the internals of one of these line-rate switches.
Packets are made up of bytes. We need a parser to put bytes into headers, like Ethernet, IP, and TCP.
The pipeline is where most of the packet processing happens (say to lookup a ports destination address and forward it to the right output port). It basically consists of a set of tables that match on specific bit patterns in the packet and carry out specific actions like forwarding the packet.
Once a packet’s output port is determined it is placed in a queue, where it is scheduled for transmission when the link is free. There’s an analogous egress pipeline, which then takes these headers and turns them back into bits on the wire.
Now, for the highest possible performance for a given chip area, these pipelines run at a clock frequency of about 1 GHz or more.

## Slide 6: Programmability at line rate
Atoms: small digital circuits that run at 1 GHz.
Atom
State
Body
Atom
State
Body
Atom
State
Body
Atom
State
Body
Atom
State
Body
Atom
State
Body
Packet
Packet
Packet
Stage 1
Stage 2
Notes: If we zoom into one of these pipelines, this is how it looks. There is a grid of atoms, arranged into an atom pipeline where packets flow from left to right. (Explain how packets flow).
These atoms are small digital circuits that make up the instruction set of the programmable router. They must finish processing their inputs within the clock period, which at 1 GHz is 1 ns so that they are ready to process the next packet.

## Slide 7: Research problems
Hardware for atoms that are both …
  fast enough to run at 1 GHz
  and support many new and existing switch features
User-friendly languages to program routers
Prototyping routers on FPGA platforms
We have UROP, SuperUROP, and MEng projects!
(Email me at anirudh@csail.mit.edu if you are interested.)
Notes: Having given that background, let me quickly outline some research problems in this space that may be of interest to some of you here.
First, can we design these atoms in hardware so that they are both fast enough to run at 1 GHz, and the operations they implement can support many switch features (after all, that’s the goal of making a switch programmable: to be able to support many existing and new switch algorithms).
At the same time, can we design user-friendly languages to program these routers? If we all had to program our desktops in assembly, we wouldn’t be too happy about it. Similarly, can we design a user-friendly language to program these routers?
And finally, because we are building these atoms as digital circuits, can we prototype them on an FPGA platform?
We have projects in all these areas and as a lab, we always have quite a few undergrads at any point in time. Send me an email if you are interested 