## Slide 1: Packet Transactions: Programming the Data Plane at Line Rate
Anirudh Sivaraman, Mihai Budiu, Alvin Cheung, Changhoon Kim, Steve Licking, George Varghese, Hari Balakrishnan, Mohammad Alizadeh, Nick McKeown
Notes: Thanks Nate. I am Anirudh and am going to be speaking about a system that enables programmable packet scheduling at line rate. This is joint work with people at MIT, Barefoot Networks, CISCO, and Stanford.

## Slide 2: Programming the data-plane at line rate
Programmable: Can we express a new data-plane algorithm?
Line-rate: Highest capacity supported by a communication standard
Notes: Maybe define data-plane algorithm formally here …
So, the talk’s title is programmable scheduling at line rate. Let’s break down each of those two parts.
When I say programmable, I mean the ability to run a new scheduling algorithm (possibly something that we don’t know of today) on a switch.
And by line rate, I mean switches that operate at the highest capacity supported by a communication standard. For Ethernet today, this is 10 Gigabits per second,
and will soon become 40 or 100 Gigabits / sec.
Now, the term line-rate should make it clear that we can’t use a software switch, Network Processor, or FPGA for the task. These platforms let you write arbitrary
scheduling algorithms, but they have typically been between 10 and 100 times slower than line-rate at any point in time.

## Slide 3: Programmability at line-rate
  OpenFlow: Match-Action interface, fixed fields, fixed actions
  P4, RMT, FlexPipe, Xpliant: Protocol-independent match-action pipeline.
Parser
Ingress Pipeline
Stage 1
Match
Scheduler
Deparser
Egress Pipeline
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Stage 1
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Eth
IP
TCP
Notes: Highlight Ingress Pipeline at the end of this slide.

## Slide 4: Isn’t P4 sufficient?
Match-action is perfect for forwarding
But, limiting for stateful algorithms
Example: RED:
On enqueue:
Calculate average queue size
if min < avg < max
calculate probability p
mark packet with probability p
else if avg > max:
mark packet
Notes:   So, it should make you wonder. Why is programmable scheduling hard?
  After all, new scheduling algorithms spring up every year.
  The problem is that, despite many years of work on programmable scheduling and hundreds of algorithms, there is
  no consensus on an abstraction to use for ALL scheduling algorithms.
  This is in contrast to other aspects of the switch such as parsing, for which parse graphs are a good abstraction
  and forwarding, for which match-action tables are a good abstraction.
  Because there is no abstraction, one approach is to throw up your hand and build an FPGA or CPU on the critical path.
  But this also isn’t feasible for line rate switches because you need to make decisions within a few clock cycles.
  So we are really looking for an abstraction that is simple enough that it can finish executing within a few clock cycles.

## Slide 5: Packet Transactions
Imperative code block in subset of C (domino) that is atomic and isolated from other such blocks
One packet transaction per pipeline
More familiar to NPU, Click programmers
Notes:   We take inspiration from models for programming software routers and NPUs.

## Slide 6: Programming with Packet Transactions
Domino
P4
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
%NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: Domino to P4 (represented as a table dependency graph)
Now, I ‘ll show you how to get there.

## Slide 7: Language constraints on domino
No loops (for, while, do while)
No unstructured control flow (goto, break, continue)
No pointers, heaps

## Slide 8: If Conversion
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Notes: If conversion: Replace branches with conditionals
Straight-line code that is easier to analyze

## Slide 9: Read and Write Flanks
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Notes: Read and write flanks: read state variables into temporaries that can now flow through the pipeline

## Slide 10: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Notes: Simplifies dependency analysis

## Slide 11: Critical Path Scheduling
Create one node for
each instruction.
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Notes: Animate this properly.

## Slide 12: Critical Path Scheduling
Add ReadAfterWrite
dependencies
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Notes: Animate this properly.

## Slide 13: Critical Path Scheduling
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Pair up read and write
flanks
Notes: Animate this properly.

## Slide 14: Critical Path Scheduling
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Condense Strongly
Connected Components
Notes: Animate this properly.

## Slide 15: Critical Path Scheduling
Schedule condensed
graph
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
%NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: Animate this properly.

## Slide 16: Generating P4 code
Required changes to P4
  Sequential execution semantics
  Expression support
  Both available in v1.1
Encapsulate every SCC in a default action
Need sequential execution for stateful components
Thanks to Antonin Bas for help with P4 code generation!
Notes: Say that this project led to sequential execution semantics.

## Slide 17: Checking feasibility at line rate
So far, haven’t constrained action bodies
Check if action bodies can be mapped to available hardware
If it can, declare that we can run it at line rate.
  x = x + 1 can be mapped to x = x + c
If we can’t, flag a compiler error E.g.
  x = (pkt.y) ? (x + 1) : x can’t be mapped to x = x + c;
Notes: Just say won’t have time to go into it here, but we do check if we can map action bodies to available hardware units.
This procedure is sound.
If yes, can run at line rate.
If not, reject code.

## Slide 18: Closing thoughts
Constructive proof that we could run a subset of C at line rate
More familiar abstraction for stateful algorithms (37 LOC for flowlet switching in domino vs 110 in P4)
Vehicle for higher-level abstractions in packet processing
Will be open sourcing code soon
Come check out the demo!