## Slide 1
Abstractions for programming line-rate switches
Programming: Can we implement a new data=plane algorithm?
  AQM
  Scheduling
  Congestion control
  Load balancing
Line rate: Highest speed supported by dedicated hardware
Programming switch data planes at line rate
The evolution of programmable switches
Programmable switching chips
Packet transactions: high-level data-plane programming
Programmable scheduling is hard
What does the scheduler do?
Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh, Alvin Cheung, Anurag Agrawal, Hari Balakrishnan, Mihai Budiu, Sharad Chole, Shang-Tse Chuang,
Tom Edsall, Sachin Katti, Changhoon Kim, Steve Licking, Nick McKeown, George Varghese
Chart: Year
| 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2014.0
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Hardware router | 32 | 80 | 240 | 640 | 3200
10—100X gap between
Hardware, and software routers
Same performance as fixed-function chips,
Some programmability
A machine model for line-rate switches
Atom | Description | Area overhead
R/W | Read or write state | 0.04%
RAW | Read, add, and write back | 0.07%
PRAW | Predicated version of RAW | 0.13%
IfElseRAW | 2 RAWs, one each when a predicate is true or false | 0.16%
Sub | IfElseRAW with a stateful subtraction capability | 0.24%
Nested | 4-way predication (nests 2 IfElseRAWs) | 0.58%
Pairs | Update a pair of state variables | 0.96%
Least
Expressive
Most
Expressive
Algorithm | LOC | Stages (max 30) | Max. atoms/stage (max 10) | Min. Atom Required
Bloom filter | 29 | 4 | 3 | R/W
Heavy hitter detection | 35 | 10 | 9 | RAW
Flowlet switching | 37 | 3 | 3 | PRAW
Sampled NetFlow | 18 | 4 | 2 | IfElseRAW
HULL | 26 | 7 | 1 | Sub
Adaptive Virtual Queue | 36 | 7 | 3 | Nested
CONGA | 32 | 4 | 2 | Pairs
CoDel | 57 | 15 | 3 | Doesn’t map
A family of atoms
Compilation results
Abstractions for line-rate programming
Packet transactions
  Stateful algorithms
  C-like syntax
  Automatically compile to a pipeline
Push-In First-Out queues
  Expresses many scheduling algorithms
  Modest area overhead
Decades of scheduling algorithms, but no consensus on
abstractions for scheduling. In contrast to:
  Parse graphs for parsing
  Match-action tables for forwarding
The scheduler has very tight timing requirements
Need an expressive abstraction running at line rate
It decides in what order are packets sent
E.g., FCFS, priorities, weighted fair-queueing
Key observation
In many algorithms, the order can be determined
before enqueue
i.e., relative order of buffered packets does not change
The Push-In First-Out Queue
Rank Computation
2
9
8
5
PIFO Scheduler
f = flow(pkt)
p.tmp = T[f] + p.len
…
...
p.rank = 2 * p.tmp
(programmable)
(fixed logic)
Rank computation is a packet transaction
(e.g., WFQ, strict priorities, shaping)
Generalizes to hierarchical scheduling)
Hardware implementation
Meets timing @ 1 GHz, 4% area overhead
Atom = action unit + state
A router’s atoms form its instruction set
Program in C-like DSL,
compile to run at line-rate