## Slide 1: Programming Line-Rate Routers
Mohammad Alizadeh
Notes: Thanks for having me here. I am Anirudh and I am a graduate student at MIT. I am going to be talking about work
I have been doing over the past year on abstractions for programming network data-planes that run at line rate.

## Slide 2: Joint work with
MIT: Suvinay Subramanian, Hari Balakrishnan
Barefoot: Changhoon Kim, Mihai Budiu, Anurag Agrawal, Steve Licking
Cisco: Da Chuang, Sharad Chole, Tom Edsall
Microsoft Research: George Varghese
Stanford: Sachin Katti, Nick McKeown
University of Washington: Alvin Cheung
Anirudh Sivaraman (MIT)
Notes: Before I start, I should mention that this is joint work with an outstanding set of collaborators from
MIT, Barefoot Networks, Cisco Systems, Microsoft Research, Stanford, and University of Washington.
Also, I encourage you to interrupt me and ask questions as we go along.

## Slide 3: Programmability at Line-Rate
Programmable: Can we express new data-plane algorithms?
  Active queue management
  Congestion control
  Measurement
  Load balancing
  Packet scheduling
Line-rate: Highest capacity supported by dedicated hardware
Stateful algorithms
Notes: Maybe define data-plane algorithm formally here …
So, the talk is about programmability at line-rate. Let’s break down each of those two parts.
When I say programmable, I mean the ability to run a new data-plane algorithm (possibly something that we don’t know of today) on a switch.
And by line rate, I mean switches that operate at the highest capacity supported by dedicated hardware at any given time. And line-rate is important, it implies that we can’t use a software switch or network processor.

## Slide 4: The quest for programmability
Chart: Year
| 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2014.0
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Hardware router | 32 | 80 | 240 | 640 | 3200
10—100X gap between hardware and software routers
Notes: Software platforms provide full programmability, but they have typically been between 10 and 100 times slower than dedicated hardware at any point in time.

## Slide 5: Programmable switching chips
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Same performance as fixed-function chips, some programmability
Notes:   And so we’ve seen the development of programmable switching chips, which aim to provide programmability without compromising performance.

## Slide 6: This Talk
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Packet transactions: High-level programming of data-plane algorithms
Programmable packet scheduling
Programmable switching chips
Same performance as fixed-function chips, some programmability
Queues/
Scheduler
Notes:   In this talk, I’m going to discuss our work on two aspects of programmable switching chips.
  Packet transactions, which is a high-level programming framework for expressing data-plane algorithms.
  A design for a programmable packet scheduler.

## Slide 7: Isn’t P4 sufficient?
Match-action is great for forwarding
But, limiting for stateful data-plane algorithms
RED Algorithm
On enqueue:
Calculate average queue size
if min < avg < max
calculate probability p
mark packet with probability p
else if avg > max:
mark packet
pipeline
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
?
Inconvenient to think in terms of match-action pipeline
Given an algorithm, hard to know if it maps

## Slide 8: Packet transactions
Packet transaction: Block of imperative code
Transaction runs to completion, one packet at a time, serially
if (count == 9):
pkt.sample = 1
count = 0
else :
pkt.sample = 0
count++
count
p1.sample = 0
p2.sample = 0
p1
p2
0
1
2
9
0
p10
p10.sample = 1
packet fields
persistent state
Notes:   That leads us to the idea of packet transactions: a block of imperative code that is atomic and isolated from other such blocks.
  What do I mean by that? The idea here is that the programmer programs to the illusion that there is exactly one packet in the system at any time.
  When a packet comes in, a sequence of statements atomically updates fields in the packet and state on the switch. All field and state updates complete
  Before the next packet comes in.

## Slide 9: Programming with packet transactions
Stage 1
Stage 2
Stage 16
if (count == 9):
pkt.sample = 1
count = 0
else:
pkt.sample = 0
count++
Packet Sampling Pipeline
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Packet Sampling Algorithm
Reject code that can’t be mapped
Compiler
Notes:   A compiler then translates this into a pipelined implementation suitable for a programmable switch.

## Slide 10: The Domino DSL
A subset of C, restricted for line-rate switch hardware
No loops (for, while, do-while)
  Packet processing time must be deterministic
No unstructured control flow (break, continue, goto)
No pointers, heaps
  Chip memory is statically allocated
Notes: The first thing we do to simplify the Domino compiler is to restrict the language.
First, there are no loops because a loop with an unbounded iteration count cannot be run at line rate.
This is because it isn’t clear how long it takes to process each packet and hence how long the packet
Processing pipeline will be.
Because we forbid all loops, we also forbid unstructured control flow such as break and continue that
let you break out of a loop.
We also forbid pointers and heaps because all memory on these chips is statically allocated.
Through this talk, I ‘ll show you how these constraints simplify the Domino compiler.

## Slide 11: A machine model for line-rate switches
pipeline
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16

## Slide 12: A machine model for line-rate switches
pipeline
Stage 1
Stage 2
Stage 16
Packet Header
state
state
action unit
state
action unit
action unit

## Slide 13: A machine model for line-rate switches
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit

## Slide 14: A machine model for line-rate switches
Atom: Smallest unit of atomic packet/state update
A router’s atoms constitute its instruction set
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit
X
constant
Add
Sub
2-to-1 Mux
X
choice
Notes: They must finish processing their inputs within the clock period, which at 1 GHz is 1 ns so that they are ready to process the next packet.

## Slide 15: Stateless vs. stateful atoms
Stateless operations
  E.g., pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
  Can be easily pipelined into two stages
  Suffices to provide simple stateless atoms alone
Stateful operations
  E.g., x = x + 1
  Cannot be pipelined; needs an atomic read+modify+write
  Explicitly design each stateful operation in hardware for atomicity
Notes: TODO: Add figure or make this description a little more precise, a little less rambling.
Stress that this is what complicates the problem.
Atom: smallest unit of atomic state update

## Slide 16: Compiling packet transactions
Packet Transactions
Preprocessing
Code Pipelining
Instruction Mapping
Processing Pipeline
Simplify sequential code
Sequential to parallel code
Respecting hardware constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 17: Preprocessing
Sequential to parallel code
Hardware constraints
Preprocessing
if (count == 9):
pkt.sample = 1
count = 0
else :
pkt.sample = 0
count++
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp;
count = pkt.new;
Notes: Two big takeaways from preprocessing:
Write out state modifications in an explicit read-modify-write form.
Remove branches and replace them with conditional operators.
Jonathan’s question:
========================
Why is predication not wasteful? It doesn’t waste time because the two halves are done in parallel in hardware.
It doesn’t waste area and power because it’s negligible anyway.
====
The preprossing stage is bunch of book-keeping tricks which make life easier on next stages
If else branches replaced by ternary operator  no branching, strictly straight-line code
Turn state variables into stylized from; only read from state, write to state  makes it simpler to identify dependencies for state variables
Two kinds of dependencies
Dependencies within a packet
Dependencies across packets (through persistent state on the switch)

## Slide 18: Code Pipelining
Create one node for each instruction
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
pkt.sample = pkt.tmp
count = pkt.new
Sequential to parallel code
Hardware constraints
Preprocessing
Notes: Now that we have flattened the code, let’s look at how we generate a pipeline from it.
To start, we make a node corresponding to each statement in the program after flattening.

## Slide 19: Code Pipelining
Sequential to parallel code
Hardware constraints
Preprocessing
Packet field dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
pkt.sample = pkt.tmp
count = pkt.new
Notes: Read/After/Write dependencies
What about other dependencies? To simplify the compiler, get rid of other types of dependencies by creating dummy variable (standard compiler technique: static single assignment

## Slide 20: Code Pipelining
State dependencies
Sequential to parallel code
Hardware constraints
Preprocessing
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
pkt.sample = pkt.tmp
count = pkt.new
Notes: Now that we have flattened the code, let’s look at how we generate a pipeline from it.
To start, we make a node corresponding to each statement in the program after flattening.
TODO: Rambling a bit too much here about bidirectional arrows.
Dependencies between fields of different packets through a state variable
--
Add double arrows between the two nodes that read and write to a state; the write to state has to happen after the read
Forward arrow mean: read has to happen before the write for this packet
Backward arrow means: the write has to happen before the read on the next packet

## Slide 21: Code Pipelining
Sequential to parallel code
Hardware constraints
Preprocessing
Strongly connected components
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
pkt.sample = pkt.tmp
count = pkt.new
Notes: TODO: Rambling here. Explain the bidirectional red arrows a bit more crisply.
Spend some time explaining the intuition behind strongly connected components.
Give some intuition for how the algorithm works, instead of just saying that this is the algorithm.
===
Strongly connected component gets to the heart what operations have to happen atomically to respect all dependencies

## Slide 22: Code Pipelining
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp
count = pkt.new
Condensed DAG
Sequential to parallel code
Hardware constraints
Preprocessing

## Slide 23: Code Pipelining
Sequential to parallel code
Hardware constraints
Preprocessing
Code pipelining
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Notes: At this point, we have a pipeline where each stage has some
sequential code that executes within it, while all pipeline stages
execute in parallel.
We have no idea whether those sequential code blocks can actually
be run at line rate or not. In other words, we haven’t quite figured out
if the sequential code block can or cannot be mapped to an instruction
provided by the switch.

## Slide 24: Instruction mapping
Sequential to parallel code
Hardware constraints
Canonicalization
Stage 1
Stage 2
Stage 16
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Notes: REQUIRES WORK here

## Slide 25: Instruction mapping: example
choice
Add
x = x * x doesn’t map
x = x + 1 maps to this atom
We use the SKETCH program synthesis tool to check if a code block maps to an atom
X
constant
Add
Sub
2-to-1 Mux
X
1
Notes: REQUIRES WORK here.
Say that if the code is rejected here, we reject the code up top as well. This is important.
===
What we need to do is figure out how to go from these atomic components to the circuit – if you get a no answer, you just reject the program
Express the circuit as an imperative program with holes to be filled  this is called an implementation sketch. Figure out if there is some assignment of wholes to implement your code block. The search for holes
This is called syntax-based synthesis. Specifically, we use the tool SKETCH to do the program synthesis. (underneath uses some kind of SAT solver)

## Slide 26: Evaluation
Expressiveness: Can we program real algorithms using packet transactions?
Feasibility: Can we design compiler targets with small area overheads?
Compilation: Can the algorithms be compiled to the targets?
Notes:   Hari: Overall, elide details even more.

## Slide 27: Expressiveness of packet transactions
Algorithm | LOC | Auto-generated P4 LOC
Bloom filter | 29 | 104
Heavy hitter detection | 35 | 192
Rate-Control Protocol | 23 | 75
Flowlet switching | 37 | 107
Sampled NetFlow | 18 | 70
HULL | 26 | 95
Adaptive Virtual Queue | 36 | 147
CONGA | 32 | 89
CoDel | 57 | 271
Notes: Takeaway: lines of code not much greater than the native form (simulation, software router)
Stress that none of these have been programmed at line rate before. They have either been burnt into hardware or programmed into software routers.

## Slide 28: Designing compiler targets
Design both stateless and stateful atoms
  Stateless: easy because stateless operations can be pipelined
  Stateful: determines which algorithms can run at line rate
1 GHz clock frequency
  300 each for stateful, stateless atoms (10 atoms per stage, 30 stages)
Synthesize atoms to 32-nm transistor library
  Estimate area overhead relative to 200 sq. mm chip.
Notes:   Need to say that there is 300 stateless + 300 of (one of the stateful) to form each target.
  REQUIRES WORK.

## Slide 29: Atoms used in targets
pkt.f3 =(pkt.f1 | constant)
OP
(pkt.f2 | constant);
where
OP = {+, -, AND, OR, > ,<, ...}
x = (pkt.f | constant);
x = (x | 0) + (pkt.f | constant);
if (predicate(x, pkt.f1, pkt.f2))
x = (x | 0) + (pkt.f1 | pkt.f2 | constant);
else:
x = x
Read/Write (R/W)
ReadAddWrite (RAW)
Predicated ReadAddWrite (PRAW)
+
Stateful
Stateless

## Slide 30: Atoms used in targets
Atom | Description | Overhead
R/W | Read or write state | 0.04%
RAW | Read, add, and write back | 0.07%
PRAW | Predicated version of RAW | 0.13%
IfElseRAW | 2 RAWs, one each when a predicate is true or false | 0.16%
Sub | IfElseRAW with a stateful subtraction capability | 0.24%
Nested | 4-way predication (nests 2 IfElseRAWs) | 0.58%
Pairs | Update a pair of state variables | 0.96%
Stateless
pkt.f3 =(pkt.f1 | constant)
OP
(pkt.f2 | constant);
where
OP = {+, -, AND, OR, > ,<, ...}
+
Least
Expressive
Most
Expressive
(0.22%)
Stateful
Notes: Takeaway: total overhead of less than 2% for stateful and stateless atoms
Seem to be rambling a bit about PRAW and IfElseRAW (remove this?)
Or at least say what PRAW and IfElseRAW are.

## Slide 31: Compiling packet transactions
Algorithm | LOC | Stages (max 30) | Max. atoms/stage (max 10) | Min. Atom Required
Bloom filter | 29 | 4 | 3 | R/W
Heavy hitter detection | 35 | 10 | 9 | RAW
Rate-Control Protocol | 23 | 6 | 2 | PRAW
Flowlet switching | 37 | 3 | 3 | PRAW
Sampled NetFlow | 18 | 4 | 2 | IfElseRAW
HULL | 26 | 7 | 1 | Sub
Adaptive Virtual Queue | 36 | 7 | 3 | Nested
CONGA | 32 | 4 | 2 | Pairs
CoDel | 57 | 15 | 3 | Doesn’t map
Notes: Takeaway: lines of code not much greater than the native form (simulation, software router)
Stress that none of these have been programmed at line rate before. They have either been burnt into hardware or programmed into software routers.

## Slide 32: Outline
Packet transactions: High-level programming of data-plane algorithms
Programmable packet scheduling
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Queues/
Scheduler
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 33: Programmable Packet Scheduling
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Queues/
Scheduler
?
Programming the packet scheduler is off-limits
for today’s switching chips
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 34: Why is programmable scheduling hard?
Decades of scheduling algorithms, but no consensus on abstractions for scheduling; in contrast to
  Parse graphs for parsing
  Match-action tables for forwarding
The scheduler has very tight timing requirements
  One decision per clock cycle is typical
Need expressive abstraction that can be implemented
at line rate
Notes:   Amy: Emphasize that this is MYYYY abstraction.
  So, it should make you wonder. Why is programmable scheduling hard?
  After all, new scheduling algorithms spring up every year.
  The problem is that, despite many years of work on programmable scheduling and hundreds of algorithms, there is
  no consensus on an abstraction to use for ALL scheduling algorithms.
  This is in contrast to other aspects of the switch such as parsing, for which parse graphs are a good abstraction
  and forwarding, for which match-action tables are a good abstraction.
  Conclude here by saying, “packet transactions are insufficient” and we invent a primitive that allows us to keep using packet transactions for this as well.
  Because there is no abstraction, one approach is to throw up your hand and build an FPGA or CPU on the critical path.
  But this also isn’t feasible for line rate switches because you need to make decisions within a few clock cycles.
  So we are really looking for an abstraction that is simple enough that it can finish executing within a few clock cycles.
  Packet transactions are insufficient. On the surface of it, scheduling operates on groups of packets
  or queues. Packet transactions on the other hand, operate one packet at a time.

## Slide 35: What does the scheduler do?
It decides
In what order are packets sent
  e.g., FCFS, priorities, weighted fair-queueing
At what time are packets sent
  e.g., Token bucket shaping
Key observation
In many algorithms, the scheduling order/time can be determined on enqueue
i.e., relative order of buffered packets does not change

## Slide 36: The Push-In First-Out Queue
Packets are pushed into an arbitrary location based on a rank number, and dequeued from the head
  First used as a proof construct by Chuang et. al. in the 90s
  Also a powerful construct for programmable scheduling
2
5
9
7
9
10
13
8
Notes:   That brings me to the primary contribution of our work, an abstraction for programmable packet scheduling.
  Central to our abstraction is the observation that many scheduling algorithms determine the relative order of packet transmissions when packets are enqueued. Put differently, the order of packets in the buffer will not change despite future packet arrivals.
  What do I mean by that? Here are a few examples of scheduling algorithms that all determine packet transmission order at packet arrival.
  The Shortest Job First scheduling discipline orders packets by their flow size, which is known when packets are enqueued.
  The Earliest Deadline First scheduling discipline orders packets by the time remaining until their deadline.
  And FCFS orders packets by packet arrival time.
  This naturally leads us to an abstraction for scheduling which is called a push-in first-out queue where packets are pushed into an arbitrary location based on a priority and dequeued from the head.
  This concept was first proposed as a proof construct in a paper from the late 90s.
  What we are showing is that this construct is practically usable as a construct for prog. Scheduling.
  The rest of this talk shows why PIFOs as an abstraction are expressive and why a PIFO is feasible at line rate.

## Slide 37: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
p.tmp = T[f] + p.len
…
...
p.rank = 2 * p.tmp
Notes: End by reminding them that the reason this works is that the rank can be computed before enqueue

## Slide 38: A programmable scheduler
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Rank Computation
Queues/
Scheduler
?
PIFO Scheduler
Rank computation expressed in P4, or compiled to P4 using Domino DSL
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 39: Weighted Fair Queuing
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len / p.w
p.rank = p.start
Rank Computation
PIFO Scheduler
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 40: Token bucket shaping
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
tokens = min(tokens +
rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
last = now
p.rank = p.send
Rank Computation
PIFO Scheduler
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 41: pFabric (SRPT)
2
9
8
5
PIFO Scheduler
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
PIFO Scheduler
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 42: pFabric (SRPT)
Rank Computation
f = flow(p)
p.rank = f.rem_size
2
9
8
5
PIFO Scheduler

## Slide 43: Beyond a single PIFO
x1
y1
x2
b1
b2
b3
y2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical Packet Fair Queuing
Hierarchical scheduling algorithms need hierarchy of PIFOs

## Slide 44: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical Packet Fair Queuing
PIFO-Red
(WFQ on a & b)
B
B
B
R
R
R
B
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
R

## Slide 45: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow

## Slide 46: PIFO in hardware
Performance requirements, based on standard single-chip shared-memory switch (e.g., Broadcom Trident)
  1 GHz pipeline
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
Naive solution: flat, sorted array, doesn’t scale
Scalable solution: use fact that ranks increase within a flow
Notes: Provide a little more intuition.

## Slide 47: A PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
1 enqueue + 1 dequeue per clock cycle
Can be shared among multiple logical PIFOs
Notes: Logical PIFOs can be supported by modifying the dequeuer logic a little bit.
Instead of dequeueing the head packet, we find the first packet for a particular logical PIFO (using an equality check + priority encoder), and then shift at that position.
Make sure to mention logical PIFOs here.

## Slide 48: A PIFO block
Enqueue:
(logical PIFO,
rank, flow)
Dequeue:
(logical PIFO)
ALU

## Slide 49: A PIFO mesh
Enq
Deq
Enq
ALU
Deq
Enq
ALU
Deq
Next-hop lookup
ALU
Next-hop lookup
Next-hop lookup

## Slide 50: Hardware feasibility
The Rank store is just a bank of FIFOs (stable hardware IP)
Flow scheduler for 1K flows meets timing at 1GHz on 16-nm transistor library
  Continues to meet timing until 2048 flows, fails timing at 4096
E.g., < 4% area overhead for 5-block PIFO mesh
  About 7 mm2
Notes: What determines clock rate and area overhead?
Maybe one or two slides on what affects what?
Make the 4% area overhead an example as opposed to the only design.
Add some scaling behavior.

## Slide 51: Summary
Packet transactions: High-level programming of data-plane algorithms
  Familiar abstraction
  Atoms formalize computational capabilities of line-rate switches
  All-or-nothing compilation
PIFO is a promising abstraction for packet scheduling
  Can express a wide range of algorithms
  Can be implemented at line rate with modest overhead
Preprints of papers appearing at SIGCOMM 2016:
  http://arxiv.org/abs/1512.05023 (Packet transactions)
  http://arxiv.org/abs/1602.06045 (PIFOs)

## Slide 53: Other future work
Instruction-set design for programmable routers
Approximate semantics for packet transactions
Sharing memory between pipeline stages
Programmable NICs

## Slide 54: Composing PIFOs: min. rate guarantees
Minimum rate guarantees:
Provide each flow a guaranteed
rate provided the sum of these
guarantees is below capacity.
PIFO-Root
Prioritize flows under
min. rate
PIFO-A
(FIFO for flow A)
PIFO-B
(FIFO for flow B)
1
3
2
4
2
A
B
A
B
A
Composing PIFOs
Notes: TODO: Flesh out this slide.
Stress that composed PIFOs can be used for more than just hierarchical scheduling.
Slightly better figure maybe?

## Slide 55: Traffic Shaping
1. update tokens
2. p.send = now +
(p.len - tokens) / rate;
3. p.prio =p.send
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Notes: A natural question is whether a PIFO can handle non-work-conserving algorithms?
So, our third example looks at Traffic Shaping, the most common of these non-work-conserving algorithms,
whose goal is to limit a flow to a fixed absolute throughput regardless of its offered load and the offered load of other flows.
We can implement Traffic Shaping using PIFOs by computing a packet’s priority in the PIFO based on the wall-clock
departure time of the packet when it is enqueued and dequeuing a packet whenever its wall-clock time arrives.
A PIFO allows you to express anything where you can determine the transmission order when packets are enqueued.
In other words, anything where the relative order doesn’t change in the future.
There are algorithms for which these are not true. In particular, hierarchical scheduling algorithms are a class of algorithms
for which this is not true. Let’s consider one in particular.

## Slide 56: LSTF
Add transmission delay to slack
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Decrement wait time in queue from slack
Initialize slack
values
Notes: Add transmission time at the switch
Too many examples.

## Slide 57: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 58: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.

## Slide 59: The quest for programmable routers
Early routers (late 60s to mid 90s) built out of commodity CPUs
  IMPs (1969): Honeywell DDP-516
  Fuzzball (1971): DEC LSI-11
  Stanford multiprotocol router (1981): DEC PDP 11
  Proteon / MIT C gateway (1980s): DEC MicroVAX II
Notes: CPUs sufficient to maintain forwarding performance (50 Kbit/s to 1 Mbit/s)
CPUs represent the peak of programmability

## Slide 60: Programmability at line-rate
Performance and predictability of hardware, line-rate routers
More programmable than fixed-function routers
  Much more than the current OpenFlow/SDN APIs for routers
  …, but less than software routers
Chipsets emerging around this paradigm: RMT, FlexPipe, Xpliant
  Moore’s law has reduced area overhead for programmability
Notes: Moore’s law has shrunk combinational logic for programmability.
It’s shrunk buffers as well, but usually that just means you increase buffers by a bit.
TCAM, SRAM, and IO remain the biggest sources of area on a chip.

## Slide 61: Programmable switching chips
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
?
Programming the packet scheduler is off-limits
for today’s switching chips
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 62: Programmable switching chips
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
?
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 63: This Talk
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Packet transactions: High-level programming of switch pipeline
Programmable packet scheduling
Programmable switching chips
Same performance as fixed-function chips, some programmability
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 64: This Talk
Out
Deparser
Egress pipeline
pipeline
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Notes:   Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 65: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 66: A machine model for line-rate routers
Deterministic pipeline
Atoms: Smallest unit of atomic packet processing / state update
A router’s atoms constitute its instruction set
Notes: They must finish processing their inputs within the clock period, which at 1 GHz is 1 ns so that they are ready to process the next packet.
Say that it’s very deterministic, latency and throughput.
Make sure to mention that atoms are the smallest unit of atomic packet processing.
REQUIRES WORK, stress the definition of atom once.