## Slide 1: Programming Line-Rate Switches
Anirudh Sivaraman
Notes: Thanks for having me here. I am Anirudh and I am a graduate student at MIT. I am going to be talking about work
I have been doing over the past year on abstractions for programming network data-planes that run at line rate.

## Slide 2: Joint work with
MIT: Suvinay Subramanian, Hari Balakrishnan, Mohammad Alizadeh
Barefoot Networks: Changhoon Kim, Anurag Agrawal, Steve Licking, Mihai Budiu
Cisco Systems: Shang-Tse Chuang, Sharad Chole, Tom Edsall
Microsoft Research: George Varghese
Stanford University: Sachin Katti, Nick McKeown
University of Washington: Alvin Cheung
Notes: Before I start, I should mention that this is joint work with an outstanding set of collaborators from
MIT, Barefoot Networks, Cisco Systems, Microsoft Research, Stanford, and University of Washington.
Also, I encourage you to interrupt me and ask questions as we go along.

## Slide 3: Traditional networking
Fixed (simple) switches and programmable (smart) end points
Notes: Go through this really quickly.

## Slide 4: This is showing signs of age …
Switch features tied to ASIC design cycles (2-3 years)
  Long lag time for new protocol formats (IPv6, VXLAN)
Operators (esp. in datacenters) need more control over switches
  Access control, load balancing, bandwidth sharing, measurement
Many switch algorithms never make it to production

## Slide 5: The quest for programmable switches
Early switches built out of minicomputers, which were sufficient
  IMPs (1969): Honeywell DDP-516
  Fuzzball (1971): DEC LSI-11
  Stanford multiprotocol switch (1981): DEC PDP 11
  Proteon / MIT C gateway (1980s): DEC MicroVAX II
Notes: Ideally, we would have a programmable switch, and continue here …
CPUs sufficient to maintain forwarding performance (50 Kbit/s to 1 Mbit/s)
CPUs represent the peak of programmability
IMPs: BBN
Fuzzball: David Mills
Proteon: Noel Chiappa
Stanford multiprotocol switch: William Yeager (ships in the night switch), basis of CISCO.

## Slide 6: The quest for programmable switches
Chart: Single-Chip Aggregate Switching Capacity
| 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2012.0 | 2014.0
Hardware switch | 32 | 80 | 240 | 640 | 1280 | 3200
Software switch | 0.1 | 0.17 | 4 | 35 | 40 | 100
Software switches (CPUs, NPUs, GPUs, FPGAs) are 10—100x slower
Notes: Mention that it is on log scale
Define line rate
Make sure to mention NPU, GPU, CPU, multi-core etc. here so that it’s clear that it’s a statement independent of platform.
Are the two lines diverging? I think it’s no if you include FPGAs: The CORSA data planes weigh in at 640G now, Tofino is at 6.4 Tbps. There’s talk of 10 Tbps switches already.
Unpredictable performance examples: hardware config (number of cores, RAM size, etc.)

## Slide 7: The vision: programmability at line rate
Performance of fastest, fixed-function switches (> 1 Tbit/s)
More programmable than fixed-function switches
  Much more than OpenFlow/SDN, which only programs routing/control plane.
  …, but less than software switches
Such programmable chips are emerging: Tofino, FlexPipe, Xpliant
  As are languages such as P4 to program them
Notes: Moore’s law has shrunk combinational logic for programmability.
It’s shrunk buffers as well, but usually that just means you increase buffers by a bit.
TCAM, SRAM, and IO remain the biggest sources of area on a chip.
As we’ll see, this focus on line rate requires careful thought and hardware design.

## Slide 8: This Talk
  The machine model: Formalizes the computational capabilities of line-rate switches
  Packet transactions: High-level programming for the switch pipeline
  Push-In First-Out Queues: Programming the scheduler
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
match/action
match/action
match/action
match/action
match/action
This talk
TCP
New
IPv4
IPv6
VLAN
Eth
Notes:   In this talk, I’m going to discuss our work on two aspects of programmable switching chips.
  Packet transactions, which is a high-level programming framework for expressing data-plane algorithms.
  A design for a programmable packet scheduler.
  TODO: There are some nasty empty text boxes hiding in the background. That was the easiest way to remove Stage 1, Stage 2, … Stage 16.

## Slide 9: A machine model for line-rate switches
pipeline
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
Notes: Ok, so, hopefully by now I have convinced you that switches should look like a pipeline underneath. Let’s took at the pipeline in more depth.
Of course, the serial view provided by packet transactions is an illusion provided to the programmer. Under the hood, the switch is heavily pipelined and processes multiple packets concurrently. Let’s look at a switch in a little more detail.
First, every stage of the pipeline has some match-action tables that process packets before handing it off. The match simply filters out packets and the actual packet processing happens in the action. So let’s focus on that alone.

## Slide 10: A machine model for line-rate switches
pipeline
Stage 1
Stage 2
Stage 16
Packet Header
state
state
action unit
state
action unit
action unit
Notes: The action is carried out by an action unit, which is a digital circuit processing packet fields. Internally, an action unit can update some local state, such as a counter. All action units in a stage process a single packet in parallel, by having different action units touch disjoint portions of the packet.

## Slide 11: A machine model for line-rate switches
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit
pipeline
Typical requirement: 1 pkt / nanosecond
Notes: In steady state, each action unit processes the packet and hands it off to the next stage, so each stage is processing one packet at any instant. Typically, for switch pipelines today this translates to processing a packet every ns at each pipeline stage.

## Slide 12: A machine model for line-rate switches
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit

## Slide 13: A machine model for line-rate switches
Atom: smallest unit of atomic packet/state update
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit
X
constant
Add
Mul
2-to-1 Mux
X
choice
A switch’s atoms constitute its instruction set
Notes: This combination of an action unit + its internal local state we call an atom. It captures atomic units of computation provided natively by the switch hardware. By atomic, we mean that any updates to state local to the atom must be visible before the next packet is processed by that atom, i.e., within a ns.
There is one important restriction with state here. State is purely local to an atom. It is not shared between atoms within a stage or across stages. It can however be carried from one stage to the next by reading it into a packet field. This is because sharing state requires a multi-ported memory, which is hard.
What does one of these atoms look like? Here’s an atom we just made up that contains the state x and an action unit that either adds or multiplies a constant with x. Both constant and choice are parameters supplied by the programmer.
You can now create a switch pipeline with a grid of such atoms. If you specify an atom, along with how many atoms you want in a stage (pipeline width) and how many stages you want (pipeline depth), you have specified its instruction set.

## Slide 14: Stateless vs. stateful operations
pkt.tmp =
pkt.f1 + pkt.f2
  Stateless operation: pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
pkt.f4 =
pkt.tmp - pkt.f3
f1
f2
f3
f4 =
tmp – f3
tmp = f1 + f2
f1
f2
f3
f4
tmp = f1 + f2
f1
f2
f3
f4
tmp
Can pipeline stateless operations
Notes: Now, let me dive a bit deeper into these atoms to show how the design process is different for atoms that do and do not modify persistent switch state. Let’s do this with some examples.
First, let’s look at the stateless op, f4 = f1 + f2 – f3., click
Now, let’s see what atoms for this operation look like. We can create two atoms in two different pipeline stages. Click,
The first adds f1 and f2 and writes it to tmp. Click,
The second subtracts f3 from tmp.
In general, you can do this for more involved stateless operations by breaking it down into a sequence of pair-wise operations on packet fields.
So, as a switch designer, you can design stateless atoms that perform arithmetic on pairs of packet fields and many stateless operations can be composed out of these simpler pair-wise instructions, by the compiler.

## Slide 15: Stateless vs. stateful operations
  Stateful operation: x = x + 1
pkt.tmp = x
pkt.tmp ++
x = pkt.tmp
tmp
tmp
= 0
tmp
= 1
tmp
tmp
= 0
tmp
= 1
X = 1
X = 0
X should be 2,
not 1!
Notes: Let’s see if we can apply the same trick to a stateful operation. Let’s pick a counter. Now, one implementation is a 3-stage pipeline. The first stage reads the counter into packet field tmp, the second one increments tmp, and the last one writes back the incremented value.
But this doesn’t work, and I’ll show you why. Let’s say two packets red and green enter the pipeline in adjacent clock cycles 0 and 1. In cycle 1, Red picks up tmp=0, while Green just enters the pipeline.
Now, in clock cycle 2, pink’s tmp becomes 1, while green’s tmp picks up the old value 0. Eventually green makes its way through the pipeline and updates x to 1, which is incorrect.
The problem is that the counter isn’t atomic anymore. To guarantee atomicity, you need the hardware to support an increment, where conceptually the rmw all complete within a clock cycle.

## Slide 16: Stateless vs. stateful operations
  Stateful operation: x = x + 1
X++
tmp
X
Cannot pipeline, need atomic operation in h/w
Notes: In general, this is true of arbitrary read-modify-write operations, where the entire rmw must complete in a clock cycle to guarantee atomicity. Unlike a stateless operation, you can’t pipeline the operation easily.
Now, this is true in general, and as your stateful operation grows more complicated, you will need to pack more and digital logic within a 1 clock cycle budget because there is no easy recipe to break it up into simpler operations.

## Slide 17: Stateful atoms can be fairly involved
Update state in one of four ways based on four predicates.
Each predicate can itself depend on the state.
Notes: Here’s a particularly extreme instance of this problem, where this atom needs us to update a state variable in one of four ways based on four predicates that themselves depend on state.
As a result, these stateful atoms look very different from instructions for processors.

## Slide 18: This Talk
  The machine model: Formalizes the computational capabilities of line-rate switches
  Packet transactions: High-level programming for the switch pipeline
  Push-In First-Out Queues: Programming the scheduler
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
match/action
match/action
match/action
match/action
match/action
This talk
TCP
New
IPv4
IPv6
VLAN
Eth
Notes:   In this talk, I’m going to discuss our work on two aspects of programmable switching chips.
  Packet transactions, which is a high-level programming framework for expressing data-plane algorithms.
  A design for a programmable packet scheduler.

## Slide 19: Packet transactions
Packet transaction: block of imperative code
Transaction runs to completion, one packet at a time, serially
if (count == 9):
pkt.sample = pkt.src
count = 0
else :
pkt.sample = 0
count++
count
p1.sample = 0
p2.sample = 0
p1
p2
0
1
2
9
0
p10
p10.sample = 1.2.3.4
Notes:   Let’s look at each in turn. So, what is a packet transaction?
  It’s a block of imperative code that captures an algorithm’s logic. More formally, when a packet comes in, a packet transaction is executed for the packet. It updates some packet fields and some state on the switch that persists across packets. Only after this transaction completes, do we move on to processing the next packet. So, there’s this illusion of processing a single packet at a time serially as though you have a really fast single-core processor.
  Let’s illustrate this with a simple example that samples the source address of every 10th packet by writing into a sample field. Here, pkt.sample denotes a packet field, while count is some persistent state stored on the switch.
  [SPEED UP]
  Now, let’s say p1 shows up. Count is 0. p1 is not sampled, count goes to 1. Similarly, with p2, it isn’t sampled and count goes to 2. Finally, when p10 arrives, it is sampled because count is 9, and count resets to 0.
  This model allows the programmer to easily specify the input/output behavior of the algorithm without worrying about details of the switch pipeline.

## Slide 20: Packet transactions are expressive
Algorithm | LOC
Bloom filter | 29
Heavy hitter detection | 35
Rate-Control Protocol | 23
Flowlet switching | 37
Sampled NetFlow | 18
HULL | 26
Adaptive Virtual Queue | 36
CONGA | 32
CoDel | 57
Notes: Ok, so now that I have shown you how to design these atoms, let’s look at what you can do with them. For this, we need some algorithms, and we picked a set spanning congestion control, measurement, load balancing, and AQM, and wrote them in Domino.
Their lines of code are listed here and they aren’t very different from the number of LOC you would have to write when programming a software switch with these algorithms. So that’s some measure of the abstraction being easy to use.
P4 is more low-level, closer to hardware, requires dealing with concurrency head on.

## Slide 21: Compiling packet transactions
Stage 1
Stage 2
Stage 16
Packet Sampling Pipeline
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1
Packet Sampling Algorithm
Compiler
Reject code that can’t be mapped
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Notes:   Ok, so we have spoken about a high-level abstraction, called packet transactions, and a low-level abstraction, called atoms. A compiler bridges these two abstractions. I’ll only briefly describe the compiler here; details are in the paper.
  The prog first writes code as a packet transaction in an imperative language called Domino. The major restriction is the lack of loops because there is no way to run a loop with an unbounded iteration count at line rate.
  The programmer then feeds this packet transaction into a compiler. The compiler does two things.
  First, it first extracts a pipeline of codelets, which are small code fragments that if executed atomically gurantee a packet transaction’s semantics. We do this using some straightforward dependency analysis.
  Second, the compiler maps this codelet pipeline to an atom pipeline.
  Now, we may be unable to map codelets to atoms because the codelet spec is beyond what the atom can support. In such cases, we reject the code. This is unlike software switches. Software switches run all code but at variable performance tied to code complexity. A prog switch runs some code, but runs it at the full line rate.

## Slide 22: (1) Serial code to codelet pipeline
Create one node for each instruction
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Now that we have flattened the code, let’s look at how we generate a pipeline from it.
To start, we make a node corresponding to each statement in the program after flattening.

## Slide 23: (1) Serial code to codelet pipeline
Packet field dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Read/After/Write dependencies

## Slide 24: (1) Serial code to codelet pipeline
State dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 25: (1) Serial code to codelet pipeline
Strongly connected components
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: NG: Spend some time explaining the intuition behind strongly connected components.

## Slide 26: (1) Serial code to codelet pipeline
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new
Condensed DAG
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 27: (1) Serial code to codelet pipeline
Code pipelining
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1

## Slide 28: (2) Codelets to atoms
Stage 1
Stage 2
Stage 16
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1
Assign each codelet to one atom.
Reject if you run out of atoms.

## Slide 29: (2) Codelets to atoms
choice
Add
x = x * x doesn’t map, reject code
x = x + 1 maps to this atom
X
constant
Add
Mul
2-to-1 Mux
X
1
Determines if algorithm can run at line rate
Use program synthesis for mapping problem.
Notes: ===
What we need to do is figure out how to go from these atomic components to the circuit – if you get a no answer, you just reject the program
Stress that we use program synthesis here.

## Slide 30: The compiler as a tool for switch design
Atom
Algorithm
Compiler
Pipeline
geometry
Algorithm doesn’t compile?
Modify pipeline geometry or atom.
Algorithm compiles
Move on to another algorithm
Notes:   Let’s see how we can now use our compiler to interactively design atoms for prog switches and also to compile to an atom pipeline once it has been developed.
  The compiler takes three inputs, the algorithm, a specification of the atom’s capabilities, and a pipeline geometry (the depth and width of the pipeline).
  Now, invariably, the algorithm won’t compile because its codelet doesn’t map to the atom we have or we don’t have enough atoms in the pipeline. Either way, we modify either the pipeline geometry or the atom type and try again.
  If the algorithm does compile, we move on to the next one, and see if the atom works for the next algorithm. We iterate till we are satisfied that the single atom covers all the algorithms we want.
  Again, we focus on stateful atoms. As I showed earlier, stateless atoms are easier to design and we use RMT’s stateless instruction set.
  Focus on stateful atoms, stateless operations are easily pipelined

## Slide 31: Demo
Notes: Let’s see a demo of this iterative process. (remember to transition smoothly to the demo and back)
Flow: Bloom filter -> describe algorithm and Domino -> say you need atom -> describe atom -> run compiler –> describe heavy hitter -> doesn’t map -> move to raw.sk -> QED
So to start off let’s take a simple algorithm that uses a bloom filter to track a set of src,dst pairs. Further, it learns new pairs in the data plane.
So the code for this is here.
At the top we declare all the pieces of state, in this case, three arrays for the bloom filter.
Below that we have the packet transaction that takes a packet as argument.
The logic for this learning filter is straightforward. We compute three indices into the three arrays that store the bloom filter.
We then check if all three locations are set to determine if this pair is already a member.
We learn this new pair regardless of whether it was a member or not.
Ok, so that’s the Domino program. We need an atom as well. So, let’s start with the simplest atom, just the ability to read a state variable and the ability to write either a constant or a packet field into the state, based on a 2-to-1 mux (show figure). So you can’t read, modify and write back with this atom.
Now, let’s run the compiler on learn filter with a pipeline made up of the rw atom of depth and width 10.
The .sk file is a format that we use to describe an atom’s capabilities.
Ok, so this maps, which is good.
Now, let’s try a slightly more complicated algorithm, a heavy hitter detector using a count-min sketch. Again, the code is straightforward.
You hash into three locations.
You Check if all three exceed a threshold.
You increment all those three locations.
So, this algorithm needs the ability to increment a piece of state, by reading, adding 1, and writing back. So we wouldn’t expect the read/write atom to work. Let’s see if the compiler tells us that. And it does.
So for this, let’s try the next more complicated atom, which is the ability to read a piece of state, add a constant or packet field to it, and then write it back. This is what its circuit looks like.
Now, as expected, if we run heavy_hitters using this atom it compiles.
That should give you a sense for how you can use this tool interactively to design atoms.

## Slide 32: Stateful atoms for programmable switches
Least
Expressive
Most
Expressive
Atom | Description
R/W | Read or write state
RAW | Read, add, and write back
PRAW | Predicated version of RAW
IfElseRAW | 2 RAWs, one each when a predicate is true or false
Sub | IfElseRAW with a stateful subtraction capability
Nested | 4-way predication (nests 2 IfElseRAWs)
Pairs | Update a pair of state variables
Notes: So, we kept going this way to design more atoms. The first two atoms on this list are what I just showed you. We also set these up in a containment hierarchy so that each atom expresses everything that the atoms above it can.

## Slide 33: Compiling packet transactions to atoms
Algorithm
Bloom filter
Heavy hitter detection
Rate-Control Protocol
Flowlet switching
Sampled NetFlow
HULL
Adaptive Virtual Queue
CONGA
CoDel
Notes: Do our atoms actually support these algorithms? We ran each algorithm on a pipeline of each of the atoms we designed. The final column lists the most expressive stateful atom that is required, i.e., what’s the maximum stateful capability you demand of the hardware to run your algorithm at line rate.
The interesting thing here is CoDel, which doesn’t map to any of our atoms. The reason is CoDel has this square root computation that none of our atoms support. And in general, this is true, there will always be algorithms that do not map to the vendor supplied atoms and hence cannot run at line rate.

## Slide 34: Compiling packet transactions to atoms
Algorithm | Most expressive stateful atom required
Bloom filter | R/W
Heavy hitter detection | RAW
Rate-Control Protocol | PRAW
Flowlet switching | PRAW
Sampled NetFlow | IfElseRAW
HULL | Sub
Adaptive Virtual Queue | Nested
CONGA | Pairs
CoDel | Doesn’t map
Notes: Do our atoms actually support these algorithms? We ran each algorithm on a pipeline of each of the atoms we designed. The final column lists the most expressive stateful atom that is required, i.e., what’s the maximum stateful capability you demand of the hardware to run your algorithm at line rate.
The interesting thing here is CoDel, which doesn’t map to any of our atoms. The reason is CoDel has this square root computation that none of our atoms support. And in general, this is true, there will always be algorithms that do not map to the vendor supplied atoms and hence cannot run at line rate.

## Slide 35: Compiling packet transactions to atoms
Algorithm | Most expressive stateful atom required | Pipeline Depth | Pipeline Width
Bloom filter | R/W | 4 | 3
Heavy hitter detection | RAW | 10 | 9
Rate-Control Protocol | PRAW | 6 | 2
Flowlet switching | PRAW | 3 | 3
Sampled NetFlow | IfElseRAW | 4 | 2
HULL | Sub | 7 | 1
Adaptive Virtual Queue | Nested | 7 | 3
CONGA | Pairs | 4 | 2
CoDel | Doesn’t map | 15 | 3
~100 atom instances are sufficient
Notes: So, how many instances of these atoms do we need? In the next two columns I list the minimal pipeline depth and width required for each algorithm. If you multiply these numbers, even in the worst case, about hundred atoms suffice.

## Slide 36: Programmability adds modest cost
All atoms meet timing at 1 GHz in a 32-nm library.
They occupy modest additional area relative to a switching chip.
Atom | Description | Atom area (micro m^2) | Area for 100 atoms relative to 200 mm^2 chip
R/W | Read or write state | 250 | 0.0125%
RAW | Read, add, and write back | 431 | 0.022%
PRAW | Predicated version of RAW | 791 | 0.039%
IfElseRAW | 2 RAWs, one each when a predicate is true or false | 985 | 0.049%
Sub | IfElseRAW with a stateful subtraction capability | 1522 | 0.076%
Nested | 4-way predication (nests 2 IfElseRAWs) | 3597 | 0.179%
Pairs | Update a pair of state variables | 5997 | 0.30%
<1 % additional area for 100 atom instances
Notes: So, is it feasible to design these 100 atoms in hardware?
To answer this, we wrote these atoms as digital circuits in Verilog and synthesized them to a recent transistor library.
First, they all comfortably meet timing at 1 GHz. Second, their area in silicon is small. More specifically, for the 100 atom instances we need, we incur less than 1% additional area. Now this obviously depends on the number of atom instances, but the takeaway is that this number is pretty small.

## Slide 37: This Talk
  The machine model: Formalizes the computational capabilities of line-rate switches
  Packet transactions: High-level programming for the switch pipeline
  Push-In First-Out Queues: Programming the scheduler
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
match/action
match/action
match/action
match/action
match/action
This talk
TCP
New
IPv4
IPv6
VLAN
Eth
Notes:   In this talk, I’m going to discuss our work on two aspects of programmable switching chips.
  Packet transactions, which is a high-level programming framework for expressing data-plane algorithms.
  A design for a programmable packet scheduler.

## Slide 38: Why is programmable scheduling hard?
Many algorithms, yet no consensus on abstractions, cf.
  Parse graphs for parsing
  Match-action tables for forwarding
  Packet transactions for data-plane algorithms
Scheduler has tight timing requirements
  Can’t simply use an FPGA/CPU
Need expressive abstraction that can run at line rate
Notes:   So, why has prog. sched eluded us? It’s because despite having many scheduling algorithms, we have no consensus on the right abstraction for scheduling.
  Why is this important? Every other aspect of a switch that is programmable has an abstraction for it. For instance, parse graphs capture varied protocol formats. Match-action tables capture many forwarding policies. Packet transactions express many stateful algorithms.
  To compound things, the scheduler has tight timing requirements: typically, one enqueue or dequeue every clock cycle. So, you can’t punt on the problem by putting an FPGA or CPU in the fast path.
  In summary, we need an expressive abstraction that runs at line rate.

## Slide 39: What does the scheduler do?
It decides
In what order are packets sent
  e.g., FCFS, priorities, weighted fair queueing
At what time are packets sent
  e.g., Token bucket shaping
Notes: To motivate an abstraction, let’s first look at what the scheduler does. It decides on two things. First, the order in which packets are transmitted. This captures work-conserving schedulers like priority scheduling, weighted fair queueing, etc. Second, the absolute time at which packets are transmitted; the canonical example being token bucket rate limiting.
So a programmable scheduler will have to provide a way to flexibly specify both order and time.

## Slide 40: A strawman programmable scheduler
Very little time on the dequeue side => limited programmability
Can we move programmability to the enqueue side instead?
Classification
Programmable logic to decide order or time
Packets
Notes: Here’s a strawman prog. scheduler.
Packets come in, they are classified into one of a fixed set of FIFOs, one for each flow. Then, on the dequeue side, some programmable logic picks the next flow to transmit whenever the link is idle. The programmable logic decides both the order in which flows are scheduled, and the absolute times at which flows are scheduled.
The problem with this strawman is that there is very little time on the dequeue side, which greatly limits the programmability it offers. At rates of 100G and beyond, the scheduler supports back-to-back dequeues every few clock cycles. So, the programmable logic must complete within a few clocks to support the next dequeue to the same scheduler.
Instead, can we move programmability to the enqueue side, where each packet has potentially much more processing time available before it is enqueued into the scheduler.
Chang’s comment: Mention that the dequeue side cannot be pipelined because of state, similar argument to Domino from the earlier slides.

## Slide 41: The Push-In First-Out Queue
Key observation
In many schedulers, relative order of buffered packets does not change
i.e., a packet’s place in the scheduling order is known at enqueue
The Push-In First-Out Queue (PIFO): Packets are pushed into an arbitrary location based on a rank, and dequeued from the head
2
5
9
7
9
10
13
8
Notes:   Let’s see how we do this. The key observation is that in many practical schedulers, the relative order of packets that are already buffered doesn’t change with future packet arrivals. Put differently, if a packet comes in, its location in the scheduling order can be determined before it is enqueued. The packet can then by pushed into this location, secure in the knowledge that we don’t have to change the relative order of packets that are already buffered.
  Now, some schedulers that confirm to this property are strict priority scheduling, where the location is determined by a packet’s priority, and FCFS, where the location is determined by arrival time.
  A natural primitive for this is a push-in first-out queue (or PIFO) where packets are pushed into an arbitrary location based on rank (which could be either scheduling order or time), but always dequeued from the head. As an illustration, if packet with rank 8 arrived to this PIFO, it would be pushed between 7 and 9.

## Slide 42: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
…
...
p.rank= T[f] + p.len
Notes: Now, how do we build a programmable scheduler based on a PIFO? To program the scheduler, we program the packet’s rank computation before enqueueing it into a PIFO because that’s the only programmable part.
How do we program the rank computation? Quite literally, by writing out a program for it. Here’s a made-up program, which computes a packet’s rank using a table T for each flow and the packet’s length.
This is the key modularity in the design. It separates out the fixed logic, which is the task of enforcing ranks, from the programmable logic, which is the task of computing ranks. Also, because the programmability is on the enqueue side, you have much more time to compute ranks for each packet. You can potentially compute a packet’s rank anywhere along the packet’s path from the packet’s host to this switch. We’ll see how this lets us express a variety of schedulers.
Ok, so where do the programmable and fixed parts go in a real switch?

## Slide 43
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
A programmable scheduler
Rank computation is a packet transaction
Rank Computation
…
…
…
…
Notes: For this, let’s bring up the switch pipeline again. The PIFOs replace the queues in the scheduler, while the rank computation runs in the ingress pipeline.
How do we run the rank computation? We express it as a packet transaction, which was the focus of my previous talk, which provides a convenient language to write these computations.

## Slide 44
In
Out
Parser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Fair queuing
Deparser
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len
p.rank = p.start
Rank Computation
Out
Notes: Now let’s see some real algorithms programmed with a PIFO.
The first is fair queueing, a work-conserving scheduler. Let’s pick the virtual start-time fair queueing implementation.
Here, for each packet we compute its virtual start time in an idealized fluid fair scheduler. We do this by setting the packet’s start time to the maximum of the finish time of the last packet in the packet’s flow and the current virtual time. Then, we update the flow’s finish time appropriately.
We then schedule packets in order of their virtual start times, which becomes a packet’s rank in the PIFO.

## Slide 45
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Token bucket shaping
tokens = min(
tokens + rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
tokens = tokens - p.len
last = now
p.rank = p.send
Rank Computation
Notes: Next, let’s look at the canonical non-work-conserving algorithm: token bucket shaping.
The rank computation here is a little more involved. It has three parts.
First, we update the tokens using a standard token bucket that increments at some rate and is capped at some burst size. We also decrement tokens to account for packet transmissions.
Second, for an incoming packet, we set its wall-clock departure time to either the current time or some time in the future when it would have made up the shortfall of tokens.
Third, this departure time becomes the packet’s rank in a PIFO.

## Slide 46: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
In
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Notes: Ok, so we have looked at two algorithms where the rank computation runs on the switch. The rank computation can, in fact, run anywhere in the network. For instance, let’s compress this pipeline down to a switch. Let’s also introduce an end host.

## Slide 47: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Rank Computation
f = flow(p)
p.rank = f.rem_size
Notes: We can use this end host to compute the ranks for the shortest remaining flow size scheduler. Here, the end host tracks TCP acks and uses this to set the remaining flow size for each packet in a flow.

## Slide 48: Beyond a single PIFO
x
1
y
1
x
2
b1
b2
b3
y
2
a1
Hierarchical scheduling algorithms need hierarchy of PIFOs
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
Notes: Ok, so we have seen examples of what a single PIFO can do. Common to these examples is the property that the relative order of buffered packets doesn’t change with future arrivals.
There are algorithms that violate this property, such as hierarchical schedulers. I’ll illustrate this through hierarchical packet-fair queueing. Here, the idea is to divide capacity between two classes, Left and Right, in some ratio. Then, we recursively divide capacity between flows within each class, such as a, b and c, d.
So, let’s see why HPFQ cannot be served by a single PIFO. Let’s say this is the current state of the system, with packets departing from the head. Now, when the first packet from flow a arrives, we need to satisfy two constraints simultaneously. One, classes red and blue must alternate because they share capacity equally. Two, within class red, a must be ahead of b, because it has a much higher weight.
To do this, we need to move the packets from b to new locations so that red and blue alternate. Then, we need to move a1 ahead of all packets of b because a has a much higher weight. This combination of moves from a and b is beyond a single PIFO that cannot change the relative order of packets that are already buffered.
But, it turns out we can do this with a hierarchy of PIFOs.

## Slide 49: Beyond a single PIFO
Hierarchical scheduling algorithms need hierarchy of PIFOs
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
Notes: Ok, so we have seen examples of what a single PIFO can do. Common to these examples is the property that the relative order of buffered packets doesn’t change with future arrivals.
There are algorithms that violate this property, such as hierarchical schedulers. I’ll illustrate this through hierarchical packet-fair queueing. Here, the idea is to divide capacity between two classes, Left and Right, in some ratio. Then, we recursively divide capacity between flows within each class, such as a, b and c, d.
So, let’s see why HPFQ cannot be served by a single PIFO. Let’s say this is the current state of the system, with packets departing from the head. Now, when the first packet from flow a arrives, we need to satisfy two constraints simultaneously. One, classes red and blue must alternate because they share capacity equally. Two, within class red, a must be ahead of b, because it has a much higher weight.
To do this, we need to move the packets from b to new locations so that red and blue alternate. Then, we need to move a1 ahead of all packets of b because a has a much higher weight. This combination of moves from a and b is beyond a single PIFO that cannot change the relative order of packets that are already buffered.
But, it turns out we can do this with a hierarchy of PIFOs.

## Slide 50: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
PIFO-Red
(WFQ on a & b)
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
B
R
B
B
R
R
B
R
Notes: This hierarchy of PIFOs is very natural and has a structure similar to the scheduler. The root PIFO arbitrates between two child PIFOs red and blue, while each child PIFO arbitrates between packets.
So, now, let’s see what happens on enq and deq. When a1 shows up, its class R is enqueued into PIFO root, while a1 is enqueued into the red PIFO. On the deq side, let’s say we dequeued now. Then, we pop B out of PIFO root, see that it points to the blue PIFO out, pop x1 out of the blue PIFO, and transmit x1.
So, by recursively dequeuing PIFOs starting from the root, we can transmit successive packets.

## Slide 51: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow
Cannot express some scheduling algorithms, e.g., output shaping.
Notes: So it turns out that we can use a tree of PIFOs for many more algorithms. I am not discussing these here, but the paper has further details.
More importantly, we have algorithms that our abstraction doesn’t support. One important class is output shaping, where we rate limit dequeues from the scheduler. We can’t implement this because PIFOs provide prog. on the enq side, not on the deq side. Again, the paper discusses this in depth.

## Slide 52: PIFO in hardware
Performance targets for a shared-memory switch
  1 GHz pipeline (64 ports * 10 Gbit/s)
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
  Scheduler is shared across ports
Naive solution: flat, sorted array is infeasible
Exploit observation that ranks increase within a flow
Notes: Ok, let’s see if a PIFO is actually feasible.
To answer this, we set out to meet some performance targets typical of a shared-memory switch like the Trident found in many dcs today. Here are some typical nos: a pipeline with a 1 GHz clock rate, 1K flows and 60K packets.
One important note is that the scheduler (and so PIFO hardware as well) is shared across all ports. So we don’t need separate PIFO hardware for each port, which means we don’t have to multiply the area overhead by the number of ports.
So, how do we do this? A naïve solution is one large array with 60K elements. An incoming element is compared in parallel to all 60K elements and shifted into the right location. With 60K parallel comparators, this is a non-starter.
Instead, we exploit the fact that most schedulers schedule across flows, with the implicit assumption that packet ranks increase within a flow. How do we use this?

## Slide 53: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
Notes: Our design has two parts.
A flow scheduler schedules across the head packets of all flows, while a rank store stores packets ranks in a first-in first-out queue for each flow.
The flow scheduler is really a PIFO over the head packets alone.
When an element (say) C6, from flow C with rank 6, is enq, it’s just appended to the back of the rank store. When D4 shows up, it bypasses the rank store and directly goes to the flow scheduler. When we deq, we just pop the head of the flow scheduler array to get A0, then reach into the rank store, pull out A2 and insert it into the flow scheduler array.
If you notice, the flow scheduler has to insert an element like A2 into a sorted array, which we do by comparing it in parallel to all elements in the array. Except now, we can actually do this because the sorted array has only 1K head packets, not all 60K packets.
This block supports up to 1 enq + 1 deq every clock cycle, which is a ns in a typical scheduler. It can also be sliced up across many logical PIFOs, which are PIFOs that are independent of each other, but share the same underlying hardware impl. An example is PIFOs for different output ports, whose schedulers run independently.

## Slide 54: Hardware feasibility
The rank store is a bank of FIFOs, used commonly to buffer data
Flow scheduler for 1K flows meets timing at 1 GHz on a 16-nm transistor library
  Continues to meet timing until 2048 flows, fails timing at 4096
  7 mm2 area for 5-level programmable hierarchical scheduler
  < 4% relative to a 200 mm2 baseline chip
Notes: We first note that the rank store is well understood hardware that switches already use to buffer data packets.
For the flow scheduler, which is more invovled, we synthesized it in Verilog in a 16 nm transistor library and it met timing for 1K flows. It continues to work through 2048 flows, but fails at 4096, so that’s the current limit on our design.
The area of this design is about 7 mm^2 for a 5-level programmable hierarchical scheduler. In context, this is about 4% of a typical switching chip.

## Slide 55: A blueprint for programmable switches
High-performance networking needs specialized hardware
Tension between specialization and programmability
Tailor abstractions to restricted classes of switch functions
  Stateful header processing without loops: Packet transactions, atoms
  Scheduling: PIFOs
  Network diagnostics/measurement: Performance queries (HotNets 2016)
Software and papers:
  http://web.mit.edu/domino (Packet transactions)
  http://web.mit.edu/pifo (PIFOs)
Notes: Keep it simple.
End of Moore’s law means specialization.
Specialization is at odds with programmability.
My approach is to tailor abstractions to very specific classes of switch functionality. The specificity lets you retain high performance, while having a class of algorithms means that it’s somewhat future proof.

## Slide 56: Backup slides

## Slide 57: FAQ
How is this different from P4?
  When we started this work a year ago, P4 was much closer to the hardware. Over time, it’s gotten more high-level, thanks in some part to this work (sequential semantics, ternary operators).
  Even now, however, P4 doesn’t provide transactional or atomic semantics.
  We do have a P4 backend.
Why a pipeline?
  NPUs have a shared-memory architecture, but sharing memory is hard and slows down the switch.

## Slide 58: FAQ
What’s in the compiler?
  Strongly Connected Components to extract atomic portions.
  Code generation using program synthesis.
Do the atoms generalize?
  We don’t know for sure. We designed the atoms and were able to tweak them a little bit to serve more algorithms. But this is something we don’t yet have a handle on.
Is someone implementing it?
  We are tabling a proposal on @atomic for P4.
  There’s industry interest in PIFO, but no one I know actively working on it.

## Slide 59: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 60: Relationship to prior compiler techniques
Technique | Prior work | Differences
If Conversion | Kennedy et al. 1983 | No breaks, continue, gotos, loops
Static Single-Assignment | Ferrante et al. 1988 | No branches
Strongly Connected Components | Lam et al. 1989 (Software Pipelining) | Scheduling in space instead of time
Synthesis for instruction mapping | Technology mapping | Map to 1 hardware primitive, not multiple
 | Superoptimization | Counter-example-guided, not brute force

## Slide 61: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 62: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we convert to static single assignment form, which simplifies dependency analysis.
Static single assignment gets its name from the fact that all variables are assigned
Exactly once and no more.
It’s useful because it gets rid of write-after-read and write-after-write dependencies. In our case,
converting to SSA is trivial because we operate on straight-line code with no branches. Typical
SSA implementations are far more involved because they have to deal with branching.

## Slide 63: Expression Flattening
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
pkt.tmp = pkt.arrival - last_time[pkt.id];
pkt.tmp2 = pkt.tmp > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp2
? pkt . new_hop
: saved_hop [ pkt . id ];
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: The last step in canonicalization is to flatten arbitrarily complicated expressions
to bring them into a form closer to the underlying hardware.
(Quickly skim over this.)

## Slide 64: Instruction mapping: results
Generic method to handle fairly complex templates
Templates determine if a Domino program can run at line rate.
Example results:
  Flowlet switching needs conditional execution to save next hop information:
  saved_hop[pkt.id] = pkt.tmp2 ? pkt.new_hop : saved_hop[pkt.id]
  Simple increment suffices for heavy-hitter detection
  count_min_sketch[hash] = count_min_sketch[hash] + 1
Sequential to parallel code
Hardware constraints
Canonicalization

## Slide 65: Generating P4 code
Required changes to P4
  Sequential execution semantics (required for read from, modify, and write back to state)
  Expression support
  Both available in v1.1
Encapsulate every codelet in a table’s default action
Chain together tables as P4 control program
Notes: Say that this project led to sequential execution semantics.

## Slide 66: Branch Removal
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I ‘ll go through these steps quickly. The first step in canonicalization is to remove branching statements.
Branches complicate control flow and make it harder to infer dependencies.
We eliminate branches using a procedure called if conversion that transforms them into C’s conditional operator.
because the only kind of branch we have is an if statement, if conversion is very straightforward in our case, because
we don’t have any kind of unstructured control flow such as a goto, break, or continue, that significantly complicate
if conversion.
This makes the code flow straight from one statement to the next without exception and makes it very easy to infer
dependencies as well: everything on the right of a “equals” is read and the one statement on the left is written.

## Slide 67: Handling State Variables
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we identify state variables, because they complicate the pipelining procedure.
In the absence of state variables, once you have straight-line code, you only need to
consider how you would pipeline the code for a single packet’s processing and you are
done because all other packets follow the same pipeline and there is no interaction
between packets. With state variables, you need to consider interactions between packets.
To simplify our analysis of state variables and dependencies between packets, we explicitly
limit the ways in which state variables can be accessed. We allow only reads and writes to
state and all other arithmetic happens on packet variables. This also lets us reuse an old
value of a state variable down the pipeline if required.

## Slide 68: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 69: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.

## Slide 70: The Domino compiler
Branch Removal
Domino
Handle state variables
Code Pipelining
Instruction Mapping
Processing Pipeline
Canonicalization
(Sequential Code)
Sequential to
parallel code
Respecting hardware
constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 71: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Pair up read/write
flanks
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we pair up reads and writes to state variables to capture the notion
that state variables remain local to a specific stage in the pipeline. If not,
we would have to read from one stage and write from another requiring
us to route longer wires on the chip.

## Slide 72: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Condense strongly
connected components
into codelets
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we look for stongly connected components in this graph,
and condense them into what we call codelets. These capture the essence of
what operations need to be run atomically for the entire transaction to execute atomically.
Now that we have eliminated circles in the graph, we can schedule the resulting
acyclic graph. This is a straightforward process known as critical
path scheduling where we put each node in the earliest pipeline
stage following all its predecessors.

## Slide 73: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Add packet-field
dependencies
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we add read after write dependencies, where we draw an arrow from the
node that writes a value to the node which reads that value.
This is ALL we need to do to handle dependencies in our case because there are
no other waw or war dependencies after SSA.

## Slide 74: Programming with Packet Transactions
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
Pipeline
Domino
pkt.new_hop =
hash3(pkt.sport,
pkt.dport,
pkt.arrival)
%NUM_HOPS;
pkt.id =
hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: TODO: Per Ravi, Hongzi, consider switching to a simpler example like sampled netflow
To give you a flavor for programming using packet transactions, we look at programming
flowlet switching, a data-plane load-balancing algorithm.
To write imperative code for each packet transaction, we use a language
called Domino with a syntax resembling C. On the right, we contrast it against
writing code in P4.
So let me first describe flowlet switching. Its logic is shown here.
The idea in flowlet switching is to load balance groups of packets separated by
a long gap in time across different paths to carry out more fine-grained traffic
splitting relative to standard ECMP.
The logic in is straightforward. You start off by populating a new
hop variable in each packet using some dynamic quantity such as the packet’s arrival time.
Then, you check if the intepacket gap between this packet and its previous one is sufficiently
large and update a state variable called saved_hop if so.
Then, you simply update the last time and set the next hop to the saved hop (which is either
the new value or the old one).
Now, if you were to explain flowlet switching to someone else, like I just did, it’s natural to express its logic
as a block of imperative code and programming in packet transactions lets you do exactly that.
The logic itself becomes the body of a function. This function flowlet is a packet transaction, which conceptually
Executes atomically on each packet. The rest of the Domino program declares state variables as global
variables, packets as structures, and lets you use the rest of C including the macro preprocessor.
================================
So that’s how you express flowlet switching in Domino. When you compile this code it generates
a pipelined implementation in P4 as shown here. This is how you would program the switch today.
The rest of this talk will describe how its relatively straightforward to build a compiler that achieves
this transformation if you exploit characteristics of the underlying domain of line-rate switches.

## Slide 75: The quest for programmability
Switch | Year | Line-rate
Cisco Catalyst | 1999 | 32 Gbit/s
Broadcom 5670 | 2004 | 80 Gbit/s
Broadcom Scorpion | 2007 | 240 Gbit/s
Broadcom Trident | 2010 | 640 Gbit/s
Broadcom Tomahawk | 2014 | 3.2 Tbit/s
Programmability => 10--100x slower than line rate.
System | Year | Substrate | Performance
Click | 2000 | CPUs | 170 Mbit/s
Intel IXP 2400 | 2002 | NPUs | 4 Gbit/s
RouteBricks | 2009 | Multi-core | 35 Gbit/s
PacketShader | 2010 | GPUs | 40 Gbit/s
NetFPGA SUME | 2014 | FPGA | 100 Gbit/s
Notes: Cisco Catalyst: http://www.cisco.com/c/dam/en/us/products/collateral/switches/catalyst-6807-xl-switch/white_paper_c11-728264.doc/_jcr_content/renditions/white_paper_c11-728264_1.jpg
Intel IXP 2400: http://www.intel.com/design/network/papers/ixp2400.pdf: 4 Gbit/s (copyright 2002)
Broadcom 5670 (2004): 80 Gbit/s (8 ports of 10 G) (https://www.broadcom.com/collateral/pb/5670-PB05-R.pdf, 2004)
Broadcom Scorpion (2007) (24 * 10 G from DCTCP paper, and http://www.enterprisetech.com/2014/09/24/broadcom-fights-ethernet-rivals-tomahawk-chips/ suggests 2007)
Trident (2010): 64 * 10 G = 640 G
Trident II (2012): 100 * 10 G = 1 Tbit/s
BCM Tomahawk (2014): 3.2 Tbit/s
Trident and Tomhawk numbers taken from the pages below.
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
TODO: Turn this into a graph.

## Slide 76: The quest for programmability
Programmability => 10--100x slower than line rate.
Chart: Performance scaling of switches
| 2000.0 | 2002.0 | 2009.0 | 2010.0 | 2014.0
Software routers | 0.17 | 4 | 35 | 40 | 100
Line-rate routers | 32 | 80 | 240 | 640 | 3200
Notes: People have recognized this need at least since the late 90s and quite a few software switch platforms have been developed where you take an existing programming substrate and repurpose it for networking.
Now, here’s a line graph showing how the performance of these software switches has scaled with time, and we can see that it’s improved about 1000 fold since 2000, which is quite impressive.
But, at the same time, if you look at the highest end switches (or what I call line-rate switches, because they run at the highest speed that the cable or line can support), they have always been between 10 and 100 times faster than these software platforms. That’s because they have been specialized from the ground up to support just routing. As a result, these programmable platforms never really gained much adoption because they were always slower than the fastest switches.
So, the takeaway, historically is that programmability has cost us 10—100x in performance. And my research looks at designing programmable switch platforms without any performance penalty.

## Slide 77: Compiler targets: diagram
Operation:
+, -, >, <,
AND, OR
pkt.f1/
constant
pkt.f2/
constant
pkt.f3
pkt.f
constant
x
2-to-1
Mux
pkt.f
constant
x
2-to-1
Mux
x
0
2-to-1
Mux
Adder

## Slide 78: Why are switches pipelined?

## Slide 79: Performance requirements at line rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
10 operations per packet: routing, access control (ACL), tunnels, …
Need to process 1 billion pkts/s, 10 ops per packet
Notes: Important segue way here: Let’s talk about why a pipeline is the right hardware architecture for a switch by arguing for it from first principles.

## Slide 80: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
10 GHz processor
Packets
match/action
Can’t build a 10 GHz processor!

## Slide 81: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action

## Slide 82: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action
match/action
match/action
match/action
Memory replication increases die area

## Slide 83: Function-parallel or pipelined architecture
Route lookup table
1 GHz circuit
ACL lookup table
Tunnel lookup table
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
match/action
match/action
match/action
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 84: P4 comparison

## Slide 85: Programming with packet transactions
Algorithm | LOC | P4 LOC
Bloom filter | 29 | 104
Heavy hitter detection | 35 | 192
Rate-Control Protocol | 23 | 75
Flowlet switching | 37 | 107
Sampled NetFlow | 18 | 70
HULL | 26 | 95
Adaptive Virtual Queue | 36 | 147
CONGA | 32 | 89
CoDel | 57 | 271
Notes: Ok, so now that I have shown you how to design these atoms, let’s look at what you can do with them. For this, we need some algorithms, and we picked a set spanning congestion control, measurement, load balancing, and AQM, and wrote them in Domino.
Their lines of code are listed here and they aren’t very different from the number of LOC you would have to write when programming a software switch with these algorithms. So that’s some measure of the abstraction being easy to use.