## Slide 1: Packet Transactions: High-Level Programming for Line-Rate Switches
Anirudh Sivaraman, Alvin Cheung, Mihai Budiu,
Changhoon Kim, Mohammad Alizadeh, Hari Balakrishnan,
George Varghese, Nick McKeown, Steve Licking
Notes: Thanks Nate. I am Anirudh and I am a graduate student at MIT. I am going to be speaking about packet transactions, which is a new abstraction for programming line-rate switches.
TODO: The contrast of the match-action stage against the white background may not be visible if the projector is bad.

## Slide 2: Programmability at line rate
Programmable: Can we express new data-plane algorithms?
  Active queue management
  Congestion control
  Measurement
  Load balancing
Line rate: Highest capacity supported by dedicated hardware
Today, fixed algorithms hard-coded into hardware
Notes: What exactly do I mean by programming a line-rate switch. By prog, I mean the ability to express new data-plane algorithms for packet processing as packets transit a switch. Here are a few examples of such algorithms.
But, we want this prog without giving up performance. We want to prog these new algos into switches that run at line rate, i.e., the highest capacity supported by dedicated hardware switches.

## Slide 3: Programmable switching chips
In
Queues/
Scheduler
Out
Parser
Deparser
Ingress pipeline
Egress pipeline
TCP
New
IPv4
IPv6
VLAN
Eth
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
match/action
Stage 1
match/action
Stage 16
Same performance as fixed-function chips, some programmability
E.g., FlexPipe, Xpliant, Tofino
Notes:   Why are we looking at this problem now?
  First, with the rise of data centers and software-defined networking, operators seek more control over their network.
  Second, perhaps more importantly, it is actually practical to build programmable chips with the same performance as the highest end fixed function chips. This is just Moore’s law for networking, where transistors are now small enough that the additional area for a prog chip is marginal. Examples of such chips include Intel’s FlexPipe, Cavium’s Xpliant and Barefoot’s Tofino.
  Now, these chips provide a restricted form of prog. As in, because they don’t give up perf, they aren’t nearly as flexible as a software router. So what prog do these chips support?
  These chips have a parser that turns packets into bytes, and as a prog you can specify the protocol format you want to parse. These parsed packets are then looked up in a sequence of match-action tables in a pipeline. Unlike (say) OpenFlow, you can match on any user-defined field in the packet and carry out an arbitrary set of actions by composing smaller primitive actions such as arithmetic on packet fields.

## Slide 4: Where do programmable chips fall short?
No way to program data-plane algorithms today
  Chips good for stateless tasks (forwarding), not stateful algorithms (AQM)
  Limited hardware support for stateful operations (counters).
  Low-level languages (P4, POF).
Questions
  Can we program data-plane algorithms in a high-level language?
  Can we design a stateful instruction set supporting these algorithms?
Notes: So, where do these prog chips fall short? Fundamentally, there is no way to program the algorithms that I mentioned in the first slide on these chips today. The reason for this is simple. These chips focus largely on stateless tasks such as packet forwarding and access control that don’t modify any state in the data plane. By contrast, most algorithms we care about modify state in the data plane, such as the moving average estimate maintained by the RED queue management algorithm or the link rate estimate maintained by the rate-control protocol.
For such algorithms, we need the hardware to support rich manipulation of state in the data plane, and it currently only provides counters.
The second problem is that the languages for prog these switches, such as P4 and POF, are still fairly low-level. They require a programmer to manually specify the sequence of match-action tables a packet needs to pass through, and aren’t well-suited to data-plane algorithms.
  So, we ask two questions:
  Can we express data-plane algorithms in a high-level language that is closer to how a user thinks of these algorithms for a software router, without worrying about things like a pipeline?
  Can we use this to design a stateful instruction set supporting these algorithms that can also run at line rate?

## Slide 5: Contributions
Packet transaction: High-level abstraction for data-plane algorithms
  Examples of several algorithms as packet transactions
Atoms: A representation for switch instruction sets
  Seven concrete stateful instructions
Compiler from packet transactions to atoms
  Allows us to iteratively design switch instruction sets
Notes: We have three concrete contributions:
First, a high-level abstraction called packet transactions to program these data-plane algorithms. We show how several important algorithms fit into this mould.
Second, a representation for the underlying programmable switch’s instruction set called atoms. We use this to design seven concrete stateful instructions that switch designers can use.
Third, a compiler to bridge these two concepts. We show how this compiler allows us to iteratively design switch instruction sets.

## Slide 6: Packet transactions
Packet transaction: block of imperative code
Transaction runs to completion, one packet at a time, serially
if (count == 9):
pkt.sample = pkt.src
count = 0
else :
pkt.sample = 0
count++
count
p1.sample = 0
p2.sample = 0
p1
p2
0
1
2
9
0
p10
p10.sample = 1.2.3.4
packet fields
persistent state
Notes:   Let’s look at each of these in turn. First, packet transactions. Intuitively, a packet transaction is a block of imperative code that captures an algorithm’s logic. Formally, each instance of a transaction runs to completion, and processes a single packet at a time, serially with no overlap between packets.
  Conceptually to a programmer, when a packet comes in, a packet transaction is executed on the packet. It updates some packet fields and some state on the switch that persists across packets. Only after this, is the next packet processed.
  Let’s illustrate this with a simple example that samples the source address of every 10th packet by writing into a sample field. Here, pkt.sample denotes a packet field, while count is some persistent state stored on the switch.
  Now, let’s say p1 shows up. Count is 0. p1 is not sampled, count goes to 1. Similarly, with p2, it isn’t sampled and count goes to 2. Finally, when p10 comes along, it is sampled because count is 9, and count resets to 0.
  This model allows the programmer to easily specify the input/output behavior of the algorithm without worrying about details of the switch pipeline.

## Slide 7: Under the hood …
pipeline
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
Notes: Of course, packet transactions are the programmer’s view. Under the hood, the switch is heavily pipelined and processes multiple packets concurrently. Let’s look at a switch in a little more detail.
First, every stage of the pipeline has some match-action tables that process packets before handing it off. The match simply filters out packets and most of the actual work happens in the action. So let’s focus on that alone.

## Slide 8: A machine model for line-rate switches
pipeline
Stage 1
Stage 2
Stage 16
Packet Header
state
state
action unit
state
action unit
action unit
Notes: The action is carried out by an action unit, which is a digital circuit acting on some packet fields. Internally, an action unit can update some internal local state, such as a counter. This is an important restriction. State is local to an atom. It is not shared between atoms within a stage or across stages. It can however be carried from one stage to the next in a packet field.
Now, all action units in a stage process a single packet in parallel, by having different action units touch disjoint portions of the packet.

## Slide 9: A machine model for line-rate switches
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit
pipeline
Typical requirement: 1 pkt / nanosecond
Notes: In steady state, each action unit processes the packet and hands it off to the next stage, so each stage is processing one packet at any instant. Typically, for switch pipelines today this translates to processing a packet every ns at each pipeline stage.

## Slide 10: A machine model for line-rate switches
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit

## Slide 11: A machine model for line-rate switches
Atom: smallest unit of atomic packet/state update
Stage 1
Stage 2
Stage 16
state
action unit
state
action unit
state
action unit
X
constant
Add
Mul
2-to-1 Mux
X
choice
A router’s atoms constitute its instruction set
Notes: This combination of an action unit + its internal state we call an atom. It captures atomic units of computation provided natively by the switch hardware. By atomic, we mean that any updates to state local to the atom must be visible before the next packet is processed by that atom, i.e., within a ns.
What does one of these atoms look like? Here’s an atom we just made up that contains the state x and an action unit that either adds or multiplies a constant with x. Both constant and choice are parameters supplied by the programmer.
You can now imagine tiling a switch with atoms of one or more types. These atom types, along with how they are laid out in a switch constitute the switch’s instruction set. A router vendor would design and expose these atoms as part of the router’s instruction set.

## Slide 12: Stateless vs. stateful operations
pkt.tmp =
pkt.f1 + pkt.f2
  Stateless operation: pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
pkt.f4 =
pkt.tmp - pkt.f3
f1
f2
f3
f4 =
tmp – f3
tmp = f1 + f2
f1
f2
f3
f4
tmp = f1 + f2
f1
f2
f3
f4
tmp
Notes: Now, let me dive a bit deeper into these atoms. To do this, it’s best to distinguish between atoms that do not touch state and modify only packet fields and atoms that do modify persistent switch state.
First, let’s look at the stateless op, f4 = f1 + f2 – f3. Here, for every packet we can carry out this operation independently because it doesn’t touch any persistent state stored on the switch; so, there are no dependencies across packets.
Now, let’s see what atoms for this operation look like. We can create two atoms in two different pipeline stages. The first adds f1 and f2 and writes it to tmp. The second subtracts f3 from tmp. For a second packet, these operations can be overlapped with the current packet and it’s still correct.
As a router designer, you can design stateless atoms that carry out arithmetic on pairs of packet fields and you’re good to go; many stateless operations can be composed out of these simpler pair-wise instructions, like I just showed.

## Slide 13: Stateless vs. stateful operations
  Stateful operation: x = x + 1
pkt.tmp = x
pkt.tmp ++
x = pkt.tmp
tmp
tmp
= 0
tmp
= 1
tmp
tmp
= 0
tmp
= 1
X = 1
X = 0
X should be 2,
not 1!
Notes: The situation’s rather different for stateful atoms. Let’s pick a counter. Now, one way to implement this is a 3-stage pipeline. The first stage reads the counter into packet field tmp, the second one increments tmp, and the last one writes back the incremented value.
But this doesn’t work, and I’ll show you why. Let’s say two packets pink and green enter the pipeline in adjacent clock cycles 0 and 1. Pink picks up tmp=0 after clock cycle 1. Green just enters the pipeline during clock cycle 1.
Now, in clock cycle 2, pink’s tmp becomes 1, while green’s tmp picks up the old value 0. You can probably see where this is going.
In clock cycle 3, pink writes back 1 into X, while green’s tmp is updated to 1.
And in clock cycle 4, green writes 1 to X again, when it should be 2.

## Slide 14: Stateless vs. stateful operations
  Stateful operation: x = x + 1
X++
tmp
X
Cannot pipeline, need atomic increment in h/w
Notes: The problem with this is that the counter isn’t atomic. To guarantee atomicity, you need the hardware to support an increment that completes in a clock cycle.
In general, this is true of arbitrary read-modify-write operations, where the entire rmw must complete in a clock cycle to guarantee atomicity. Unlike a stateless operation, you can’t pipeline the operation and still retain correctness.

## Slide 15: Stateful atoms can be fairly involved
Nested-If-Else:
Update state in one of four ways based on four predicates.
Each predicate can itself depend on the state.
Notes: As a result, the stateful atoms can end up looking fairly complicated because they pack all the updates to a state within a clock cycle. So, here’s one of our most complicated atoms, which we call a nested if-else.
This essentially allows us to update state in one of four ways depending on four predicates (essentially the four possibilities if you have a pair of nested if-else statements). Each of these four predicates can themselves depend on the state being updated.
As a result, these stateful atoms look very different from standard x86 instructions. The game here is to pack the maximum useful state update functionality within a timing budget of 1 clock cycle.

## Slide 16: Compiling packet transactions
Stage 1
Stage 2
Stage 16
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Packet Sampling Pipeline
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1
Packet Sampling Algorithm
Compiler
Notes:   Ok, so we have spoken about a high-level abstraction, called packet transactions, and a low-level abstraction, called atoms. I’ll now briefly describe the compiler that bridges these two abstractions. I am not discussing the compiler in any detail; there is a more detailed description in the paper.
  The prog first writes code as a packet transaction in an imperative language called Domino. This is like C or Python, except there are no loops because there is no way to run a loop with an unbounded iteration count at line rate.
  The prog then feeds this packet transaction into a compiler. The compiler does two main things.
  First, it first extracts a pipeline of codelets, which are small code fragments that if executed atomically gurantee a packet transaction’s semantics. We do this using some straightforward dependency analysis of operations within the transaction.
  Second, the compiler maps this codelet pipeline to an atom pipeline provided by the hardware. This problem boils down to program synthesis, where we want to configure an atom’s parameters so that it matches up exactly with the spec.
  The important thing about this compiler is that we may be unable to map codelets to atoms because the codelet is beyond what the atom can support. In such cases, we reject the code. This is unlike software routers. Software routers run all code but at variable performance tied to code complexity. A prog switch runs some code, but runs it at the full line rate.

## Slide 17: Designing programmable routers
Atom
Algorithms
Compiler
Pipeline
geometry
All algorithms
compile?
Some algorithm doesn’t compile?
DONE
Modify pipeline geometry or atom, but respect line rate
Focus on stateful atoms, stateless operations (atoms) are easily pipelined
Notes:   Let’s see how we can now use our system to:
  Design atoms for prog routers in the first place, and then
  Compile to these newly designed prog routers.
  Let’s focus on designing these prog routers first. The compiler takes three inputs, the algorithms it cares about, a specification of the atom’s capabilities, and a pipeline geometry (which specifies the depth of the pipeline and its width, the number of atoms in each stage).
  For now, we assume we are designing a single atom type that covers all our algorithms because it simplifies the process of designing the atom and optimizing its circuit implementation.
  Now, invariably, some algorithm won’t compile because its codelet doesn’t map to the atom we have or we don’t have enough atoms. If so, we modify either the pipeline geometry or the atom type and try again.
  We iterate till we are satisfied that the atom we have covers all the algorithms we want.
  Again, we focus on stateful atoms. As I showed earlier, stateless atoms are easier to design and we use RMT’s stateless instruction set.

## Slide 18: Demo

## Slide 19: Stateful atoms for programmable routers
Least
Expressive
Most
Expressive
Atom | Description
R/W | Read or write state
RAW | Read, add, and write back
PRAW | Predicated version of RAW
IfElseRAW | 2 RAWs, one each when a predicate is true or false
Sub | IfElseRAW with a stateful subtraction capability
Nested | 4-way predication (nests 2 IfElseRAWs)
Pairs | Update a pair of state variables
Notes: Everyone here: Give some examples of what each atom does as a column on the side.
Peter: Explain each in terms of the previous one.
Maybe bring each row up one after the other.
Ravi, NG: Provide some context for why these seven.
What would you need to support more atoms?
What is the eventual limit of this process.

## Slide 20: Compilation results
Algorithm | LOC
Bloom filter | 29
Heavy hitter detection | 35
Rate-Control Protocol | 23
Flowlet switching | 37
Sampled NetFlow | 18
HULL | 26
Adaptive Virtual Queue | 36
CONGA | 32
CoDel | 57

## Slide 21: Compilation results
Algorithm | LOC | Most expressive stateful atom required
Bloom filter | 29 | R/W
Heavy hitter detection | 35 | RAW
Rate-Control Protocol | 23 | PRAW
Flowlet switching | 37 | PRAW
Sampled NetFlow | 18 | IfElseRAW
HULL | 26 | Sub
Adaptive Virtual Queue | 36 | Nested
CONGA | 32 | Pairs
CoDel | 57 | Doesn’t map

## Slide 22: Compilation results
Algorithm | LOC | Most expressive stateful atom required | Stages (max 30) | Max. atoms/ stage (max 10)
Bloom filter | 29 | R/W | 4 | 3
Heavy hitter detection | 35 | RAW | 10 | 9
Rate-Control Protocol | 23 | PRAW | 6 | 2
Flowlet switching | 37 | PRAW | 3 | 3
Sampled NetFlow | 18 | IfElseRAW | 4 | 2
HULL | 26 | Sub | 7 | 1
Adaptive Virtual Queue | 36 | Nested | 7 | 3
CONGA | 32 | Pairs | 4 | 2
CoDel | 57 | Doesn’t map | 15 | 3
A few hundred atom instances are sufficient

## Slide 23
Atom | Description | Atom area (micro m^2)
R/W | Read or write state | 250
RAW | Read, add, and write back | 431
PRAW | Predicated version of RAW | 791
IfElseRAW | 2 RAWs, one each when a predicate is true or false | 985
Sub | IfElseRAW with a stateful subtraction capability | 1522
Nested | 4-way predication (nests 2 IfElseRAWs) | 3597
Pairs | Update a pair of state variables | 5997
Modest cost to programmability
All atoms meet timing at 1 GHz in a 32 nm library.
They occupy modest additional area relative to a switching chip.
Notes: Takeaway: total overhead of less than 2% for stateful and stateless atoms
Seem to be rambling a bit about PRAW and IfElseRAW (remove this?)
Or at least say what PRAW and IfElseRAW are.
Just put area in micrometer squared.
Talk about 32 nm library, 1 GHz, and give actual numbers.
Maybe just mention the baseline switching chip off to the side.
<1% seems too insignificant to even mention.
Basically, REDO the results part to provide more context.

## Slide 24
Atom | Description | Atom area (micro m^2) | Area for 300 atoms relative to 200 mm^2 chip
R/W | Read or write state | 250 | 0.04%
RAW | Read, add, and write back | 431 | 0.07%
PRAW | Predicated version of RAW | 791 | 0.13%
IfElseRAW | 2 RAWs, one each when a predicate is true or false | 985 | 0.16%
Sub | IfElseRAW with a stateful subtraction capability | 1522 | 0.24%
Nested | 4-way predication (nests 2 IfElseRAWs) | 3597 | 0.58%
Pairs | Update a pair of state variables | 5997 | 0.96%
Modest cost to programmability
All atoms meet timing at 1 GHz in a 32 nm library.
They occupy modest additional area relative to a switching chip.
Notes: Takeaway: total overhead of less than 2% for stateful and stateless atoms
Seem to be rambling a bit about PRAW and IfElseRAW (remove this?)
Or at least say what PRAW and IfElseRAW are.
Just put area in micrometer squared.
Talk about 32 nm library, 1 GHz, and give actual numbers.
Maybe just mention the baseline switching chip off to the side.
<1% seems too insignificant to even mention.
Basically, REDO the results part to provide more context.

## Slide 25: Conclusion
An abstraction for data-plane algorithms (packet transactions)
A representation for router instruction sets (atoms)
A blue print for designing programmable router hardware
Source code: http://web.mit.edu/domino

## Slide 26: Backup slides

## Slide 27: Sequential to pipelined code
Create one node for each instruction
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Now that we have flattened the code, let’s look at how we generate a pipeline from it.
To start, we make a node corresponding to each statement in the program after flattening.

## Slide 28: Sequential to pipelined code
Packet field dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: Read/After/Write dependencies

## Slide 29: Sequential to pipelined code
State dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 30: Sequential to pipelined code
Strongly connected components
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0
Notes: NG: Spend some time explaining the intuition behind strongly connected components.

## Slide 31: Sequential to pipelined code
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new
Condensed DAG
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 32: Sequential to pipelined code
Code pipelining
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1

## Slide 33: Hardware constraints
Stage 1
Stage 2
Stage 16
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1

## Slide 34: Hardware constraints: example
choice
Add
x = x * x doesn’t map
x = x + 1 maps to this atom
Determines if algorithm can/cannot run at line rate
X
constant
Add
Mul
2-to-1 Mux
X
1
Notes: ===
What we need to do is figure out how to go from these atomic components to the circuit – if you get a no answer, you just reject the program
Stress that we use program synthesis here.

## Slide 35: Our work
Packet transaction in Domino
For each packet
Calculate average queue size
if min < avg < max
calculate probability p
mark packet with probability p
else if avg > max
mark packet
pipeline
match/action
Stage 1
match/action
Stage 2
match/action
Stage 16
Compiler
Program in imperative DSL, compile to run at line-rate

## Slide 36: Stateless vs. stateful atoms
Stateless operations
  E.g., pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
  Can be easily pipelined into two stages
  Suffices to provide simple stateless atoms alone
Stateful operations
  E.g., x = x + 1
  Cannot be pipelined; needs an atomic read+modify+write instruction
  Explicitly design each stateful operation in hardware for atomicity
  Determines which algorithms run at line rate
Notes: “Let’s dig into these atoms a little bit” as the transit phrase instead of saying “there’s one important conceptual distinction I would like to make”.
TODO: Add figure or make this description a little more precise, a little less rambling.
Stress that this is what complicates the problem.
Atom: smallest unit of atomic state update
Mohammad: Bring up an atom diagram.
Mohammad: This wasn’t clear. Hari was a little confused as well. Every stateless operation cannot be pipelined.
Maybe add a pipeline diagram.
Katrina: tell her that stateful is more challenging. Call out what’s hard about this.
Peter: Draw analogy with GPU. Need to design for worst case, which is atomically mutate everything within one clock.
Katrina: Describe clearly why stateless vs. stateful is hard.
Don’t make it sound more ad hoc than it was.
Stress that these operations were fundamental and not ad hoc.
NG: better algorithms than bloom filters and heavy hitters.

## Slide 37: Software vs. hardware routers
Software routers (CPUs, NPUs, GPUs, multi-core, FPGA) lose 10—100x performance
Chart: Year
| 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2014.0
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Hardware router | 32 | 80 | 240 | 640 | 3200
Notes: Mention that it is on log scale
Define line rate
Unpredictable performance examples: hardware config (number of cores, RAM size, etc.)
Make sure to mention NPU, GPU, CPU, multi-core etc. here so that it’s clear that it’s a statement independent of platform.

## Slide 38: Stateful atoms for programmable routers
pkt.f1 = x;
x = (pkt.f2 | constant);
x = (x | 0) + (pkt.f | constant);
if (predicate(x, pkt.f1, pkt.f2))
x = (x | 0) + (pkt.f1 | pkt.f2 | constant);
else:
x = x
Read/Write (R/W) (Bloom Filters)
ReadAddWrite (RAW) (Sketches)
Predicated ReadAddWrite (PRAW) (RCP)

## Slide 39: Language constraints on Domino
No loops (for, while, do-while)
No unstructured control flow (break, continue, goto)
No pointers, heaps
Notes: The first thing we do to simplify the Domino compiler is to restrict the language.
First, there are no loops because a loop with an unbounded iteration count cannot be run at line rate.
This is because it isn’t clear how long it takes to process each packet and hence how long the packet
Processing pipeline will be.
Because we forbid all loops, we also forbid unstructured control flow such as break and continue that
let you break out of a loop.
We also forbid pointers and heaps because all memory on these chips is statically allocated.
Through this talk, I ‘ll show you how these constraints simplify the Domino compiler.

## Slide 40: Instruction mapping: bin packing
Sequential to parallel code
Hardware constraints
Canonicalization
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Notes: Amy: Replace the atoms instead of sitting on top of them.

## Slide 41: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 42: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 43: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we convert to static single assignment form, which simplifies dependency analysis.
Static single assignment gets its name from the fact that all variables are assigned
Exactly once and no more.
It’s useful because it gets rid of write-after-read and write-after-write dependencies. In our case,
converting to SSA is trivial because we operate on straight-line code with no branches. Typical
SSA implementations are far more involved because they have to deal with branching.

## Slide 44: Expression Flattening
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
pkt.tmp = pkt.arrival - last_time[pkt.id];
pkt.tmp2 = pkt.tmp > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp2
? pkt . new_hop
: saved_hop [ pkt . id ];
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: The last step in canonicalization is to flatten arbitrarily complicated expressions
to bring them into a form closer to the underlying hardware.
(Quickly skim over this.)

## Slide 45: Generating P4 code
Required changes to P4
  Sequential execution semantics (required for read from, modify, and write back to state)
  Expression support
  Both available in v1.1
Encapsulate every codelet in a table’s default action
Chain together tables as P4 control program
Notes: Say that this project led to sequential execution semantics.

## Slide 46: Relationship to prior compiler techniques
Technique | Prior work | Differences
If Conversion | Kennedy et al. 1983 | No breaks, continue, gotos, loops
Static Single-Assignment | Ferrante et al. 1988 | No branches
Strongly Connected Components | Lam et al. 1989 (Software Pipelining) | Scheduling in space instead of time
Synthesis for instruction mapping | Technology mapping | Map to 1 hardware primitive, not multiple
 | Superoptimization | Counter-example-guided, not brute force

## Slide 47: Branch Removal
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I ‘ll go through these steps quickly. The first step in canonicalization is to remove branching statements.
Branches complicate control flow and make it harder to infer dependencies.
We eliminate branches using a procedure called if conversion that transforms them into C’s conditional operator.
because the only kind of branch we have is an if statement, if conversion is very straightforward in our case, because
we don’t have any kind of unstructured control flow such as a goto, break, or continue, that significantly complicate
if conversion.
This makes the code flow straight from one statement to the next without exception and makes it very easy to infer
dependencies as well: everything on the right of a “equals” is read and the one statement on the left is written.

## Slide 48: Handling State Variables
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we identify state variables, because they complicate the pipelining procedure.
In the absence of state variables, once you have straight-line code, you only need to
consider how you would pipeline the code for a single packet’s processing and you are
done because all other packets follow the same pipeline and there is no interaction
between packets. With state variables, you need to consider interactions between packets.
To simplify our analysis of state variables and dependencies between packets, we explicitly
limit the ways in which state variables can be accessed. We allow only reads and writes to
state and all other arithmetic happens on packet variables. This also lets us reuse an old
value of a state variable down the pipeline if required.

## Slide 49: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.