## Slide 1: Hardware and software for fast and programmable network monitoring
Srinivas Narayana, Anirudh Sivaraman, Vikram Nathan, Prateesh Goyal, Venkat Arun, Mohammad Alizadeh, Vimal Jeyakumar, and Changhoon Kim
Slides courtesy Srinivas Narayana
Notes: Thank you for the invitation. I am going to be speaking about work that I did as a grad student on designing hardware and software for fast and programmable network monitoring. This is joint work with many excellent collaborators. In particular, I want to mention the lead author on this work, Srinivas Narayana, who is a postdoc at MIT.
So let’s break down the talk’s title: we want both fast and programmable network monitoring. By fast, I mean the ability to run at a switch’s line rate. And by programmable, I mean the ability to express whatever network monitoring question you care about and get accurate results.

## Slide 2: Example: Who caused a microburst?
Queue build-up deep in the network
Per-pkt info: challenging in software
6.4Tbit/s switch: Need 100M recs/s
COTS: 100K-1M recs/s/core
End-to-end probes
Sampling
Counters & Sketches
Mirror packets
Notes: So what might be an example of a performance monitoring question? One example is a microburst, which is common in many production networks. A microburst is a situation in which you occasionally experience latency spikes in the network. This might be for any number of reasons, but one common reason is that some switch in a network is occasionally seeing bursts of traffic from an ill-behaved flow.
When you see this problem, you want to localize which switch queue is contributing to the high latency, and what traffic is filling up the queue. There are a few ways to tackle this problem, none of which are completely satisfactory.
You can send end-to-end probes, but that only tells you that the end-to-end latency is high. It doesn’t tell you where the latency is building up. You can sample the queue’s latency or packets, but then you need to decide what the sampling frequency is. You can use counters and approximate data structures like sketches, but they are tuned for volume statistics like link utilization and number of packets from a specific flow. They don’t effectively generalize beyond such statistics.
One alternative to this to mirror packets and use emerging technologies like in-band-network telemetry to piggyback queue information on the packet. The problem now is that the packets that transit the problematic queue are now scattered all over the network. They need to be collected together to determine at which switch and when queues build up. And the overhead of doing this in software is quite prohibitive.

## Slide 3
Switches should be first-class citizens in performance monitoring.
Notes: Our focus in this talk will be on seeing if we can use switches as first-class citizens in performance monitoring by augmenting them with a small set of measurement primitives to enable programmable network monitoring. You can think of this as designing a hardware instruction set and a software programming language for network performance monitoring on high-speed switches.

## Slide 4: Why monitor from switches?
Already see the queues & concurrent connections
Infeasible to stream all the data out for external processing
Can we filter and aggregate performance on switches directly?
Notes: But just to reiterate, why would you want to monitor from switches. Here are a couple of reasons. In many cases the problem is localized to a single switch (or a small set of switches), and instrumenting those directly is more convenient than having the data be distributed across end points. The alternative of sending all data to an end point for external processing consumes too much network and compute capacity. So the concrete technical question we try to answer is whether we can perform filtering and aggregation on switches directly.

## Slide 5
We want to build “future-proof” hardware:
Language-directed hardware design
Notes: Now, when you build an instruction set, you want it to be as general as possible. Otherwise, it ends up being overfitted in a sense to your current set of use cases, without any guarantee that it can generalize to other use cases. To avoid this, and to attempt to build somewhat future-proof hardware, we adopt a design methodology called language-directed hardware design where we start with an expressive programming language and then design hardware to efficiently support this programming language.

## Slide 6
Expressive query language
Line-rate switch hardware primitives
Performance monitoring use cases
Notes: In more detail, this is how our workflow looks. We start with an informal description of several performance monitoring use cases similar to our Microburst example before. We then design an expressive query language to capture all of these use cases and future unanticipated use cases that are similar to these use cases. Once we have designed this language, we use it to design switch hardware primitives as well.
While this slide shows this process as mostly one directional from use cases to hardware, there is also a bit of feedback in practice. For instance, we restrict our language to what can be reasonably implemented in line-rate hardware. In particular, our language isn’t Turing complete so you can’t do everything with it that you can do with a CPU. In our minds, this was a reasonable tradeoff because that’s the price you pay for high performance.

## Slide 7: Contributions
Marple, a performance query language
Line-rate switch hardware design
  Aggregation: Programmable key-value store
Query compiler

## Slide 8
Queries
Query Compiler
Programmable switches
with the key-value store
Marple programs
Switch programs
To collection servers
Results

## Slide 9
Marple: Performance query language

## Slide 10: Marple: Performance query language
Stream: For each packet at each queue,
  S:= (switch, qid, hdrs, uid, tin, tout, qsize)
Location
Packet identification
Queue entry and exit timestamps
Queue depth seen by packet

## Slide 11: Marple: Performance query language
Stream: For each packet at each queue,
  S:= (switch, qid, hdrs, uid, tin, tout, qsize)
Familiar functional operators
filter
map
zip
groupby

## Slide 12: Example: High queue latency packets
R1 = filter(S, tout – tin > 1 ms)

## Slide 13: Example: Per-flow average latency
  R1 = filter(S, proto == TCP)
  R2 = groupby(R1, 5tuple, ewma)
  def ewma([avg],[tin, tout]):
  avg = (1-⍺)*avg + ⍺*(tout-tin)
Fold function

## Slide 14: Example: Microburst diagnosis
def bursty([last_time, nbursts], [tin]):
if tin - last_time > 800 ms:
nbursts = nbursts + 1
last_time = tin
result = groupby(S, 5tuple, bursty)

## Slide 15: Many performance queries (see paper)
Transport protocol diagnoses
  Fan-in problems (incast and outcast)
  Incidents of reordering and retransmissions
  Interference from bursty traffic
Flow-level metrics
  Packet drop rates
  Queue latency EWMA per connection
  Incidence and lengths of flowlets
Network-wide questions
  Route flapping
  High end to end latencies
  Locations of persistently long queues
...

## Slide 16
Implementing Marple on switches

## Slide 17: Implementing Marple on switches
filter
map
zip
groupby
Stateless match-action rules
[RMT SIGCOMM’13]
  S:= (switch, hdrs, uid, qid, tin, tout, qsize)
Switch telemetry
[INT SOSR’15]

## Slide 18: Implementing Marple on switches
filter
map
zip
groupby
Stateless match-action rules
[RMT SIGCOMM’13]
  S:= (switch, hdrs, uid, qid, tin, tout, qsize)
Switch telemetry
[INT SOSR’15]

## Slide 19: Implementing aggregation
  ewma_query = groupby(S, 5tuple, ewma)
  def ewma([avg], [tin, tout]):
  avg = (1-⍺)*avg + ⍺*(tout-tin)
Compute & update values at switch line rate (1 pkt/ns)
Scale to millions of aggregation keys (e.g., 5-tuples)

## Slide 20
Challenge:
Neither SRAM nor DRAM is both fast and dense

## Slide 21
Caching:
the illusion of fast and large memory

## Slide 22: Caching
Key
Value
On-chip cache (SRAM)
Key
Value
Off-chip backing store (DRAM)
Notes: On-chip cache of the key-value store is in SRAM
Off-chip backing store is in DRAM
But: cache misses lead to router pipeline stalls and non-determinism

## Slide 23: Caching
Key
Value
Read value for 5-tuple key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Modify value using ewma
Write back updated value

## Slide 24: Caching
Key
Value
Read value for 5-tuple key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Req. key K
Resp. Vback
Vback
K

## Slide 25: Caching
Key
Value
Key
Value
On-chip cache (SRAM)
Req. key K
Resp. Vback
K
Vback
Read value for 5-tuple key K
Off-chip backing store (DRAM)
K
Vback

## Slide 26: Caching
Key
Value
Key
Value
On-chip cache (SRAM)
Request key K
Respond K, V’’
K
V’’
K
V’’
Read value for 5-tuple key K
Off-chip backing store (DRAM)
Modify and write must wait for DRAM.
Non-deterministic DRAM latencies stall packet pipeline.
Notes: Stress that DRAM is built for the average case.

## Slide 27
Instead, we treat cache misses as
packets from new flows.

## Slide 28: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
K
V0
Read value for key K
Off-chip backing store (DRAM)

## Slide 29: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K,Vcache
K
Vback
K
V0
Read value for key K
Off-chip backing store (DRAM)

## Slide 30: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K,Vcache
K
K
V0
Read value for key K
Off-chip backing store (DRAM)
Merge
Vback

## Slide 31: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K,Vcache
K
K
V0
Read value for key K
Off-chip backing store (DRAM)
Nothing to wait for.
Vback

## Slide 32: How about value accuracy after evictions?
How do we merge evicted statistics value with previous value accurately?
Let’s represent the statistics operation as a function g over a packet sequence p1, p2, …
g([pi])
Action of g over a packet sequence,
e.g, for a counter g([pi]) = p1.len + p2.len + …

## Slide 33: The Merge operation
merge(g([qj]), g([pi]))
= g([p1,…,pn,q1,…,qm])
Example: if g is a counter, merge is just addition.
Easy generalization to all associative statistics (min, max, product, set union, intersection, etc.)
Vcache
Vback
Statistics over the entire packet sequence

## Slide 34: Mergeability beyond associative statistics
Can merge any statistic g by storing entire pkt sequence in cache
  … but that’s a lot of extra state!
Can we merge with “small” extra state?
Small: extra state size ≈ size of the statistics value being tracked

## Slide 35: Linear-in-state: Merge w. small extra state
S = A * S + B
Examples: Packet and byte counters, EWMA, functions over a window of packets, …
State maintained by the statistic
Functions of a bounded number of packets in the past

## Slide 36: Intuition for linear-in-state
Let’s say we are tracking an EWMA :
If the EWMA starts at or and ends at or respectively
after packets, then:
So we can take a final value calculated from initial value and modify it for a new initial stateusing:
I1
I2
F1
F2

## Slide 37: Intuition for linear-in-state
In our problem:
Small extra state: only number of packets (N), instead of storing each packet
I1
I2
F1
F2
Notes: Say that the more formal result is in the paper.

## Slide 38: Microbursts: Linear-in-state!
def bursty([last_time, nbursts], [tin]):
if tin - last_time > 800 ms:
nbursts = nbursts + 1
last_time = tin
result = groupby(S, 5tuple, bursty)
nbursts: S = A * S + B, where
A = 1
  B = {1, if current pkt within time gap from last;
  0 otherwise}

## Slide 39: Several useful linear-in-state statistics
Counting successive TCP packets that are out of sequence
Histogram of flowlet sizes
Counting number of timeouts in a TCP connection
Micro-burst detection
EWMAs
The linear-in-state operation can also be cheaply implemented using a multiply-accumulate hardware instruction.

## Slide 40: Other linear-in-state queries
Counting successive TCP packets that are out of order
Histogram of flowlet sizes
Counting number of timeouts in a TCP connection
… 7/10 example queries in our paper

## Slide 41
Evaluation:
Is processing the evictions feasible?

## Slide 42: Eviction processing
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K’,V’cache
K’
V’back
K
V0
Off-chip backing store (DRAM)

## Slide 43: Eviction processing at backing store
Trace-based evaluation:
  “Core14”, “Core16”: Core router traces from CAIDA (2014, 16)
  “DC”: University data center trace from [Benson et al. IMC ’10]
  Each has ~100M packets
Query aggregates by 5-tuple (key)
  Show results for key+value size of 256 bits
8-way set-associative LRU cache eviction policy
Eviction ratio: % of incoming pkts that result in a cache eviction

## Slide 44: Eviction ratio vs. Cache size

## Slide 45: Eviction ratio vs. Cache size
218 keys == 64 Mbits
4% pkt eviction ratio
25X reduction from processing each pkt

## Slide 46: Eviction ratio  Eviction rate
Consider 64-port X 100-Gbit/s switch
Memory: 256 Mbits
  7.5% area
Eviction rate: 8M records/s
  ~ 32 cores

## Slide 47: See more in the paper…
More performance query examples
Query compilation algorithms
Evaluating hardware resources for stateful computations
Implementation & end-to-end walkthroughs on mininet

## Slide 48: Summary
On-switch aggregation reduces software data processing
Linear in state: fully accurate per-flow aggregation at line rate
Paper and code available at http://web.mit.edu/marple