## Slide 1: Programmable switches
Slides courtesy Patrick Bosshart and Mihai Budiu

## Slide 2: Outline
Motivation for programmable switches
Early attempts at programmability
Programmability without losing performance: The Reconfigurable Match-Action Table model
The P4 programming language
What’s happened since?

## Slide 3: Recap
Data plane: packet-to-packet behavior of a switch, short timescales of a few ns
Control plane: Establishing routes for end-to-end connectivity, longer timescales of a few ms

## Slide 4: SDN (as of 2013)
Separating control and data planes
Move control plane out of the switch into a central location
Well-defined API to data plane
OpenFlow was a pragmatic solution (lowest common denominator)

## Slide 5: The network isn’t truly software-defined
Can’t “program” the data plane
Can’t change headers
Still tied to vendor’s features
Most router algorithms never make it to production (PDQ, pFabric, D3, CoDel)

## Slide 6: Why program the data plane?
Headers change occasionally (VXLAN, NVGRE)
  … requiring hardware redesign
Too constrained by a vendor’s whims
  Can’t try a new protocol in production
  Lengthy standardization process.
Hardware bugs are costly
People can’t make up their minds
  ECMP, VXLAN, NVGRE, …, what else??
Every other domain does this: GPUs, DSPs, mobile phones
Notes: Burgeoning OpenFlow spec.
This is really not all that revolutionary. Every other domain does this: NVIDIA’s GPUs, TI’s DSPs, mobile phones,

## Slide 7: Early attempts at programmable routers
Chart: Performance scaling
| 1999 | 2000 | 2002 | 2004 | 2007 | 2009 | 2010 | 2014
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Line-Rate router | 32 | 80 | 240 | 640 | 3200
10—100 x loss in performance relative to line-rate, fixed-function routers
Unpredictable performance (e.g., cache contention)
Notes: Mention that it is on log scale
Define line rate
Unpredictable performance examples: hardware config (number of cores, RAM size, etc.)

## Slide 8: The RMT model: programmability + performance
Performance: 1 Tbit/s (also called line rate)
Programmability: New headers, new modifications to packet headers, flexibly size lookup tables, (limited) state modification

## Slide 9: Performance requirements at line-rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
~10 operations per packet (e.g., routing, ACL, tunnels)
Need to process 1 billion packets per second, 10 ops per packet
Notes: Before we discuss the RMT model, let’s talk a bit about the switch architecture.
The paper doesn’t go into much detail about this and assumes a switch is going to have a pipeline of match-action tables (fixed or not). Why is this a good architecture?
Q: Why is a switch architected as a pipeline? Are there other architectures?

## Slide 10: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
Packets
Only sustains 100 M packets per second

## Slide 11: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets

## Slide 12: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
Memory replication increases die area
Lookup table
Match
Action
Match
Action
Match
Action
Lookup table
Match
Action
Match
Action
Match
Action
Lookup table
Match
Action
Match
Action
Match
Action

## Slide 13: Function-parallel or pipelined architecture
Route lookup table
Match
Action
1 GHz circuit
ACL lookup table
Match
Action
Tunnel lookup table
Match
Action
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
But, needs careful circuit design to run at 1 GHz
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 14: Fixed function switch
Deparser
In
Queues
Data
Out
ACL Stage
L3 Stage
L2 Stage
Action: set L2D
Stage 1
L2 Table
L2: 128k x 48
Exact match
Action: set L2D, dec TTL
Stage 2
L3 Table
L3: 16k x 32
Longest prefix
match
Action: permit/deny
Stage 3
ACL Table
ACL: 4k
Ternary match
Parser
Notes: Ok, so with this pipeline model, here’s what a fixed function switch looks like
Each table is hardwired to a specific task.
If you want to size smaller or larger tables, you are out of luck.

## Slide 15: Adding flexibility to a fixed-function switch
Flexibility to:
  Trade one memory size for another
  Add a new table
  Add a new header field
  Add a different action

## Slide 16: Two simple ideas in RMT
Programmable parser
Pipeline of match-action tables
  Match on any parsed field
  Actions combine packet-editing operations (pkt.f1 = pkt.f2 op pkt.f3) in parallel
Notes: This is all you really need to know about the paper 
The rest is just how to make it run at 1 GHz

## Slide 17: The RMT Abstract Model
Parse graph
Table graph

## Slide 18: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
IPV6
TCP
UDP
Ethernet IPV4 TCP
Packet:

## Slide 19: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
TCP
UDP
Ethernet IPV4 TCP
Packet:

## Slide 20: Arbitrary Fields: The Parse Graph
Ethernet
IPV4
TCP
UDP
Ethernet IPV4 RCP TCP
Packet:
RCP

## Slide 21: Reconfigurable Match Tables: The Table Graph
VLAN
MAC
FORWARD
IPV4-DA
ETHERTYPE
RCP
ACL
IPV6-DA

## Slide 22: Changes to Parse Graph and Table Graph
Ethernet
IPV4
TCP
UDP
Done
ACL
L2S
L2D
IPV4-DA
ETHERTYPE
Table Graph
VLAN
VLAN
IPV6-DA
IPV6
RCP
RCP
Parse Graph
MY-TABLE

## Slide 23: But the Parse Graph and Table Graph don’t show you how to build a switch

## Slide 24: Programmable parser
State machine to capture parser’s operation (much like a finite automaton to detect regular expressions)
Implemented as a ternary content-addressable memory (CAM with wildcard bits)
Configure TCAM based on parse graph
Gibb et al. ANCS 2013: Design Principles for Packet Parsers
Notes: Say that it’s not very different from how grep works on Linux.

## Slide 25: Match/Action Forwarding Model
Programmable Parser
Deparser
In
Queues
Action
Stage 1
Match Table
Action
Stage 2
Match Table
…
Data
Out
Action
Stage N
Match Table
Match
Action Stage
Match
Action Stage
Match
Action Stage

## Slide 26: RMT Logical to Physical Table Mapping
TCAM
640b
640b
Physical
Stage n
Physical
Stage 2
Logical Table 1
Ethertype
Logical Table 6
L2D
8 UDP
2
VLAN
3
IPV4
5
IPV6
4
L2S
7 TCP
SRAM
HASH
Physical
Stage 1
ACL
UDP
TCP
L2S
L2D
IPV4
ETH
VLAN
IPV6
9 ACL
Table Graph
Action
Match Table
Action
Match Table
Action
Match Table
Notes: To make it possible to efficiently use multiple stages of match tables, it is assumed that the RMT Model can be configured to map Logical Tables to the Physical Tables.
To create bigger tables, one table may traverse multiple stages.
To create many smaller tables, several tables can be packed into one stage.
To make the allocation even more flexible, the Action instructions and the Statistic could share the same table space.
This slide gives a crude representation of how the the Logical Tables could be mapped to the Physical Tables.
In practice, the control plane would need to create a Table Flow Graph (to accompany the Parse Graph) to decide how the Logical Tables are mapped.
The control plane is assumed to know the number and size of the physical stages available.
There could be as few as 1 stage. A given switch might only allow Logical Tables to directly correspond to Physical Tables.

## Slide 27: Action Processing Model
Instruction
ALU
Match result
Header In
Field
Header Out
Field
Data
Notes: Action processing is assumed to be available in each physical stage of the pipeline.
The headers are available along with the match result and metadata. Optional state could be available to the Action Processors.
There are assumed to be some number of processors (could be 1, could be hundreds) to perform Actions on headers.
The Action instruction set is assumed to be protocol independent (e.g. “insert these 8 bits starting at bit 19 of the 3rd header”).

## Slide 28
ALU
VLIW Instructions
Match result
Modeled as Multiple VLIW CPUs per Stage
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Notes: Allows you to edit packet fields in parallel.

## Slide 29: RMT switch design, some specifics
64 x 10Gb ports
  960M packets/second
  1GHz pipeline
16 programmable parsers
32 Match/action stages
Notes: Mention latency here: each stage about a few 10 ns.
More parsers than pipelines.
Q: What about latency here?

## Slide 30: Cost of Configurability: Comparison with Conventional Switch
Design in 28 nm CMOS.
Many functions identical: I/O, data buffer, scheduling…
Key takeaway:
  Memory and serial I/O lines dominate area
  Combinational logic for action units and parsing are small in comparison (Moore’s law for networking)
Notes: Prop: Explain the electronic design automation process on the blackboard here.

## Slide 31: Chip Comparison with Fixed Function Switches
Section | Area % of chip | Extra Cost
IO, buffer, queue, CPU, etc | 37% | 0.0%
Match memory & logic | 54.3% | 8.0%
VLIW action engine | 7.4% | 5.5%
Parser + deparser | 1.3% | 0.7%
Total extra area cost |  | 14.2%
Section | Power % of chip | Extra Cost
I/O | 26.0% | 0.0%
Memory leakage | 43.7% | 4.0%
Logic leakage | 7.3% | 2.5%
RAM active | 2.7% | 0.4%
TCAM active | 3.5% | 0.0%
Logic active | 16.8% | 5.5%
Total extra power cost |  | 12.4%
Area
Power
Notes: Give context on what metrics matter in hardware design.

## Slide 32: Questions: hardware design
The high-level idea is great, but the hardware details are confusing
RMT is presented as a theoretical model, no real-world demonstration.
What’s the performance compared to traditional switches?
How does a pipeline affect packet processing time?
I had not imagined table lookups to be this complicated.
Can we handle some of the most frequently used lookup rules quickly?

## Slide 33: Programming the RMT/other programmable chips: P4
RMT provides flexibility, but programming it is akin to x86 assembly
Concurrently, other programmable chips being developed: Intel FlexPipe, Cavium Xpliant, CORSA, …
Portable language to program these chips
How do we retain control / data plane separation?

## Slide 34: P4 Scope
Control plane
Data plane
Control traffic
Packets
Table mgmt.
Traditional switch
Control plane
Data plane
P4 Program
P4-defined switch
P4 table mgmt.
Notes: This is the P4 API: a new API between the control-plane and the data plane.
The data plane performs mostly stateless high-speed processing.
The data plane is lean and fast; most of the complexity is still in the control plane. P4 does not address this aspect.

## Slide 35: Q: Which data plane? A: Any data plane!
Control plane
Data plane
Programmable switches
FPGA switches
Programmable NICs
Software switches
Notes: P4 should be portable across a large spectrum of switch implementations.

## Slide 36: Data plane programmability
P4
P4
P4
Programmable blocks
Fixed function
Notes: P4 expresses the behavior of significant data plane functions. It currently is not rich enough to describe the complete functionality of the data plane.

## Slide 37: How does it work?
Programmable
parser
Packet (byte[])
Headers
eth
vlan
ipv4
Programmable
match-action
units
Metadata
eth
mtag
ipv4
Programmable
reassembly
Packet
Payload
err
bcast
port
Queuing
eth
mtag
ipv4
Headers
Notes: How is packet processing performed in P4?
This is a high-level view.

## Slide 38: P4 language
Programmable
parser
Programmable
match-action
units
Programmable
reassembly
State-machine; bitfield extraction
Table lookup and update; bitfield manipulation; control flow
Bitfield assembly
No: memory (pointers), loops, recursion, floating point
Notes: The P4 language has elements corresponding to the previously-described function blocks: parsing, match/action, and reassembly.

## Slide 39: Parsing = State machines
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
0x8100 : parse_vlan;
0x800 : parse_ipv4;
0x86DD : parse_ipv6;
}
}
TCP
New
IPv4
IPv6
VLAN
Eth
Notes: The parser is essentially a state-machine driven by the packet header.
It extracts packet fields into general-purpose registers (“metadata”).

## Slide 40: Match
﻿
table ipv4_lpm
{
reads {
ipv4.dstAddr : lpm;
}
actions {
set_next_hop;
drop;
}
}
dstAddr | action
0.* | drop
10.0.0.* | set_next_hop
224.* | drop
192.168.* | drop
10.0.1.* | set_next_hop
Lookup key
Notes: The Match performs table lookups based on metadata.
The table contents is managed by the control plane.

## Slide 41: Actions
action set_nhop(nhop_ipv4_addr, port)
{
modify_field(metadata.nhop_ipv4_addr, nhop_ipv4_addr);
modify_field(standard_metadata.egress_port, port);
add_to_field(ipv4.ttl, -1);
}
nhop_ipv4_addr | port
10.0.0.10 | 1
10.0.1.10 | 2
dstAddr | action
0.* | drop
10.0.0.* | set_next_hop
224.* | drop
192.168.* | drop
10.0.1.* | set_next_hop
Notes: Actions are code fragments that manipulate metadata. They are driven by information obtained from table look-ups.

## Slide 42: Control-Flow
control ingress
{
apply(port);
if (valid(vlan_tag[0])) {
apply(port_vlan);
}
apply (bridge_domain);
if (valid(mpls_bos)) {
apply(mpls_label);
}
retrieve_tunnel_vni();
if (valid(vxlan) or valid(genv) or valid(nvgre)) {
apply(dest_vtep);
apply(src_vtep);
}
}
M/A
M/A
M/A
M/A
M/A
Notes: P4 supports conditional forward-only control-flow.

## Slide 43: Reassembly
Driven by header types
add_header(ipv6);
remove_header(vlan);
Notes: Lavanya’s work on compilers for P4, maybe add a few slides as well.

## Slide 44: Table contents management
Control plane
Data plane
Manage tables contents
(Tied to P4 program)
Notes: Table contents is uploaded into the data plane by the control plane.
P4 control plane is similar to OpenFlow.
War stories from P4 working groups and such.

## Slide 45: Questions: programming this chip
Are these languages primarily intended for Google, Microsoft etc?
It seems extremely possible to write code that just won’t compile.
How does reconfiguring the switch work?
Is it easy to reconfigure these switches?
It’s interesting that the authors present P4 as a “strawman proposal”, given the fact that P4 has received significant attention since then.
Virtual switch compared to a physical switch for running P4?

## Slide 46: What’s happened since?

## Slide 47: Momentum around p4.org in industry
P4 reference software switch
P4 compiler
Workshops
Industry adoption (Netronome, Xilinx, Barefoot, CISCO, VMWare, …)
Culture shift: move towards open source
Notes: Too early to say if this will be widely adopted or not.
Staid companies such as AT&T and CISCO showing up at the working group meetings.

## Slide 48: Growing research interest in academia
P4 compilers (Jose et al.)
Stateful algorithms (Sivaraman et al., Packet Transactions)
Higher-level languages (Arashloo et al., SNAP)
Programmable scheduling (Sivaraman et al., PIFO; Mittal et al., UPS)
Protocol-independent software switches (Shahbaz et al., PISCES)
Programmable NICs (Kaufman et al., FlexNIC)
Network measurement (Li et al., FlowRadar)
Notes: Flesh this out a little more.

## Slide 49: Conclusion
How do we design a flexible chip?
  The RMT switch model
  Bring processing close to the memories:
    pipeline of many stages
  Bring the processing to the wires:
    224 action CPUs per stage
How much does it cost?
  15%
Notes: Mention 28 nm CMOS earlier.
Look at Nick’s slides on PISA.
Figure out what points to emphasize: Logic doesn’t cost all that much relative to wires and memory isn’t too much. Add Nick’s slides on die area contributions of logic and memory.

## Slide 50: P4 Summary
Simple language
  Parsing, bit-field manipulation, table lookup, control flow, packet reassembly
Efficient execution (high speed switching)
Simple cost model
Abstract resources
Portable
Expressive:
  New protocols, forwarding policies, monitoring and instrumentation
Notes: We will release the first version of the language soon.
We are actively working on an improved version which fixed some shortcomings – which we plan to release as well.

## Slide 51: What does SDN want?
Multiple stages of match-action
  Flexible allocation
Flexible actions
Flexible header fields
No coincidence OpenFlow built this way…

## Slide 52: What’s Hard about a Flexible Switch Chip?
Big chip
High frequency (1 GHz)
Wiring intensive
Many crossbars
Lots of TCAM
Interaction between physical design and architecture
Good news? No need to read 7000 IETF RFC’s!

## Slide 53: Early attempts
Active networks: Capsules + Java interpreters
NPUs: Intel IXPs
CPUs: Click, DPDK
FPGAs: NetFPGA, Arista 7124 FX
Programmability => Loss in performance