## Slide 1: Hardware and software for fast and programmable network monitoring
Srinivas Narayana, Anirudh Sivaraman, Vikram Nathan, Prateesh Goyal, Venkat Arun, Mohammad Alizadeh, Vimal Jeyakumar, and Changhoon Kim
Slides courtesy Srinivas Narayana

## Slide 2: Example: Who caused a microburst?
Queue build-up deep in the network
Per-pkt info: challenging in software
6.4Tbit/s switch: Need 100M recs/s
COTS: 100K-1M recs/s/core
End-to-end probes
Sampling
Counters & Sketches
Mirror packets

## Slide 3
Switches should be first-class citizens in performance monitoring.

## Slide 4: Why monitor from switches?
Already see the queues & concurrent connections
Infeasible to stream all the data out for external processing
Can we filter and aggregate performance on switches directly?

## Slide 5
We want to build “future-proof” hardware:
Language-directed hardware design

## Slide 6
Expressive query language
Line-rate switch hardware primitives
Performance monitoring use cases

## Slide 7: Contributions
Marple, a performance query language
Line-rate switch hardware design
  Aggregation: Programmable key-value store
Query compiler

## Slide 8
Queries
Query Compiler
Programmable switches
with the key-value store
Marple programs
Switch programs
To collection servers
Results

## Slide 9
Marple: Performance query language

## Slide 10: Marple: Performance query language
Stream: For each packet at each queue,
  S:= (switch, qid, hdrs, uid, tin, tout, qsize)
Location
Packet identification
Queue entry and exit timestamps
Queue depth seen by packet

## Slide 11: Marple: Performance query language
Stream: For each packet at each queue,
  S:= (switch, qid, hdrs, uid, tin, tout, qsize)
Familiar functional operators
filter
map
zip
groupby

## Slide 12: Example: High queue latency packets
R1 = filter(S, tout – tin > 1 ms)

## Slide 13: Example: Per-flow average latency
  R1 = filter(S, proto == TCP)
  R2 = groupby(R1, 5tuple, ewma)
  def ewma([avg],[tin, tout]):
  avg = (1-⍺)*avg + ⍺*(tout-tin)
Fold function

## Slide 14: Example: Microburst diagnosis
def bursty([last_time, nbursts], [tin]):
if tin - last_time > 800 ms:
nbursts = nbursts + 1
last_time = tin
result = groupby(S, 5tuple, bursty)

## Slide 15: Many performance queries (see paper)
Transport protocol diagnoses
  Fan-in problems (incast and outcast)
  Incidents of reordering and retransmissions
  Interference from bursty traffic
Flow-level metrics
  Packet drop rates
  Queue latency EWMA per connection
  Incidence and lengths of flowlets
Network-wide questions
  Route flapping
  High end to end latencies
  Locations of persistently long queues
...

## Slide 16
Implementing Marple on switches

## Slide 17: Implementing Marple on switches
filter
map
zip
groupby
Stateless match-action rules
[RMT SIGCOMM’13]
  S:= (switch, hdrs, uid, qid, tin, tout, qsize)
Switch telemetry
[INT SOSR’15]

## Slide 18: Implementing Marple on switches
filter
map
zip
groupby
Stateless match-action rules
[RMT SIGCOMM’13]
  S:= (switch, hdrs, uid, qid, tin, tout, qsize)
Switch telemetry
[INT SOSR’15]

## Slide 19: Implementing aggregation
  ewma_query = groupby(S, 5tuple, ewma)
  def ewma([avg], [tin, tout]):
  avg = (1-⍺)*avg + ⍺*(tout-tin)
Compute & update values at switch line rate (1 pkt/ns)
Scale to millions of aggregation keys (e.g., 5-tuples)

## Slide 20
Challenge:
Neither SRAM nor DRAM is both fast and dense

## Slide 21
Caching:
the illusion of fast and large memory

## Slide 22: Caching
Key
Value
On-chip cache (SRAM)
Key
Value
Off-chip backing store (DRAM)
Notes: On-chip cache of the key-value store is in SRAM
Off-chip backing store is in DRAM
But: cache misses lead to router pipeline stalls and non-determinism

## Slide 23: Caching
Key
Value
Read value for 5-tuple key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Modify value using ewma
Write back updated value

## Slide 24: Caching
Key
Value
Read value for 5-tuple key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Req. key K
Resp. Vback
Vback
K

## Slide 25: Caching
Key
Value
Key
Value
On-chip cache (SRAM)
Req. key K
Resp. Vback
K
Vback
Read value for 5-tuple key K
Off-chip backing store (DRAM)
K
Vback

## Slide 26: Caching
Key
Value
Key
Value
On-chip cache (SRAM)
Request key K
Respond K, V’’
K
V’’
K
V’’
Read value for 5-tuple key K
Off-chip backing store (DRAM)
Modify and write must wait for DRAM.
Non-deterministic DRAM latencies stall packet pipeline.
Notes: Stress that DRAM is built for the average case.

## Slide 27
Instead, we treat cache misses as
packets from new flows.

## Slide 28: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
K
V0
Read value for key K
Off-chip backing store (DRAM)

## Slide 29: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K,Vcache
K
Vback
K
V0
Read value for key K
Off-chip backing store (DRAM)

## Slide 30: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K,Vcache
K
K
V0
Read value for key K
Off-chip backing store (DRAM)
Merge
Vback

## Slide 31: Cache misses as new keys
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K,Vcache
K
K
V0
Read value for key K
Off-chip backing store (DRAM)
Nothing to wait for.
Vback

## Slide 32: How about value accuracy after evictions?
How do we merge evicted statistics value with previous value accurately?
Let’s represent the statistics operation as a function g over a packet sequence p1, p2, …
g([pi])
Action of g over a packet sequence,
e.g, for a counter g([pi]) = p1.len + p2.len + …

## Slide 33: The Merge operation
merge(g([qj]), g([pi]))
= g([p1,…,pn,q1,…,qm])
Example: if g is a counter, merge is just addition.
Easy generalization to all associative statistics (min, max, product, set union, intersection, etc.)
Vcache
Vback
Statistics over the entire packet sequence

## Slide 34: Mergeability beyond associative statistics
Can merge any statistic g by storing entire pkt sequence in cache
  … but that’s a lot of extra state!
Can we merge with “small” extra state?
Small: extra state size ≈ size of the statistics value being tracked

## Slide 35: Linear-in-state: Merge w. small extra state
S = A * S + B
Examples: Packet and byte counters, EWMA, functions over a window of packets, …
State maintained by the statistic
Functions of a bounded number of packets in the past

## Slide 36: Intuition for linear-in-state
Let’s say we are tracking an EWMA :
If the EWMA starts at or and ends at or respectively
after packets, then:
So we can take a final value calculated from initial value and modify it for a new initial stateusing:
I1
I2
F1
F2

## Slide 37: Intuition for linear-in-state
In our problem:
Small extra state: only number of packets (N), instead of storing each packet
I1
I2
F1
F2
Notes: Say that the more formal result is in the paper.

## Slide 38: Microbursts: Linear-in-state!
def bursty([last_time, nbursts], [tin]):
if tin - last_time > 800 ms:
nbursts = nbursts + 1
last_time = tin
result = groupby(S, 5tuple, bursty)
nbursts: S = A * S + B, where
A = 1
  B = {1, if current pkt within time gap from last;
  0 otherwise}

## Slide 39: Several useful linear-in-state statistics
Counting successive TCP packets that are out of sequence
Histogram of flowlet sizes
Counting number of timeouts in a TCP connection
Micro-burst detection
EWMAs
The linear-in-state operation can also be cheaply implemented using a multiply-accumulate hardware instruction.

## Slide 40: Other linear-in-state queries
Counting successive TCP packets that are out of order
Histogram of flowlet sizes
Counting number of timeouts in a TCP connection
… 7/10 example queries in our paper

## Slide 41
Evaluation:
Is processing the evictions feasible?

## Slide 42: Eviction processing
Key
Value
Key
Value
On-chip cache (SRAM)
Evict K’,V’cache
K’
V’back
K
V0
Off-chip backing store (DRAM)

## Slide 43: Eviction processing at backing store
Trace-based evaluation:
  “Core14”, “Core16”: Core router traces from CAIDA (2014, 16)
  “DC”: University data center trace from [Benson et al. IMC ’10]
  Each has ~100M packets
Query aggregates by 5-tuple (key)
  Show results for key+value size of 256 bits
8-way set-associative LRU cache eviction policy
Eviction ratio: % of incoming pkts that result in a cache eviction

## Slide 44: Eviction ratio vs. Cache size

## Slide 45: Eviction ratio vs. Cache size
218 keys == 64 Mbits
4% pkt eviction ratio
25X reduction from processing each pkt

## Slide 46: Eviction ratio  Eviction rate
Consider 64-port X 100-Gbit/s switch
Memory: 256 Mbits
  7.5% area
Eviction rate: 8M records/s
  ~ 32 cores

## Slide 47: See more in the paper…
More performance query examples
Query compilation algorithms
Evaluating hardware resources for stateful computations
Implementation & end-to-end walkthroughs on mininet

## Slide 48: Summary
On-switch aggregation reduces software data processing
Linear in state: fully accurate per-flow aggregation at line rate
Paper and code available at http://web.mit.edu/marple