## Slide 1: Making the fastest routers programmable
Anirudh Sivaraman

## Slide 2: Traditional network architecture
Fixed-function routers and programmable end points

## Slide 3: But, today’s reality is very different
We are demanding more from routers: ACLs, tunnels, etc
Yet, routers are still fixed-function
Rate of innovation exceeds our ability to get things into routers
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters
Notes: Fixed-function routers are great because they let you evolve one part of the network alone
But, we seem to demand much more, and there’s no consensus as to what should be in a router
But, routers are fixed-function, so even though they support some of these demands, they can’t cater to everyone’s requirements.
Now bc there’s no consensue and routers are fixed function, rate of innovation is …

## Slide 4: But, today’s reality is very different
We are demanding more from routers: ACLs, tunnels, etc
Yet, routers are still fixed-function
Rate of innovation exceeds our ability to get things into routers
1980s
1990s
2000s
2010s
WFQ
VirtualClock
CSFQ
STFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
IntServ
DiffServ
ECN
Flowlets
PDQ
HPFQ
FCP
Heavy Hitters

## Slide 5: One approach: Use a software router
Chart: Aggregate Capacity
| 1969.0 | 1982.0 | 1983.0 | 1985.0 | 1999.0 | 2000.0 | 2002.0 | 2004.0 | 2007.0 | 2009.0 | 2010.0 | 2012.0 | 2014.0
Fastest router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 32 | 80 | 240 | 640 | 1280 | 3200
Software router | 0.00075 | 0.0005 | 0.0004 | 0.08 | 0.1 | 0.17 | 4 | 35 | 40 | 100
Software routers 10—100x worse than the fastest routers
Software routers suffer from non-deterministic performance

## Slide 6: My work: performance+programmability
Domino (SIGCOMM ‘16):
programming streaming
algorithms
PIFO (SIGCOMM ‘16):
programming scheduling
algorithms
Performance+programmability for important classes of router functions
Scheduler
Ingress pipeline
Egress pipeline
Notes:   I’ll discuss two pieces of work: Domino to run on the pipelines and PIFO to run on the scheduler.

## Slide 7: My work: performance+programmability
Scheduler
Ingress pipeline
Egress pipeline
Domino (SIGCOMM ‘16):
programming streaming
algorithms
PIFO (SIGCOMM ‘16):
programming scheduling
algorithms
Performance+programmability for important classes of router functions
Notes:   I’ll start with Domino. It has two main ideas: a set of hardware primitives and a compiler to compile to these primitives.

## Slide 8: A fixed-function router pipeline
Eth
IP
TCP
Input
Ports
Queues/
Scheduler
Parser
match/action
ACL
Egress pipeline
match/action
Multicast
Deterministic pipelines supporting 1 packet/cycle (1 GHz)
Only local memory
match/action
Tunnels
match/action
Forwarding
Ingress pipeline
Constrained action units
Eth
IP
TCP
match/action
Measurement
match/action
Eth
IP
TCP
Output
Ports
Header
Vector
Notes: TODO: Remember to talk about packets marching in lock step.
Other examples of egress functionality (outside all of our programmable examples)

## Slide 9: A programmable atom pipeline
Atom: local memory + action unit,
constrained to handle 1 packet/cycle
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Local
Memory
action unit
Packet
Choice of atoms dictates the algorithms a router supports
1 cycle
(1 ns)
latency
action unit
X
const
Add
Add
2-to-1 Mux
X
choice
pkt.f
Notes: Ok, so how do we decide what atoms to place in the router and whether an atom can support an algorithm. That’s where the Domino compiler comes in to bridge the gap between algorithms and atoms.
TODO: Maybe call it local state?

## Slide 10: The Domino compiler
Pipeline stages
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0
:(pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1
Input: Algorithms as
packet transactions
Code
pipelining
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Extracting
atoms
Output: Atoms
Checking
against
existing
atoms
Output: Pipeline
Configuration
Notes: TODO: crystallize description of packet transactions.
TODO: It’s important to mention NO LOOPS here!!!
Describe the sampling algorithm.
Maybe describe how the pipeline stages correspond to the logic in the sampling algorithm.
TODO: At the end of this slide make the point that we reject algorithms that can’t run on atoms unlike a software router.

## Slide 11: Code pipelining for stateless algorithms
pkt.tmp =
pkt.f1 + pkt.f2
  Stateless algorithm: pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
pkt.f4 =
pkt.tmp - pkt.f3
Easy to pipeline stateless algorithms

## Slide 12: Code pipelining for stateful algorithms
  Stateful algorithm: x = g(x)
p.tmp = x
p.t1=
s1(p.tmp)
x = p.tn
X
Can’t pipeline: must do x = g(x) atomically in 1 stage
p.tn =
sn(p.t_{n-1})
1. Throughput is 1/N
2. X is shared
N stages

## Slide 13: Code pipelining: an example
Create one node for each instruction
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 14: Code pipelining: an example
Stateless
(intra-packet)
dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 15: Code pipelining: an example
Stateful
(inter-packet) dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 16: Code pipelining: an example
Strongly connected components (SCCs)
(Lam (1988):
Software pipelining)
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1)
count = pkt.new
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 17: Code pipelining: an example
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new
Contract SCCs to form DAG
pkt.sample = pkt.tmp ?
pkt.src : 0

## Slide 18: Code pipelining: an example
After Depth-First Search
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp ?
pkt.src : 0
Stage 2
Stage 1

## Slide 19: Extracting atoms
pkt.x = pkt.a + pkt.b
pkt.x = pkt.a - pkt.b
pkt.c = pkt.a (BINOP) pkt.b
x = x + 1
x = x + mux(C, pkt.a)
Accumulator
Stateless

## Slide 20: Does an algorithm map to a given atom?
X = X * p.b
X = X + 7
Checks if algorithm can run at 1 packet/cycle
action unit
X
const
Add
Add
2-to-1 Mux
X
choice
pkt.f
Formulate mapping problem as program synthesis
No mapping
Notes: TODO: Maybe call this accumulator?

## Slide 21: Results: A catalog of reusable atoms
Atoms | Description
Stateless | Binary operations on a pair of packet fields
Accumulator | Increment state by value (packet field or constant)
Read/Write | Read or write a state variable
Conditional Accumulator | Accumulate differently based on one predicate
Nested Conditional Accumulator | Accumulate differently based on two predicates
Pairs | Update a pair of mutually dependent state variables
Notes: Stress that this is *a* set of atoms, not *the* set.

## Slide 22: Results: A catalog of reusable atoms
Atoms | Description | Examples
Stateless | Binary operations on a pair of packet fields | TTL decrement, setting header fields, etc.
Accumulator | Increment state by value (packet field or constant) | Counters, sketches, heavy hitters
Read/Write | Read or write a state variable | Bloom filters, indicator variables
Conditional Accumulator | Accumulate differently based on one predicate | Rate Control Protocol, Flowlet switching, sampling
Nested Conditional Accumulator | Accumulate differently based on two predicates | HULL, AVQ
Pairs | Update a pair of mutually dependent state variables | CONGA

## Slide 23: Results: A catalog of reusable atoms
Atoms | Description | Examples | 32-nm atom area (mm2) @ 1 GHz | Additional area for 100 atoms
Stateless | Binary operations on a pair of packet fields | TTL decrement, setting header fields, etc. | 1384 | 0.07%
Accumulator | Increment state by value (packet field or constant) | Counters, sketches, heavy hitters | 431 | 0.022%
Read/Write | Read or write a state variable | Bloom filters, indicator variables | 250 | 0.0125%
Conditional Accumulator | Accumulate differently based on one predicate | Rate Control Protocol, Flowlet switching, sampling | 985 | 0.049%
Nested Conditional Accumulator | Accumulate differently based on two predicates | HULL, AVQ | 3597 | 0.18%
Pairs | Update a pair of mutually dependent state variables | CONGA | 5997 | 0.30%
<1 % additional chip area for 100 atom instances

## Slide 24: What algorithms do atoms enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
SRPT
WFQ
STFQ
IntServ
HPFQ

## Slide 25: What algorithms do atoms enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
WFQ
STFQ
IntServ
HPFQ

## Slide 26: My work: performance+programmability
Scheduler
Ingress pipeline
Egress pipeline
Domino (SIGCOMM ‘16):
programming streaming
algorithms
PIFO (SIGCOMM ‘16):
programming scheduling
algorithms
Notes:   I’ll start with Domino. It has two main ideas: a set of hardware primitives and a compiler to compile to these primitives.

## Slide 27: Why programmable scheduling?
Different performance objectives demand different schedulers
  Isolating different tenants in a datacenter: fair queueing
  Single tenant with many short flows: shortest remaining processing time
Status quo: Menu of schedulers baked into hardware
  Can configure coefficients, but not program a new algorithm

## Slide 28: Why is programmable scheduling hard?
Many algorithms, yet no consensus on primitives
Tight timing requirements: can’t simply use an FPGA/CPU
Need expressive primitive that can run at high speed

## Slide 29: What does the scheduler do?
It decides
In what order are packets sent
  e.g., first-in first-out, priorities, weighted fair queueing
At what time are packets sent
  e.g., rate limits

## Slide 30: Schedulers in routers today
Classification
Packets
Fixed schedulers
(priority,
round robin,
rate limits)

## Slide 31: A strawman programmable scheduler
Very tight time budget between consecutive dequeues (5 cycles @ 100G)
Can we refactor by precomputing programmable operations off the critical path?
Classification
Programmable dequeue()
function
Packets

## Slide 32: The Push-In First-Out Queue
Key observation
In many schedulers, relative order of buffered packets does not change with future packet arrivals
A packet’s place in the scheduling order is known at enqueue
The Push-In First-Out Queue (PIFO): Packets are pushed into an arbitrary location based on a rank, and dequeued from the head
2
5
9
7
9
10
13
8

## Slide 33: A programmable scheduler
To program the scheduler, program the rank computation
Rank Computation
(programmable)
(fixed logic)
2
9
8
5
PIFO Scheduler
f = flow(pkt)
…
...
p.rank= T[f] + p.len
Notes: Stress pre-computation here.

## Slide 34
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
A programmable scheduler
Rank Computation
…
…
…
…

## Slide 35
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Fair queuing
Rank Computation
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len
p.rank = p.start

## Slide 36
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Token bucket shaping
Rank Computation
tokens = min(
tokens + rate * (now – last), burst)
p.send = now +
max( (p.len – tokens) / rate, 0)
tokens = tokens - p.len
last = now
p.rank = p.send

## Slide 37: Beyond a single PIFO
Hierarchical scheduling algorithms need hierarchy of PIFOs
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
Notes: TODO: Maybe say hierarchical schedulers can use (instead of need) a hierarchy of PIFOs

## Slide 38: Tree of PIFOs
b1
b3
b2
a1
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
PIFO-Red
(WFQ on a & b)
PIFO-root
(WFQ on Red & Blue)
x1
x2
y1
y2
PIFO-Blue
(WFQ on x & y)
a1
a1
B
R
B
B
R
R
B
R

## Slide 39: PIFO in hardware
Performance targets for a shared-memory router
  1 GHz pipeline (64 ports * 10 Gbit/s)
  1K flows/physical queues
  60K packets (12 MB packet buffer, 200 byte cell)
  Scheduler is shared across ports
Naive solution: flat, sorted array of 60K elements is infeasible
Exploit observation that ranks increase within a flow: sort 1K head packets, one from each flow
7 mm2 area in a 16-nm library for a
5-level programmable scheduler (4% overhead)

## Slide 40: What algorithms do PIFOs enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
WFQ
STFQ
IntServ
HPFQ

## Slide 41: What algorithms do PIFOs enable?
1980s
1990s
2000s
2010s
VirtualClock
CSFQ
Bloom Filters
DRR
RED
AVQ
XCP
RCP
CoDel
DeTail
DCTCP
HULL
SRPT
PIE
DiffServ
ECN
Flowlets
PDQ
FCP
Heavy Hitters
WFQ
STFQ
IntServ
HPFQ

## Slide 42: Broader impact
Packet transactions now in P4
Industry interest in PIFOs, Domino’s compiler techniques

## Slide 43: Future Work
Primitives to program other network devices:
  Network Interface Cards
  Middleboxes (proxies, firewalls, WAN optimizers, etc.)
Hardware and software for specialized distributed systems
  The end of Moore’s law => hardware specialization
  We’ll soon have specialized clusters of accelerators and cores
  Requires straddling disciplines: hardware, systems, and compilers
Notes:   TODO: Rehearse second future work point.
  Why networking and architecture are linked?
  As an architect, you can’t think of your network as a low-latency pipe anymore---not if every memory access touches the network.
  As a networking researcher, you can’t think of architecture as a blackbox and use an Ethernet link anymore: too high latency.
  Memory disaggregation is causing networking and architecture concerns to be intertwined.

## Slide 44: Backup slides
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0
: (pkt.old + 1);
count = pkt.new;
pkt.old = count;
count = pkt.old + 1;
state = mux(state RELOP C, true) ?
mux(state + p.a, 0)
: mux(state + p.c, 0)

## Slide 45: Programming streaming algorithms
E.g., packet sampler:
Many clock cycles (ns) to process each packet
But, routers handle 1 packet/cycle (1 GHz)
Pipelining bridges this gap
  Atoms: primitives to atomically modify headers, state
  A compiler to
    Extract atoms from a corpus of algorithms
    Check if an atom pipeline can support a new algorithm
if (count == 9):
pkt.sample = pkt.src
count = 0
else:
pkt.sample = 0
count++
Notes: IMPORTANT: There’s one big difference between this machine and a processor pipeline. A processor can run any algorithm, but throughput inversely correlates with complexity. On a programmable router only algorithms that sustain one packet per clock cycle can run; all others are rejected. While this seems harsh, this obviates any need for performance profiling and is the model of routers that operators are used to.
I’ll give a one-slide overview of the work before I dive into its specific technical contributions.
First, let’s consider an example of a streaming algorithm, which I’ll call the packet sampler. Say you want to sample the source IP address of every 10th packet going through a router. Here’s what the code looks like: I have highlighted router state in red. you count from 0 – 9 and then sample every 10th packet, resetting the count to 0.
First, we note that the packet sampler spends more than 1 clock cycle per packet, where each clock cycle is a ns. Let’s say each LOC was one instruction and took one cycle, that’s at least three cycles per packet regardless of which branch the code takes.
We want this algorithm to run at high speeds. What is this speed? A high-end router handles 1 packet every clock cycle regardless of what features you enable. We would like the same guarantee regardless of what algorithm you program into the router.
Now, when each packet takes multiple clock cycles, but we need to process a new packet every clock cycle, the standard technique is to use a pipeline. Fixed-function routers use a pipeline where each pipeline stage carries out a fixed function like tunneling, forwarding, etc. In the context of this pipeline, we introduce two new ideas.
First is the concept of an atom, which are high-speed hardware primitives that we can embed into the router pipeline’s stages in place of fixed functionality. Atoms modify headers and/or state, and execute atomically: any state updated by an atom is visible to the next packet arriving at that stage a clock cycle. All atoms in a router support 1 packet per cycle, unlike say x86 instructions that have variable throughput depending on instruction.
Second, we built a compiler to go from high-level descriptions of algorithms to atoms. This compiler serves two purposes. In the design phase, we use this compiler to extract atoms from algorithms in a way that the atoms allow not just those, but hopefully other algorithms to be programmed. Once the router has been designed, we use the compiler to check if a given atom pipeline can support a new algorithm.
There’s one big difference between this machine and a processor pipeline. A processor can run any algorithm, but throughput inversely correlates with complexity. On a programmable router only algorithms that sustain one packet per clock cycle can run; all others are rejected. While this seems harsh, this obviates any need for performance profiling and is the model of routers that operators are used to.

## Slide 46: One approach: Use end points
Give up on changing routers, use end points instead
But, end point approaches are inaccurate or inefficient
  Estimating a router’s loss rates from end point measurements is inaccurate
  Congestion control from end points is inefficient
Notes: As a network operator who wants to add functionality to their network, what can you do if a router doesn’t have the features you want? The first approach is to give up on changing routers and do everything from the end points. Many network operators have done this for a variety of different networking tasks. But this is a rather roundabout way of doing things. As an example, let’s say you want to measure if a router deep inside the network is losing packets. One approach is to collect enough measurement date from endpoints scattered throughout the network and then analyze it to indirectly infer if there’s loss on a particular router. Not only is this indirect, it’s also necessarily inaccurate relative to just measuring things on that router.
As another example, the problem of congestion control deals with managing the transmission of packets from end points into the network so that the network’s resources (links, buffers, etc.) are not overloaded. Most solutions to this problem rely entirely on the end points to do congestion control without any router support. At the same time, it is well-known that there are much more efficient ways of doing congestion control if we could add just a little bit of intelligence to the routers.

## Slide 47: Packet Transactions: High-Level Programming for Line-Rate Switches (SIGCOMM 2016)
Anirudh Sivaraman, Alvin Cheung, Mihai Budiu,
Changhoon Kim, Mohammad Alizadeh, Hari Balakrishnan,
George Varghese, Nick McKeown, Steve Licking
Joint work with collaborators at MIT, University of Washington,
Barefoot Networks, Microsoft Research, and Stanford University
Notes: I’ll talk about Domino first. This is based on a paper that appeared at SIGCOMM last year, and is joint work with collaborators at MIT, UW, Barefoot, MSR, and Stanford. The goal of this work was to able to program streaming algorithms on high-speed routers. These are router algorithms that process the incoming packet stream in one pass. The router does a bounded amount of work per packet and maintains a bounded amount of router state to carry out its work. They include algorithms for managing a router’s resources, such as its link capacity and buffers.

## Slide 48: Programmable Packet Scheduling at Line Rate (SIGCOMM 2016)
Anirudh Sivaraman, Suvinay Subramanian, Mohammad Alizadeh,
Sharad Chole, Shang-Tse Chuang, Anurag Agrawal, Hari Balakrishnan,
Tom Edsall, Sachin Katti, Nick McKeown
Joint work with collaborators at MIT, Cisco Systems,
Stanford University, and Barefoot Networks
Notes: I’ll start with the PIFO work. This project was joint work with a number of collaborators from MIT, Cisco Systems, Stanford, and Barefoot Networks.

## Slide 49: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Ingress pipeline
Egress pipeline
Queues/
Scheduler
PIFO Scheduler
Notes: Ok, so we have looked at two algorithms where the rank computation runs on the switch. The rank computation can, in fact, run anywhere in the network. For instance, let’s compress this pipeline down to a switch. Let’s also introduce an end host.

## Slide 50: Shortest remaining flow size
2
9
8
5
PIFO Scheduler
Rank Computation
f = flow(p)
p.rank = f.rem_size
Notes: We can use this end host to compute the ranks for the shortest remaining flow size scheduler. Here, the end host has an RPC-like workload, where each RPC is a flow, and sets the remaining flow size to the remaining number of bytes in the current RPC.

## Slide 51: Beyond a single PIFO
x
1
y
1
x
2
b1
b2
b3
y
2
a1
Hierarchical scheduling algorithms need hierarchy of PIFOs
Red (0.5)
Blue (0.5)
a
(0.99)
b
(0.01)
x
(0.5)
y
(0.5)
root
Hierarchical
Packet Fair Queuing (HPFQ)
Notes: Ok, so we have seen examples of what a single PIFO can do. Common to these examples is the property that the relative order of buffered packets doesn’t change with future arrivals.
There are algorithms that violate this property, such as hierarchical schedulers. I’ll illustrate this through hierarchical packet-fair queueing. Here, the idea is to divide capacity between two classes, Left and Right, in some ratio. Then, we recursively divide capacity between flows within each class, such as a, b and c, d.
So, let’s see why HPFQ cannot be served by a single PIFO. Let’s say this is the current state of the system, with packets departing from the head. Now, when the first packet from flow a arrives, we need to satisfy two constraints simultaneously. One, classes red and blue must alternate because they share capacity equally. Two, within class red, a must be ahead of b, because it has a much higher weight.
To do this, we need to move the packets from b to new locations so that red and blue alternate. Then, we need to move a1 ahead of all packets of b because a has a much higher weight. This combination of moves from a and b is beyond a single PIFO that cannot change the relative order of packets that are already buffered.
But, it turns out we can do this with a hierarchy of PIFOs.

## Slide 52: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
Notes: If you need to cut something: slide 25 and 26.
Happy to talk about the impl. Details offline.
Try and fix orientation of the scheduler.
Feedback: If the point is to just quickly show that you have a hardware implementation and it’s feasible, just use the detailed hardware diagram from the CSAIL talk.
TODO: Give a very brief description + hardware diagram from the CSAIL talk.
Our design has two parts.
A flow scheduler schedules across the head packets of all flows, while a rank store stores packets ranks in a first-in first-out queue for each flow.
The flow scheduler is really a PIFO over the head packets alone.
When an element (say) C6, from flow C with rank 6, is enq, it’s just appended to the back of the rank store. When D4 shows up, it bypasses the rank store and directly goes to the flow scheduler. When we deq, we just pop the head of the flow scheduler array to get A0, then reach into the rank store, pull out A2 and insert it into the flow scheduler array.
If you notice, the flow scheduler has to insert an element like A2 into a sorted array, which we do by comparing it in parallel to all elements in the array. Except now, we can actually do this because the sorted array has only 1K head packets, not all 60K packets.
This block supports up to 1 enq + 1 deq every clock cycle, which is a ns in a typical scheduler. It can also be sliced up across many logical PIFOs, which are PIFOs that are independent of each other, but share the same underlying hardware impl. An example is PIFOs for different output ports, whose schedulers run independently.

## Slide 53: A single PIFO block
2
Rank Store
(SRAM)
Flow Scheduler
(flip-flops)
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
7 mm2 area in a 16-nm library for a
5-level programmable scheduler (4% overhead)
Notes: Our design has two parts.
A flow scheduler schedules across the head packets of all flows, while a rank store stores packets ranks in a first-in first-out queue for each flow.
The flow scheduler is really a PIFO over the head packets alone.
When an element (say) C6, from flow C with rank 6, is enq, it’s just appended to the back of the rank store. When D4 shows up, it bypasses the rank store and directly goes to the flow scheduler. When we deq, we just pop the head of the flow scheduler array to get A0, then reach into the rank store, pull out A2 and insert it into the flow scheduler array.
If you notice, the flow scheduler has to insert an element like A2 into a sorted array, which we do by comparing it in parallel to all elements in the array. Except now, we can actually do this because the sorted array has only 1K head packets, not all 60K packets.
This block supports up to 1 enq + 1 deq every clock cycle, which is a ns in a typical scheduler. It can also be sliced up across many logical PIFOs, which are PIFOs that are independent of each other, but share the same underlying hardware impl. An example is PIFOs for different output ports, whose schedulers run independently.

## Slide 54: Acknowledgements
MIT: Suvinay Subramanian, Hari Balakrishnan, Mohammad Alizadeh
Barefoot Networks: Changhoon Kim, Anurag Agrawal, Steve Licking, Mihai Budiu
Cisco Systems: Shang-Tse Chuang, Sharad Chole, Tom Edsall
Microsoft Research: George Varghese
Stanford University: Sachin Katti, Nick McKeown
University of Washington: Alvin Cheung
Notes: I would like to thank an outstanding set of collaborators from
MIT, Barefoot Networks, Cisco Systems, Microsoft Research, Stanford, and University of Washington.

## Slide 55: Recent activity in the area
2008--2013: OpenFlow: Specify router-to-router connectivity
2013--now: Programmable router chips (Barefoot’s Tofino, Intel’s FlexPipe, Cavium’s Xpliant), programming languages (P4)
Router chip programmability is still nascent
  Goal: feature parity with legacy routers without baking in features
  Basic header manipulation; recognize new protocol formats

## Slide 56: Code pipelining in one slide
Goal: if each stage runs atomically, transaction must run atomically
Easy without state: only intra-packet dependencies
  Perform depth-first search on DAG of intra-packet dependencies
  All nodes at the same depth belong to the same pipeline stage
State causes inter-packet dependencies
  Cycles in dep. graph: state read must follow write from previous packet.
  Find strongly connected components; contract SCCs to single nodes
  Depth-first search on resulting DAG

## Slide 57: Future work: An era of specialized systems
With Moore’s law ending, hardware specialization is a necessity
  Video encoding, graphics, machine learning, bitcoin mining, …
Recurring tension between programmability and specialization
  Simple question: How do we design a cluster of processors and accelerators for (machine learning / video encoding / …)?
  Requires synthesizing ideas from languages, compilers, hardware, and networking
Notes: TODO: Check if this is necessary.
If we were completely untethered.
    What’s in the accelerators?
    What’s the storage medium?
    What’s the right programming model?
    What’s the right congestion-control protocol?

## Slide 58: Early routers
Early routers were eminently programmable minicomputers
  IMPs (1969): Honeywell DDP-516 950 Kbit/s (The IMP paper)
  MIT C gateway (1980-1982): 500 Kbit/s on M68K (Lixia Zhang’s paper)
  Fuzzballs (1971-1991): Most known for use on the NSFNET Phase-1 Backbone Network (1986-88): DEC PDP-11/73: 400 Kbit/s (Mill’s paper from SIGCOMM 88)
  Stanford multiprotocol router (1981): DEC PDP 11 / Motorola 68000
  Proteon (1985): 80 Mbit/s (http://www.historyofcomputercommunications.info/Book/12/12.22_Proteon.html#_ftn3)

## Slide 59: Expressiveness of PIFOs
Fine-grained priorities: shortest-flow first, earliest deadline first, service-curve EDF
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow
Cannot express some scheduling algorithms, e.g., output shaping.
Notes: So it turns out that we can use a tree of PIFOs for many more algorithms. I am not discussing these here, but the paper has further details.
More importantly, we have algorithms that our abstraction doesn’t support. One important class is output shaping, where we rate limit dequeues from the scheduler. We can’t implement this because PIFOs provide prog. on the enq side, not on the deq side. Again, the paper discusses this in depth.

## Slide 60: FAQ
How is this different from P4?
  When we started this work a year ago, P4 was much closer to the hardware. Over time, it’s gotten more high-level, thanks in some part to this work (sequential semantics, ternary operators).
  We do have a P4 backend.
Why a pipeline?
  NPUs have a shared-memory architecture, but sharing memory is hard and slows down the switch.

## Slide 61: FAQ
What’s in the compiler?
  Strongly Connected Components to extract atomic portions.
  Code generation using program synthesis.
Do the atoms generalize in an ML sense?
  We don’t know for sure. We designed the atoms and were able to tweak them a little bit to serve more algorithms. But this is something we don’t yet have a handle on.

## Slide 62: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 63: Relationship to prior compiler techniques
Technique | Prior work | Differences
If Conversion | Kennedy et al. 1983 | No breaks, continue, gotos, loops
Static Single-Assignment | Ferrante et al. 1988 | No branches
Strongly Connected Components | Lam et al. 1989 (Software Pipelining) | Scheduling in space instead of time
Synthesis for instruction mapping | Technology mapping | Map to 1 hardware primitive, not multiple
 | Superoptimization | Counter-example-guided, not brute force

## Slide 64: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 65: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we convert to static single assignment form, which simplifies dependency analysis.
Static single assignment gets its name from the fact that all variables are assigned
Exactly once and no more.
It’s useful because it gets rid of write-after-read and write-after-write dependencies. In our case,
converting to SSA is trivial because we operate on straight-line code with no branches. Typical
SSA implementations are far more involved because they have to deal with branching.

## Slide 66: Expression Flattening
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
pkt.tmp = pkt.arrival - last_time[pkt.id];
pkt.tmp2 = pkt.tmp > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp2
? pkt . new_hop
: saved_hop [ pkt . id ];
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: The last step in canonicalization is to flatten arbitrarily complicated expressions
to bring them into a form closer to the underlying hardware.
(Quickly skim over this.)

## Slide 67: Instruction mapping: results
Generic method to handle fairly complex templates
Templates determine if a Domino program can run at line rate.
Example results:
  Flowlet switching needs conditional execution to save next hop information:
  saved_hop[pkt.id] = pkt.tmp2 ? pkt.new_hop : saved_hop[pkt.id]
  Simple increment suffices for heavy-hitter detection
  count_min_sketch[hash] = count_min_sketch[hash] + 1
Sequential to parallel code
Hardware constraints
Canonicalization

## Slide 68: Generating P4 code
Required changes to P4
  Sequential execution semantics (required for read from, modify, and write back to state)
  Expression support
  Both available in v1.1
Encapsulate every codelet in a table’s default action
Chain together tables as P4 control program
Notes: Say that this project led to sequential execution semantics.

## Slide 69: Branch Removal
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I ‘ll go through these steps quickly. The first step in canonicalization is to remove branching statements.
Branches complicate control flow and make it harder to infer dependencies.
We eliminate branches using a procedure called if conversion that transforms them into C’s conditional operator.
because the only kind of branch we have is an if statement, if conversion is very straightforward in our case, because
we don’t have any kind of unstructured control flow such as a goto, break, or continue, that significantly complicate
if conversion.
This makes the code flow straight from one statement to the next without exception and makes it very easy to infer
dependencies as well: everything on the right of a “equals” is read and the one statement on the left is written.

## Slide 70: Handling State Variables
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we identify state variables, because they complicate the pipelining procedure.
In the absence of state variables, once you have straight-line code, you only need to
consider how you would pipeline the code for a single packet’s processing and you are
done because all other packets follow the same pipeline and there is no interaction
between packets. With state variables, you need to consider interactions between packets.
To simplify our analysis of state variables and dependencies between packets, we explicitly
limit the ways in which state variables can be accessed. We allow only reads and writes to
state and all other arithmetic happens on packet variables. This also lets us reuse an old
value of a state variable down the pipeline if required.

## Slide 71: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 72: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.

## Slide 73: The Domino compiler
Branch Removal
Domino
Handle state variables
Code Pipelining
Instruction Mapping
Processing Pipeline
Canonicalization
(Sequential Code)
Sequential to
parallel code
Respecting hardware
constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 74: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Pair up read/write
flanks
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we pair up reads and writes to state variables to capture the notion
that state variables remain local to a specific stage in the pipeline. If not,
we would have to read from one stage and write from another requiring
us to route longer wires on the chip.

## Slide 75: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Condense strongly
connected components
into codelets
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we look for stongly connected components in this graph,
and condense them into what we call codelets. These capture the essence of
what operations need to be run atomically for the entire transaction to execute atomically.
Now that we have eliminated circles in the graph, we can schedule the resulting
acyclic graph. This is a straightforward process known as critical
path scheduling where we put each node in the earliest pipeline
stage following all its predecessors.

## Slide 76: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Add packet-field
dependencies
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we add read after write dependencies, where we draw an arrow from the
node that writes a value to the node which reads that value.
This is ALL we need to do to handle dependencies in our case because there are
no other waw or war dependencies after SSA.

## Slide 77: Programming with Packet Transactions
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
Pipeline
Domino
pkt.new_hop =
hash3(pkt.sport,
pkt.dport,
pkt.arrival)
%NUM_HOPS;
pkt.id =
hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: TODO: Per Ravi, Hongzi, consider switching to a simpler example like sampled netflow
To give you a flavor for programming using packet transactions, we look at programming
flowlet switching, a data-plane load-balancing algorithm.
To write imperative code for each packet transaction, we use a language
called Domino with a syntax resembling C. On the right, we contrast it against
writing code in P4.
So let me first describe flowlet switching. Its logic is shown here.
The idea in flowlet switching is to load balance groups of packets separated by
a long gap in time across different paths to carry out more fine-grained traffic
splitting relative to standard ECMP.
The logic in is straightforward. You start off by populating a new
hop variable in each packet using some dynamic quantity such as the packet’s arrival time.
Then, you check if the intepacket gap between this packet and its previous one is sufficiently
large and update a state variable called saved_hop if so.
Then, you simply update the last time and set the next hop to the saved hop (which is either
the new value or the old one).
Now, if you were to explain flowlet switching to someone else, like I just did, it’s natural to express its logic
as a block of imperative code and programming in packet transactions lets you do exactly that.
The logic itself becomes the body of a function. This function flowlet is a packet transaction, which conceptually
Executes atomically on each packet. The rest of the Domino program declares state variables as global
variables, packets as structures, and lets you use the rest of C including the macro preprocessor.
================================
So that’s how you express flowlet switching in Domino. When you compile this code it generates
a pipelined implementation in P4 as shown here. This is how you would program the switch today.
The rest of this talk will describe how its relatively straightforward to build a compiler that achieves
this transformation if you exploit characteristics of the underlying domain of line-rate switches.

## Slide 78: The quest for programmability
Switch | Year | Line-rate
Cisco Catalyst | 1999 | 32 Gbit/s
Broadcom 5670 | 2004 | 80 Gbit/s
Broadcom Scorpion | 2007 | 240 Gbit/s
Broadcom Trident | 2010 | 640 Gbit/s
Broadcom Tomahawk | 2014 | 3.2 Tbit/s
Programmability => 10--100x slower than line rate.
System | Year | Substrate | Performance
Click | 2000 | CPUs | 170 Mbit/s
Intel IXP 2400 | 2002 | NPUs | 4 Gbit/s
RouteBricks | 2009 | Multi-core | 35 Gbit/s
PacketShader | 2010 | GPUs | 40 Gbit/s
NetFPGA SUME | 2014 | FPGA | 100 Gbit/s
Notes: Cisco Catalyst: http://www.cisco.com/c/dam/en/us/products/collateral/switches/catalyst-6807-xl-switch/white_paper_c11-728264.doc/_jcr_content/renditions/white_paper_c11-728264_1.jpg
Intel IXP 2400: http://www.intel.com/design/network/papers/ixp2400.pdf: 4 Gbit/s (copyright 2002)
Broadcom 5670 (2004): 80 Gbit/s (8 ports of 10 G) (https://www.broadcom.com/collateral/pb/5670-PB05-R.pdf, 2004)
Broadcom Scorpion (2007) (24 * 10 G from DCTCP paper, and http://www.enterprisetech.com/2014/09/24/broadcom-fights-ethernet-rivals-tomahawk-chips/ suggests 2007)
Trident (2010): 64 * 10 G = 640 G
Trident II (2012): 100 * 10 G = 1 Tbit/s
BCM Tomahawk (2014): 3.2 Tbit/s
Trident and Tomhawk numbers taken from the pages below.
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
TODO: Turn this into a graph.

## Slide 79: The quest for programmability
Programmability => 10--100x slower than line rate.
Chart: Performance scaling of switches
| 2000.0 | 2002.0 | 2009.0 | 2010.0 | 2014.0
Software routers | 0.17 | 4 | 35 | 40 | 100
Line-rate routers | 32 | 80 | 240 | 640 | 3200
Notes: People have recognized this need at least since the late 90s and quite a few software switch platforms have been developed where you take an existing programming substrate and repurpose it for networking.
Now, here’s a line graph showing how the performance of these software switches has scaled with time, and we can see that it’s improved about 1000 fold since 2000, which is quite impressive.
But, at the same time, if you look at the highest end switches (or what I call line-rate switches, because they run at the highest speed that the cable or line can support), they have always been between 10 and 100 times faster than these software platforms. That’s because they have been specialized from the ground up to support just routing. As a result, these programmable platforms never really gained much adoption because they were always slower than the fastest switches.
So, the takeaway, historically is that programmability has cost us 10—100x in performance. And my research looks at designing programmable switch platforms without any performance penalty.

## Slide 80: Compiler targets: diagram
Operation:
+, -, >, <,
AND, OR
pkt.f1/
constant
pkt.f2/
constant
pkt.f3
pkt.f
constant
x
2-to-1
Mux
pkt.f
constant
x
2-to-1
Mux
x
0
2-to-1
Mux
Adder

## Slide 81: Why are switches pipelined?

## Slide 82: Performance requirements at line rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
10 operations per packet: routing, access control (ACL), tunnels, …
Need to process 1 billion pkts/s, 10 ops per packet
Notes: Important segue way here: Let’s talk about why a pipeline is the right hardware architecture for a switch by arguing for it from first principles.

## Slide 83: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
10 GHz processor
Packets
match/action
Can’t build a 10 GHz processor!

## Slide 84: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action

## Slide 85: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
match/action
match/action
match/action
match/action
Memory replication increases die area

## Slide 86: Function-parallel or pipelined architecture
Route lookup table
1 GHz circuit
ACL lookup table
Tunnel lookup table
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
match/action
match/action
match/action
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 87: P4 comparison

## Slide 88: Programming with packet transactions
Algorithm | LOC | P4 LOC
Bloom filter | 29 | 104
Heavy hitter detection | 35 | 192
Rate-Control Protocol | 23 | 75
Flowlet switching | 37 | 107
Sampled NetFlow | 18 | 70
HULL | 26 | 95
Adaptive Virtual Queue | 36 | 147
CONGA | 32 | 89
CoDel | 57 | 271
Notes: Ok, so now that I have shown you how to design these atoms, let’s look at what you can do with them. For this, we need some algorithms, and we picked a set spanning congestion control, measurement, load balancing, and AQM, and wrote them in Domino.
Their lines of code are listed here and they aren’t very different from the number of LOC you would have to write when programming a software switch with these algorithms. So that’s some measure of the abstraction being easy to use.