## Slide 1: Programming Line-Rate Routers
Anirudh Sivaraman
Notes: Thanks for having me here. I am Anirudh and I am a graduate student at MIT. I am going to be talking about work
I have been doing over the past year on abstractions for programming network data-planes that run at line rate.

## Slide 2: Joint work with
MIT: Suvinay Subramanian, Hari Balakrishnan, Mohammad Alizadeh
Barefoot Networks: Changhoon Kim, Mihai Budiu, Anurag Agrawal, Steve Licking
Cisco Systems: Shang-Tse Chuang, Sharad Chole, Tom Edsall
Microsoft Research: George Varghese
Stanford University: Sachin Katti, Nick McKeown
University of Washington: Alvin Cheung
Notes: Before I start, I should mention that this is joint work with an outstanding set of collaborators from
MIT, Barefoot Networks, Cisco Systems, Microsoft Research, Stanford, and University of Washington.
Also, I encourage you to interrupt me and ask questions as we go along.

## Slide 3: Traditional networking
Fixed (simple) routers and programmable (smart) end points
Notes: Go through this really quickly.

## Slide 4: Why is the traditional view insufficient?
Router features tied to ASIC design cycles (2-3 years)
  Long lag time for new protocol formats (IPv6, VXLAN)
Operators (especially in datacenters) need greater control
  Access control, load balancing, bandwidth sharing, measurement
Many proposals never make it to production
Ideally, we would have a programmable router

## Slide 5: The quest for programmable routers
Early routers (late 60s to mid 90s) built out of commodity CPUs
  IMPs (1969): Honeywell DDP-516
  Fuzzball (1971): DEC LSI-11
  Stanford multiprotocol router (1981): DEC PDP 11
  Proteon / MIT C gateway (1980s): DEC MicroVAX II
Notes: CPUs sufficient to maintain forwarding performance (50 Kbit/s to 1 Mbit/s)
CPUs represent the peak of programmability

## Slide 6: The quest for programmable routers
Chart: Performance scaling
| 1999 | 2000 | 2002 | 2004 | 2007 | 2009 | 2010 | 2014
Software router | 0.1 | 0.17 | 4 | 35 | 40 | 100
Line-Rate router | 32 | 80 | 240 | 640 | 3200
10—100 x loss in performance relative to line-rate, fixed-function routers
Unpredictable performance (e.g., cache contention)
Notes: Mention that it is on log scale
Define line rate
Unpredictable performance examples: hardware config (number of cores, RAM size, etc.)

## Slide 7: The vision: programmability at line-rate
Performance and predictability of hardware, line-rate routers
More programmable than fixed-function routers
  …, but less than software routers
Emerging chipsets around this paradigm: RMT, FlexPipe, Xpliant
  Moore’s law has reduced area overhead for programmability
Notes: Moore’s law has shrunk combinational logic for programmability.
It’s shrunk buffers as well, but usually that just means you increase buffers by a bit.
TCAM, SRAM, and IO remain the biggest sources of area on a chip.

## Slide 8: My work
  The machine model: Formalizing the computational capabilities of line-rate routers
  Packet transactions: High-level programming for the router pipeline
  Push-In First-Out Queues: Programming the scheduler
Parser
Ingress Pipeline
Stage 1
Match
Scheduler
Deparser
Egress Pipeline
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Stage 1
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Eth
IP
TCP
Notes: Say that we are going to look at the router architecture to see how my work fits into the router architecture.

## Slide 9: Performance requirements at line-rate
Aggregate capacity ~ 1 Tbit/s
Packet size ~ 1000 bits
~10 operations per packet (e.g., routing, ACL, tunnels)
Need to process 1 billion packets per second, 10 ops per packet

## Slide 10: Single processor architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
Packets
Only sustains 100 M packets per second

## Slide 11: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets

## Slide 12: Packet-parallel architecture
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
Lookup table
Match
Action
Match
Action
Match
Action
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
1: route lookup
2: ACL lookup
3: tunnel lookup
.
.
.
10: …
1 GHz processor
Packets
Memory replication increases die area
Lookup table
Match
Action
Match
Action
Match
Action
Lookup table
Match
Action
Match
Action
Match
Action
Lookup table
Match
Action
Match
Action
Match
Action

## Slide 13: Function-parallel or pipelined architecture
Route lookup table
Match
Action
1 GHz circuit
ACL lookup table
Match
Action
Tunnel lookup table
Match
Action
Packets
1 GHz circuit
1 GHz circuit
Route lookup
ACL lookup
Tunnel lookup
Factors out global state into per-stage local state
Replaces full-blown processor with a circuit
But, needs careful circuit design to run at 1 GHz
Notes: Net result is a reduction in die area.
TODO: Make sure to mention that these are very, very restricted units and not general purpose processors.
The game is designing these atoms or primitives
TODO: Rambling a bit too much here.

## Slide 14: A machine model for line-rate routers
Deterministic pipeline
Atoms: Smallest unit of atomic packet processing / state update
A router’s atoms constitute its instruction set
Notes: They must finish processing their inputs within the clock period, which at 1 GHz is 1 ns so that they are ready to process the next packet.
Say that it’s very deterministic, latency and throughput.
Make sure to mention that atoms are the smallest unit of atomic packet processing.
REQUIRES WORK, stress the definition of atom once.

## Slide 15: Stateless vs. stateful atoms
Stateless operations
  E.g., pkt.f4 = pkt.f1 + pkt.f2 – pkt.f3
  Can be easily pipelined into two stages
  Suffices to provide simple stateless atoms alone
Stateful operations
  E.g., x = x + 1
  Cannot be pipelined; needs an atomic read+modify+write instruction
  Explicitly design each stateful operation in hardware for atomicity
Notes: TODO: Add figure or make this description a little more precise, a little less rambling.
Stress that this is what complicates the problem.
Atom: smallest unit of atomic state update

## Slide 16: My work
  A machine model for programmable line-rate routers
  Packet transactions: An abstraction for programming the switch pipeline
  Push-In First-Out Queues: An abstraction for programming the scheduler
Parser
Ingress Pipeline
Stage 1
Match
Scheduler
Deparser
Egress Pipeline
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Stage 1
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Eth
IP
TCP

## Slide 17: Packet transactions
Packet transaction: Block of imperative code
Each transaction runs to completion, processes one packet at a time
if (count == 9):
pkt.sample = 1
count = 0
else :
pkt.sample = 0
count++
count
p1.sample = 0
p2.sample = 0
p1
p2
0
1
2
9
0
p10
p10.sample = 1
Notes:   TODO: Rambling a bit too much here.
  That leads us to the idea of packet transactions: a block of imperative code that is atomic and isolated from other such blocks.
  What do I mean by that? The idea here is that the programmer programs to the illusion that there is exactly one packet in the system at any time.
  When a packet comes in, a sequence of statements atomically updates fields in the packet and state on the switch. All field and state updates complete
  Before the next packet comes in. So the next packet doesn’t see any intermediate state.
  A compiler then translates this into a pipelined implementation suitable for a programmable switch.

## Slide 18: Programming with packet transactions
if (count == 9):
pkt.sample = 1
count = 0
else :
pkt.sample = 0
count++
Packet sampling pipeline
Packet sampling algorithm
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Reject code if it can’t be mapped
Notes: TODO: Should we introduce the term Domino here at all? Maybe remove it altogether.
Amy: What is the goal of the compiler?
The goal of the compiler is to isolate portions of the code that need to execute atomically and schedule them based on dependencies between them.
Mention the most important language restriction in the compiler: no loops.

## Slide 19: The Domino compiler
Domino
Preprocessing
Code Pipelining
Instruction Mapping
Processing Pipeline
Simplify sequential code
Sequential to parallel code
Respecting hardware constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 20: Code after preprocessing
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp;
count = pkt.new;
Sequential to parallel code
Hardware constraints
Preprocessing
if (count == 9):
pkt.sample = 1
count = 0
else :
pkt.sample = 0
count++
Notes: Two big takeaways from preprocessing:
Write out state modifications in an explicit read-modify-write form.
Remove branches and replace them with conditional operators.
Jonathan’s question:
========================
Why is predication not wasteful? It doesn’t waste time because the two halves are done in parallel in hardware.
It doesn’t waste area and power because it’s negligible anyway.

## Slide 21: Code Pipelining
Create one node for
each instruction.
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp
count = pkt.new
Sequential to parallel code
Hardware constraints
Preprocessing
Notes: Now that we have flattened the code, let’s look at how we generate a pipeline from it.
To start, we make a node corresponding to each statement in the program after flattening.

## Slide 22: Code Pipelining
Packet field dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp
count = pkt.new
Sequential to parallel code
Hardware constraints
Preprocessing

## Slide 23: Code Pipelining
State dependencies
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp
count = pkt.new
Sequential to parallel code
Hardware constraints
Preprocessing
Notes: Now that we have flattened the code, let’s look at how we generate a pipeline from it.
To start, we make a node corresponding to each statement in the program after flattening.
TODO: Rambling a bit too much here about bidirectional arrows.

## Slide 24: Code Pipelining
Strongly connected components
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp
count = pkt.new
Sequential to parallel code
Hardware constraints
Preprocessing
Notes: TODO: Rambling here. Explain the bidirectional red arrows a bit more crisply.
Spend some time explaining the intuition behind strongly connected components.
Give some intuition for how the algorithm works, instead of just saying that this is the algorithm.

## Slide 25: Code Pipelining
Condensed DAG
pkt.old = count
pkt.tmp = pkt.old == 9
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
pkt.sample = pkt.tmp
count = pkt.new
Sequential to parallel code
Hardware constraints
Preprocessing

## Slide 26: Code Pipelining
Sequential to parallel code
Hardware constraints
Canonicalization
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Code pipeline
Notes: At this point, we have a pipeline where each stage has some
sequential code that executes within it, while all pipeline stages
execute in parallel.
We have no idea whether those sequential code blocks can actually
be run at line rate or not. In other words, we haven’t quite figured out
if the sequential code block can or cannot be mapped to an instruction
provided by the switch.

## Slide 27: Instruction mapping
Sequential to parallel code
Hardware constraints
Canonicalization
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Notes: REQUIRES WORK here

## Slide 28: Instruction mapping: example
x = x * x doesn’t map
Add
(1)
x = x + 1 maps to this atom
Notes: REQUIRES WORK here.
Say that if the code is rejected here, we reject the code up top as well. This is important.

## Slide 29: Evaluation
Expressiveness: Can we program real algorithms using packet transactions?
Feasibility: Can we design compiler targets with small area overheads?
Compilation: Can the algorithms be compiled to the targets?
Notes:   Hari: Overall, elide details even more.

## Slide 30: Expressiveness of packet transactions
Feasibility
Compilation
Expressiveness
Algorithm | LOC
Bloom filter | 29
Heavy hitter detection | 35
Rate-Control Protocol | 23
Flowlet switching | 37
Sampled NetFlow | 18
HULL | 26
Adaptive Virtual Queue | 36
CONGA | 32
CoDel | 57
Notes: Takeaway: lines of code not much greater than the native form (simulation, software router)
Stress that none of these have been programmed at line rate before. They have either been burnt into hardware or programmed into software routers.
Say that the alternative today is to do it in P4, which is painful. Add P4 LOC as well to show how it can be automated??

## Slide 31: Expressiveness of packet transactions
Algorithm | LOC | Auto- generated P4 LOC
Bloom filter | 29 | 104
Heavy hitter detection | 35 | 192
Rate-Control Protocol | 23 | 75
Flowlet switching | 37 | 107
Sampled NetFlow | 18 | 70
HULL | 26 | 95
Adaptive Virtual Queue | 36 | 147
CONGA | 32 | 89
CoDel | 57 | 271
Feasibility
Compilation
Expressiveness
Notes: Takeaway: lines of code not much greater than the native form (simulation, software router)
Stress that none of these have been programmed at line rate before. They have either been burnt into hardware or programmed into software routers.

## Slide 32: Designing compiler targets
Design both stateless and stateful atoms
  Stateless: easy because stateless operations can be pipelined
  Stateful: determines which algorithms can run at line rate
1 GHz clock frequency
  300 each for stateful, stateless atoms (10 atoms per stage, 30 stages)
Synthesize atoms to 32-nm transistor library
  Estimate area overhead relative to 200 sq. mm chip.
Feasibility
Compilation
Expressiveness
Notes:   Need to say that there is 300 stateless + 300 of (one of the stateful) to form each target.
  REQUIRES WORK.

## Slide 33: Atoms used in targets
pkt.f3 =(pkt.f1 | constant)
OP
(pkt.f2 | constant);
where
OP = {+, -, AND, OR, > ,<, ...}
x = (pkt.f | constant);
x = (x | 0) + (pkt.f | constant);
if (predicate(x, pkt.f1, pkt.f2))
x = (x | 0) + (pkt.f1 | pkt.f2 | constant);
else:
x = x
Stateless
Read/Write (R/W)
ReadAddWrite (RAW)
Predicated ReadAddWrite (PRAW)
+
Stateful
Feasibility
Compilation
Expressiveness

## Slide 34: Atoms used in targets
pkt.f3 =(pkt.f1 | constant)
OP
(pkt.f2 | constant);
where
OP = {+, -, AND, OR, > ,<, ...}
Stateless
+
Atom | Description
R/W | Read or write state
RAW | Read, add, and write back
PRAW | Predicated version of RAW
IfElseRAW | 2 RAWs, one each when a predicate is true or false
Sub | IfElseRAW with a stateful subtraction capability
Nested | 4-way predication (nests 2 IfElseRAWs)
Pairs | Update a pair of state variables
Least
Expressive
Most
Expressive
Stateful
Feasibility
Compilation
Expressiveness
Notes: TODO: Requires work.

## Slide 35: Atoms used in targets
pkt.f3 =(pkt.f1 | constant)
OP
(pkt.f2 | constant);
where
OP = {+, -, AND, OR, > ,<, ...}
Stateless (0.22 %)
+
Atom | Description | Overhead
R/W | Read or write state | 0.04%
RAW | Read, add, and write back | 0.07%
PRAW | Predicated version of RAW | 0.13%
IfElseRAW | 2 RAWs, one each when a predicate is true or false | 0.16%
Sub | IfElseRAW with a stateful subtraction capability | 0.24%
Nested | 4-way predication (nests 2 IfElseRAWs) | 0.58%
Pairs | Update a pair of state variables | 0.96%
Stateful
Feasibility
Compilation
Expressiveness
Notes: Takeaway: total overhead of less than 2% for stateful and stateless atoms
Seem to be rambling a bit about PRAW and IfElseRAW (remove this?)
Or at least say what PRAW and IfElseRAW are.

## Slide 36: Compiling Domino algorithms
Algorithm | LOC | Stages (max 30) | Max. atoms/ stage (max 10) | Most expressive atom required
Bloom filter | 29 | 4 | 3 | R/W
Heavy hitter detection | 35 | 10 | 9 | RAW
Rate-Control Protocol | 23 | 6 | 2 | PRAW
Flowlet switching | 37 | 3 | 3 | PRAW
Sampled NetFlow | 18 | 4 | 2 | IfElseRAW
HULL | 26 | 7 | 1 | Sub
Adaptive Virtual Queue | 36 | 7 | 3 | Nested
CONGA | 32 | 4 | 2 | Pairs
CoDel | 57 | 15 | 3 | Doesn’t map
Feasibility
Compilation
Expressiveness
Notes: Takeaway: lines of code not much greater than the native form (simulation, software router)
Stress that none of these have been programmed at line rate before. They have either been burnt into hardware or programmed into software routers.

## Slide 37: My work
  A machine model for programmable line-rate routers
  Packet transactions: An abstraction for programming stateful data-plane algorithms
  Push-In First-Out Queues: An abstraction for programming the scheduler
Parser
Ingress Pipeline
Stage 1
Match
Scheduler
Deparser
Egress Pipeline
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Stage 1
Match
Action
Match
Action
Match
Action
Stage N
Match
Action
Match
Action
Match
Action
Eth
IP
TCP
Notes: Ok, so far, I have presented a higher-level abstraction for both the ingress and egress pipelines.
This is great, but an important class of data-plane algorithms are still left out.
And that’s scheduling. In the remaining half, I ‘ll present a design for a programmable scheduler.
Today’s packet schedulers allow you to pick from one of
a set of scheduling algorithms available on the switch. These include things like Deficit Round Robin, strict priority scheduling, and 2-level
Hierarchical scheduling. While a user can tune coefficients in these algorithms, she can’t change the core scheduling logic itself.

## Slide 38: Why is programmable scheduling hard?
Plenty of scheduling algorithms
Yet, no consensus on the right abstractions for scheduling
In contrast to
  Parse graphs for parsing
  Match-action tables for forwarding
On the surface, packet transactions are insufficient
Notes:   Amy: Emphasize that this is MYYYY abstraction.
  So, it should make you wonder. Why is programmable scheduling hard?
  After all, new scheduling algorithms spring up every year.
  The problem is that, despite many years of work on programmable scheduling and hundreds of algorithms, there is
  no consensus on an abstraction to use for ALL scheduling algorithms.
  This is in contrast to other aspects of the switch such as parsing, for which parse graphs are a good abstraction
  and forwarding, for which match-action tables are a good abstraction.
  Conclude here by saying, “packet transactions are insufficient” and we invent a primitive that allows us to keep using packet transactions for this as well.
  Because there is no abstraction, one approach is to throw up your hand and build an FPGA or CPU on the critical path.
  But this also isn’t feasible for line rate switches because you need to make decisions within a few clock cycles.
  So we are really looking for an abstraction that is simple enough that it can finish executing within a few clock cycles.
  Packet transactions are insufficient. On the surface of it, scheduling operates on groups of packets
  or queues. Packet transactions on the other hand, operate one packet at a time.

## Slide 39: The Push-In First-Out Queue
Relative scheduling order of enqueued packets doesn’t change with future arrivals
i.e., we can determine scheduling order at packet arrival
Examples:
  SJF: Order determined by flow size
  FCFS: Order determined by arrival time
Push-in first-out queues (PIFO): packets are pushed into an arbitrary location based on a priority, and dequeued from the head
First used as a proof construct by Chuang et. al
Notes:   That brings me to the primary contribution of our work, an abstraction for programmable packet scheduling.
  Central to our abstraction is the observation that many scheduling algorithms determine the relative order of packet transmissions when packets are enqueued. Put differently, the order of packets in the buffer will not change despite future packet arrivals.
  What do I mean by that? Here are a few examples of scheduling algorithms that all determine packet transmission order at packet arrival.
  The Shortest Job First scheduling discipline orders packets by their flow size, which is known when packets are enqueued.
  The Earliest Deadline First scheduling discipline orders packets by the time remaining until their deadline.
  And FCFS orders packets by packet arrival time.
  This naturally leads us to an abstraction for scheduling which is called a push-in first-out queue where packets are pushed into an arbitrary location based on a priority and dequeued from the head.
  This concept was first proposed as a proof construct in a paper from the late 90s.
  What we are showing is that this construct is practically usable as a construct for prog. Scheduling.
  The rest of this talk shows why PIFOs as an abstraction are expressive and why a PIFO is feasible at line rate.

## Slide 40: A programmable scheduler
Classification & Transmission Order Computation
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Classification & Transmission Order Computation
Key idea: separate priority computation from enforcement
Notes: REQUIRES WORK: Stress the key idea

## Slide 41: Shortest remaining processing time
Push-In-First-Out (PIFO) Queue
Scheduler
f = flow(p)
p.prio = f.rem_size
Notes: Our first example is pFabric, a recent datacenter scheduling algorithm that seeks to minimize flow completion time.
pFabric boils down to the shortest remaining processing time discipline. pFabric implements SRPT by
tracking the remaining flow size for each flow using TCP acknowledgements and inserting this as the packet’s priority in the flow’s packets.
Then, the scheduler itself simply schedules packets based on the remaining flow size. So this is an example where the end host determines
the packet’s priority and the switch respects it.

## Slide 42: Weighted Fair Queuing
f = flow(p)
p.start = max(T[f].finish, virtual_time)
T[f].finish = p.start + p.len / p.w
p.prio = p.start
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Notes: As our second example, let’s look at Weighted Fair Queueing, an algorithm that divides link capacity equitably
among flows. Most implementations of Weighted Fair Queueing use a virtual time calculation. Here, we look at the
Virtual Start-Time Fair Queueing implementation, which schedules packets based on their virtual start time. Computing
the virtual start-time requires the switch to track the virtual finish time of the last packet in each flow as shown in the simplified version of WFQ on the slides.
This algorithm can be implemented using PIFOs by maintaining this state on the ingress pipeline of a programmable switch
architecture such as the RMT architecture and updating the virtual finish time every time a packet is enqueued.

## Slide 43: Composing PIFOs
Hierarchical packet-fair
queueing (HPFQ)
A (0.3)
B (0.7)
1
(0.1)
2
(0.9)
3
(0.3)
4
(0.7)
PIFO-root
(WFQ on A and B)
PIFO-A
(WFQ on 1 and 2)
PIFO-B
(WFQ on 3 and 4)
1
3
2
4
2
A
B
A
B
A
Composing PIFOs
Notes: Hari: In truth, we need a hierarchy of PIFOs and quickly skip over.
The idea in Hierarchical Packet Fair Queueing (HPFQ) is to divide link capacity between classes
and then to recursively divide capacity between flows belonging to each class.
But, it turns out you can implement HPFQ using a tree of PIFOs that is isomorphic to the HPFQ tree.
PIFO-root has classes A and B for entries while PIFO-A and PIFO-B have packets from either flow A or B.
When a packet is enqueued, we enqueue the packet itself in either PIFO-A or PIFO-B and the packet’s class
In PIFO-root.
We use PIFO-root to divide capacity between two classes A and B using some implementation of WFQ.
Then, whenever PIFO-root is dequeued by the link’s transmitter, it returns a pointer to either PIFO-A or PIFO-B.
We then recursively dequeue packets from either PIFO-A or PIFO-B to transmit a packet.
Maybe add a slide after this to talk about the PIFO abstraction in totality.
TODO:
Mohammad: Composing PIFOs, give more than just one example. This is non-trivial about PIFOs: very different looking algorithms all boil down to a composition of a PIFO. This is the most surprising part of the PIFO. Take these very different looking algorithms can be mapped to composing PIFOs.
Mohammad: It’ll be good to have non-hierarchical scheduling algorithms using a combination of PIFOs. Try adding min. rate guarantees.

## Slide 44: Expressiveness of PIFOs
Fine-grained priorities: shortest-job first, earliest deadline first.
Hierarchical scheduling: HPFQ, Class-Based Queuing
Non-work-conserving algorithms: Token buckets, Stop-And-Go, Rate Controlled Service Disciplines
Least Slack Time First
Service Curve Earliest Deadline First
Minimum and maximum rate limits on a flow

## Slide 45: PIFO in hardware
Performance requirements:
  Comparable to single-chip shared-memory switches (e.g., Broadcom Trident)
  1 GHz pipeline
  ~ 1K flows/physical queues
  ~ 60K packets
Naive solution: flat, sorted array, doesn’t scale
Scalable solution: use the fact that priorities increase within a flow
Notes: Provide a little more intuition.

## Slide 46: A scalable PIFO block
2
Priority
Store
Flow Scheduler
A
B
Dequeue
Enqueue
A
0
B
1
C
3
C
2
4
3
4
5
C
6
D
4
A
2
D
Notes: Say that the numbers are the priorities of the packets.

## Slide 47: Hardware feasibility
Priority store is just a bank of FIFOs (stable hardware IP)
Flow scheduler for 60K packets, 1K flows meets timing at 1GHz on a 16-nm transistor library
E.g., 4% area overhead to program 5-level hierarchies
Notes: What determines clock rate and area overhead?
Maybe one or two slides on what affects what?
Make the 4% area overhead an example as opposed to the only design.

## Slide 48: Looking forward
The end of Moore’s law => more specialized hardware
The solution: high-performance abstractions for programming specific router functionality
  Stateful algorithms: Packet transactions, atoms
  Scheduling: PIFOs
  Network diagnostics/measurement: ?
Preprints:
  http://arxiv.org/abs/1512.05023 (Packet transactions)
  http://arxiv.org/abs/1602.06045 (PIFOs)
Notes: TODO: Rehearse this slide more and more.
REQUIRES WORK.
Increasingly affecting end-host networking (FPGA-based NICs)
Happening in other domains (graphics, video decoding, and so on).
Can’t do 100G and 400G on a software NIC easily.
Targeting abstractions give us programmability without a loss in performance.

## Slide 49: Backup slides

## Slide 50: The SKETCH algorithm
We have an automated search procedure that configures the atoms appropriately to match the specification, using a SAT solver to verify equivalence.
This procedure uses 2 SAT solvers:
Generate random input x.
Does there exist configuration such that spec and impl. agree on random input?
Can we use the same configuration for all x?
If not, add the x to set of counter examples and go back to step 1.

## Slide 51: Hardware feasibility of PIFOs
Number of flows handled by a PIFO affects timing.
Number of logical PIFOs within a PIFO, priority and metadata width, and number of PIFO blocks only increases area.

## Slide 52: Other future work
Instruction-set design for programmable routers
Approximate semantics for packet transactions
Sharing memory between pipeline stages
Programmable NICs

## Slide 53: Instruction mapping: bin packing
Sequential to parallel code
Hardware constraints
Canonicalization
pkt.old = count;
pkt.tmp = pkt.old == 9;
pkt.new = pkt.tmp ? 0 : (pkt.old + 1);
count = pkt.new;
pkt.sample = pkt.tmp;
Stage 2
Stage 1
Notes: Amy: Replace the atoms instead of sitting on top of them.

## Slide 54: Composing PIFOs: min. rate guarantees
Minimum rate guarantees:
Provide each flow a guaranteed
rate provided the sum of these
guarantees is below capacity.
PIFO-Root
Prioritize flows under
min. rate
PIFO-A
(FIFO for flow A)
PIFO-B
(FIFO for flow B)
1
3
2
4
2
A
B
A
B
A
Composing PIFOs
Notes: TODO: Flesh out this slide.
Stress that composed PIFOs can be used for more than just hierarchical scheduling.
Slightly better figure maybe?

## Slide 55: Traffic Shaping
1. update tokens
2. p.send = now +
(p.len - tokens) / rate;
3. p.prio =p.send
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Notes: A natural question is whether a PIFO can handle non-work-conserving algorithms?
So, our third example looks at Traffic Shaping, the most common of these non-work-conserving algorithms,
whose goal is to limit a flow to a fixed absolute throughput regardless of its offered load and the offered load of other flows.
We can implement Traffic Shaping using PIFOs by computing a packet’s priority in the PIFO based on the wall-clock
departure time of the packet when it is enqueued and dequeuing a packet whenever its wall-clock time arrives.
A PIFO allows you to express anything where you can determine the transmission order when packets are enqueued.
In other words, anything where the relative order doesn’t change in the future.
There are algorithms for which these are not true. In particular, hierarchical scheduling algorithms are a class of algorithms
for which this is not true. Let’s consider one in particular.

## Slide 56: LSTF
Add transmission delay to slack
Push-In-First-Out (PIFO) Queue
Scheduler
Ingress Pipeline
Decrement wait time in queue from slack
Initialize slack
values
Notes: Add transmission time at the switch
Too many examples.

## Slide 57: Packet transactions: conclusion
More familiar abstraction
Programming line-rate switches need not be hard
Simple user interface: code that compiles runs at line rate
Notes: Now, at this point, I have described the core techniques in domino.
Practical appeal:
---------------------
The compiler techniques are interesting intellectually, but I think the far greater practical appeal of packet transactions is there familiarity to programmers
As one glib quantitative comparison, flowlet switching is 37 LOC in domino and compiles to around 110 lines in P4. We had similar
results for other benchmarks such as conga, codel, and RCP and this should give you some indication that it’s a more familiar programming model.
Philosophical appeal:
---------------------------
The broader philosophical appeal is that programming line-rate switches need not be hard. You don’t need to err on either side
of the compiler-user tradeoff. If you understand your domain well enough, you can develop a suitably constrained language, for which
you can write a simple compiler. The compiler I wrote was about 3000 lines, which is pretty small in comparison to most compilers.
Usability appeal:
--------------------------
Finally, from a usability perspective, packet transactions dramatically simplify the interface between the user and the hardware.
Your code either compiles and runs at line rate or is rejected, which means you don’t actually have to profile your code anymore.
There is no question of performance profiling, cache hits, cache misses and predicting performance that have plagued software routers

## Slide 58: The PIFO abstraction in one slide
PIFO: A sorted array that let us insert an entry (packet or PIFO pointer) into a PIFO based on a programmable priority
Entries are always dequeued from the head
If an entry is a packet, dequeue and transmit it
If an entry is a PIFO, dequeue it, and continue recursively
Notes: To summarize, let’s look at what the PIFO abstraction entails.

## Slide 59: Motivating packet transactions
Example: count number of packets
On enqueue:
Calculate average queue size
if min < avg < max
calculate probability p
mark packet with probability p
else if avg > max:
mark packet
Runs to completion, process one packet at a time
Notes:   TODO: Use common example across figures 8, 9, and 10. Maybe sampled Netflow?? (Ask Mohammad if that’s an appropriate term)
  So, I ‘ll begin with packet transactions.
  A natural question here is why isn’t a language like P4, an emerging language for such programmable switches sufficient?
  To answer that, I ‘ll make the observation that for any domain-specific programming language there is typically
  constant tension between ease of use for the programmer and ease of development for the compiler writer.
  P4 errs considerably on the compiler writer’s side, by being too close to the underlying hardware.
  For instance, you need to express everything as a table, and spell out connections between the tables.
  Second, actions within a table are assumed to execute in parallel because that’s how data-parallel hardware executes.
  This is ideally suited to forwarding, but requires significant shoehorning for stateful algorithms such as active queue management
  and in-network congestion control. Why is this? Historically, these algorithms have been implemented on software platforms
  and in simulation and are typically expressed as snippets of imperative code, with no references to tables. This is
  the case for almost any software platform: Click, Intel’s earlier Network Processor, or the Linux kernel.

## Slide 60: Language constraints on Domino
No loops (for, while, do-while)
No unstructured control flow (break, continue, goto)
No pointers, heaps
Notes: The first thing we do to simplify the Domino compiler is to restrict the language.
First, there are no loops because a loop with an unbounded iteration count cannot be run at line rate.
This is because it isn’t clear how long it takes to process each packet and hence how long the packet
Processing pipeline will be.
Because we forbid all loops, we also forbid unstructured control flow such as break and continue that
let you break out of a loop.
We also forbid pointers and heaps because all memory on these chips is statically allocated.
Through this talk, I ‘ll show you how these constraints simplify the Domino compiler.

## Slide 61: Static Single-Assignment
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id];
...
pkt.last_time = pkt.arrival;
last_time[pkt.id] = pkt.last_time ;
pkt.id0 = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time0 = last_time[pkt.id0];
...
pkt.last_time1 = pkt.arrival;
…
last_time [pkt.id0] = pkt.last_time1 ;
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we convert to static single assignment form, which simplifies dependency analysis.
Static single assignment gets its name from the fact that all variables are assigned
Exactly once and no more.
It’s useful because it gets rid of write-after-read and write-after-write dependencies. In our case,
converting to SSA is trivial because we operate on straight-line code with no branches. Typical
SSA implementations are far more involved because they have to deal with branching.

## Slide 62: Expression Flattening
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
pkt.tmp = pkt.arrival - last_time[pkt.id];
pkt.tmp2 = pkt.tmp > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp2
? pkt . new_hop
: saved_hop [ pkt . id ];
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: The last step in canonicalization is to flatten arbitrarily complicated expressions
to bring them into a form closer to the underlying hardware.
(Quickly skim over this.)

## Slide 63: Instruction mapping: results
Generic method to handle fairly complex templates
Templates determine if a Domino program can run at line rate.
Example results:
  Flowlet switching needs conditional execution to save next hop information:
  saved_hop[pkt.id] = pkt.tmp2 ? pkt.new_hop : saved_hop[pkt.id]
  Simple increment suffices for heavy-hitter detection
  count_min_sketch[hash] = count_min_sketch[hash] + 1
Sequential to parallel code
Hardware constraints
Canonicalization

## Slide 64: Generating P4 code
Required changes to P4
  Sequential execution semantics (required for read from, modify, and write back to state)
  Expression support
  Both available in v1.1
Encapsulate every codelet in a table’s default action
Chain together tables as P4 control program
Notes: Say that this project led to sequential execution semantics.

## Slide 65: Relationship to prior compiler techniques
Technique | Prior work | Differences
If Conversion | Kennedy et al. 1983 | No breaks, continue, gotos, loops
Static Single-Assignment | Ferrante et al. 1988 | No branches
Strongly Connected Components | Lam et al. 1989 (Software Pipelining) | Scheduling in space instead of time
Synthesis for instruction mapping | Technology mapping | Map to 1 hardware primitive, not multiple
 | Superoptimization | Counter-example-guided, not brute force

## Slide 66: PIFO in hardware: HotNets version
Meets timing at 1 GHz on a 16 nm node
5 % area overhead for 3-level hierarchy
Challenges wisdom that sorting is hard
Min
Max
Range search CAM
MiniPIFO
Mini-PIFO bank
1
10
10
100
100
300
300
500
500
1000
1000
2000
1
10
10
100
100
300
300
500
1000
500
1000
2000
128 elements
1000 mini-PIFOs
Notes: As an example, let’s look at a PIFO that can hold up to 128 K entries. This is more than sufficient for the majority of switching chips today.
The naïve way to implement this is to build a single sorted array with up to 128 K entries, compare an incoming element’s priority to all
The elements in the sorted array in parallel and then drop the packet into the right position, by shifting the array appropriately.
Unfortunately, it’s impossible to build and operate on a single array of this size in hardware in parallel.
So we break up this array into several smaller arrays, each of which we can actually operate on in parallel. Each such miniPIFO has 128 elements
And is small enough that we can read, compare in parallel, and write back to the array at line rate.
How do we determine which of the mini PIFOs a packet should go into? We accomplish this with a range-search CAM that lets us index into the
mini-PIFO bank. To support a 128K entry data structure, we need a range-search CAM with 1024 entries.
The most challenging part of this process was the range-seach CAM with 1000 entries. It wasn’t obvious that we could do this in hardware, so
we synthesized it on a 16 nm technology node and were pleasantly surprised to find that it met timing at 1 Ghz, a typical processing rate for
a switch pipeline. This suggests that technology has scaled to a point where sorting ~1000 entries in hardware isn’t all that challenging.
Now, what’s the cost of this structure? We find that it incurs an additional 5% area overhead relative to a baseline switch chip such
as the Broadcom Trident. In return, it gives us a 3-level programmable hierarchy with essentially an unbounded number of queues.
The Trident, by contrast, supports a two-level of hierarchy across at most 8 queues.
Overall, our results are surprising because a long-line of work including DRR and SFQ start off on the premise that sorting is hard
at line rate. Our synthesis results suggest that it is worthwhile revisiting this assumption because transistors have scaled to a point
where this is no longer hard, at least for the buffer sizes required for most switching chips.

## Slide 67: Branch Removal
pkt.tmp = pkt.arrival - last_time[pkt.id] > THRESHOLD;
saved_hop [ pkt . id ] = pkt.tmp
? pkt . new_hop
: saved_hop [ pkt . id ];
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop [ pkt . id ] = pkt . new_hop ;
}
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I ‘ll go through these steps quickly. The first step in canonicalization is to remove branching statements.
Branches complicate control flow and make it harder to infer dependencies.
We eliminate branches using a procedure called if conversion that transforms them into C’s conditional operator.
because the only kind of branch we have is an if statement, if conversion is very straightforward in our case, because
we don’t have any kind of unstructured control flow such as a goto, break, or continue, that significantly complicate
if conversion.
This makes the code flow straight from one statement to the next without exception and makes it very easy to infer
dependencies as well: everything on the right of a “equals” is read and the one statement on the left is written.

## Slide 68: Handling State Variables
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
...
last_time[pkt.id] = pkt.arrival;
…
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
pkt.last_time = last_time[pkt.id]; // Read flank
...
pkt.last_time = pkt.arrival;
…
last_time[pkt.id] = pkt.last_time; // Write flank
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we identify state variables, because they complicate the pipelining procedure.
In the absence of state variables, once you have straight-line code, you only need to
consider how you would pipeline the code for a single packet’s processing and you are
done because all other packets follow the same pipeline and there is no interaction
between packets. With state variables, you need to consider interactions between packets.
To simplify our analysis of state variables and dependencies between packets, we explicitly
limit the ways in which state variables can be accessed. We allow only reads and writes to
state and all other arithmetic happens on packet variables. This also lets us reuse an old
value of a state variable down the pipeline if required.

## Slide 69: Instruction mapping: the SKETCH algorithm
Map each codelet to an atom template
Convert codelet and template both to functions of bit vectors
Q: Does there exist a template config s.t.
for all inputs,
codelet and template functions agree?
Quantified boolean satisfiability (QBF) problem
Use the SKETCH program synthesis tool to automate it
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Now, I am wary of writing SAT formulas and asserting logic conditions. It turns out there is a tool called SKETCH, which takes programs and turns them automatically into Boolean functions and a QBF formula to check equality between the functions. (basically automate the steps above).
SKETCH is a tool that does this automatically for us, where codelets are SKETCH specs and templates are partial programs.

## Slide 70: FAQ
Does predication require you to do twice the amount of work (for both the if and the else branch)?
  Yes, but it’s done in parallel, so it doesn’t affect timing.
  The additional area overhead is negligible.
What do you do when code doesn’t map?
  We reject it and the programmer retries
Why can’t you give better diagnostics?
  It’s hard to say why a SAT solver says unsatisfiable, which is at the heart of these issues.
Approximating square root.
  Approximation is a good next step, especially for algorithms that are ok with sampling.
How do you handle wrap arounds in the PIFO?
  We don’t right now.
Is the compiler optimal?
  No, it’s only correct.

## Slide 71: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Pair up read/write
flanks
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Next, we pair up reads and writes to state variables to capture the notion
that state variables remain local to a specific stage in the pipeline. If not,
we would have to read from one stage and write from another requiring
us to route longer wires on the chip.

## Slide 72: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Condense strongly
connected components
into codelets
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we look for stongly connected components in this graph,
and condense them into what we call codelets. These capture the essence of
what operations need to be run atomically for the entire transaction to execute atomically.
Now that we have eliminated circles in the graph, we can schedule the resulting
acyclic graph. This is a straightforward process known as critical
path scheduling where we put each node in the earliest pipeline
stage following all its predecessors.

## Slide 73: Code Pipelining
pkt.id = hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id]
pkt.tmp = pkt.arrival – pkt.last_time
last_time[pkt.id] = pkt.arrival
pkt.tmp2 = pkt.tmp > THRESHOLD
pkt.saved_hop = saved_hop[pkt.id]
pkt.next_hop = pkt.tmp2 ?pkt.new_hop : pkt.saved_hop
saved_hop[pkt.id] = pkt.tmp2 ?pkt.new_hop :pkt.saved_hop
pkt.next_hop = hash3(pkt.sport,
pkt.dport, pkt.arrival)
%NUM_HOPS
Add packet-field
dependencies
Sequential to parallel code
Hardware constraints
Canonicalization
Notes: Then, we add read after write dependencies, where we draw an arrow from the
node that writes a value to the node which reads that value.
This is ALL we need to do to handle dependencies in our case because there are
no other waw or war dependencies after SSA.

## Slide 74: Programming with Packet Transactions
#define NUM_FLOWLETS 8000
#define THRESHOLD 5
#define NUM_HOPS 10
struct Packet { int sport; int dport; …};
int last_time [NUM_FLOWLETS] = {0};
int saved_hop [NUM_FLOWLETS] = {0};
void flowlet(struct Packet pkt) {
pkt.new_hop = hash3(pkt.sport, pkt.dport, pkt.arrival)
% NUM_HOPS;
pkt.id = hash2(pkt.sport, pkt.dport) % NUM_FLOWLETS;
if (pkt.arrival - last_time[pkt.id] > THRESHOLD) {
saved_hop[pkt.id] = pkt.new_hop;
}
last_time[pkt.id] = pkt.arrival;
pkt.next_hop = saved_hop[pkt.id];
}
Pipeline
Domino
pkt.new_hop =
hash3(pkt.sport,
pkt.dport,
pkt.arrival)
%NUM_HOPS;
pkt.id =
hash2(pkt.sport,
pkt.dport)
% NUM_FLOWLETS
pkt.last_time = last_time[pkt.id];
last_time[pkt.id] = pkt.arrival;
pkt.tmp = pkt.arrival – pkt.last_time;
pkt.tmp2 = pkt.tmp > 5;
pkt.saved_hop = saved_hop[pkt.id];
saved_hop[pkt.id] = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop;
pkt.next_hop = pkt.tmp2 ?
  pkt.new_hop :
    pkt.saved_hop ;
Stage 1
Stage 2
Stage 3
Stage 4
Stage 6
Stage 5
Notes: TODO: Per Ravi, Hongzi, consider switching to a simpler example like sampled netflow
To give you a flavor for programming using packet transactions, we look at programming
flowlet switching, a data-plane load-balancing algorithm.
To write imperative code for each packet transaction, we use a language
called Domino with a syntax resembling C. On the right, we contrast it against
writing code in P4.
So let me first describe flowlet switching. Its logic is shown here.
The idea in flowlet switching is to load balance groups of packets separated by
a long gap in time across different paths to carry out more fine-grained traffic
splitting relative to standard ECMP.
The logic in is straightforward. You start off by populating a new
hop variable in each packet using some dynamic quantity such as the packet’s arrival time.
Then, you check if the intepacket gap between this packet and its previous one is sufficiently
large and update a state variable called saved_hop if so.
Then, you simply update the last time and set the next hop to the saved hop (which is either
the new value or the old one).
Now, if you were to explain flowlet switching to someone else, like I just did, it’s natural to express its logic
as a block of imperative code and programming in packet transactions lets you do exactly that.
The logic itself becomes the body of a function. This function flowlet is a packet transaction, which conceptually
Executes atomically on each packet. The rest of the Domino program declares state variables as global
variables, packets as structures, and lets you use the rest of C including the macro preprocessor.
================================
So that’s how you express flowlet switching in Domino. When you compile this code it generates
a pipelined implementation in P4 as shown here. This is how you would program the switch today.
The rest of this talk will describe how its relatively straightforward to build a compiler that achieves
this transformation if you exploit characteristics of the underlying domain of line-rate switches.

## Slide 75: The Domino compiler
Branch Removal
Domino
Handle state variables
Code Pipelining
Instruction Mapping
Processing Pipeline
Canonicalization
(Sequential Code)
Sequential to
parallel code
Respecting hardware
constraints
Notes: At a high level, the compiler has three parts that roughly correspond to the front, middle and back ends.
The frontend maintains the same sequential code illusion that is presented to the programmer and converts it into a progressively more canonical form.
The mid end carries out the important conceptual step of going from sequential to parallel code. It turns sequential code into a pipelined implementation while handling state.
The back end is where the rubber meets the road. Here, we check whether the pipelined implementation can actually be mapped to circuits provided by the hardware.

## Slide 76: Diagrams

## Slide 77
Add
Sub
constant
x
2-to-1 Mux
x
choice

## Slide 78: The quest for programmability
Switch | Year | Line-rate
Cisco Catalyst | 1999 | 32 Gbit/s
Broadcom 5670 | 2004 | 80 Gbit/s
Broadcom Scorpion | 2007 | 240 Gbit/s
Broadcom Trident | 2010 | 640 Gbit/s
Broadcom Tomahawk | 2014 | 3.2 Tbit/s
Programmability => 10--100x slower than line rate.
System | Year | Substrate | Performance
Click | 2000 | CPUs | 170 Mbit/s
Intel IXP 2400 | 2002 | NPUs | 4 Gbit/s
RouteBricks | 2009 | Multi-core | 35 Gbit/s
PacketShader | 2010 | GPUs | 40 Gbit/s
NetFPGA SUME | 2014 | FPGA | 100 Gbit/s
Notes: Cisco Catalyst: http://www.cisco.com/c/dam/en/us/products/collateral/switches/catalyst-6807-xl-switch/white_paper_c11-728264.doc/_jcr_content/renditions/white_paper_c11-728264_1.jpg
Intel IXP 2400: http://www.intel.com/design/network/papers/ixp2400.pdf: 4 Gbit/s (copyright 2002)
Broadcom 5670 (2004): 80 Gbit/s (8 ports of 10 G) (https://www.broadcom.com/collateral/pb/5670-PB05-R.pdf, 2004)
Broadcom Scorpion (2007) (24 * 10 G from DCTCP paper, and http://www.enterprisetech.com/2014/09/24/broadcom-fights-ethernet-rivals-tomahawk-chips/ suggests 2007)
Trident (2010): 64 * 10 G = 640 G
Trident II (2012): 100 * 10 G = 1 Tbit/s
BCM Tomahawk (2014): 3.2 Tbit/s
Trident and Tomhawk numbers taken from the pages below.
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
https://www.broadcom.com/products/Switching/Data-Center/BCM56860
TODO: Turn this into a graph.

## Slide 79: The quest for programmability
Programmability => 10--100x slower than line rate.
Chart: Performance scaling of routers
| 2000 | 2002 | 2009 | 2010 | 2014
Software routers | 0.17 | 4 | 35 | 40 | 100
Line-rate routers | 32 | 80 | 240 | 640 | 3200
Notes: People have recognized this need at least since the late 90s and quite a few software router platforms have been developed where you take an existing programming substrate and repurpose it for networking.
Now, here’s a line graph showing how the performance of these software routers has scaled with time, and we can see that it’s improved about 1000 fold since 2000, which is quite impressive.
But, at the same time, if you look at the highest end routers (or what I call line-rate routers, because they run at the highest speed that the cable or line can support), they have always been between 10 and 100 times faster than these software platforms. That’s because they have been specialized from the ground up to support just routing. As a result, these programmable platforms never really gained much adoption because they were always slower than the fastest routers.
So, the takeaway, historically is that programmability has cost us 10—100x in performance. And my research looks at designing programmable router platforms without any performance penalty.

## Slide 80: Compiler targets: diagram
Operation:
+, -, >, <,
AND, OR
pkt.f1/
constant
pkt.f2/
constant
pkt.f3
pkt.f
constant
x
2-to-1
Mux
pkt.f
constant
x
2-to-1
Mux
x
0
2-to-1
Mux
Adder